## Slide 1
Product presentation
SRU-plus
Universal swivel unit

## Slide 2
Universal swivel unit
The rotary actuator with the largest, most comprehensive range on the market
Universal unit for pneumatic swivel and turning movements.

## Slide 3
Principle of function
Housing
3
Pinion
2
Drive
1
Sleeve technology
4
Damping
5
Functional description
When subjected to pressure, the two pneumatic pistons move their end faces in a straight line in their respective bores thus turning the pinion by means of the serrations on their sides.

## Slide 4
Advantages – Your benefits
Finely graded series with a steady increase in torque for multiple cases of application, the correct size as a standard product is available
Swivel angle can be selected as either 90° or 180° complete flexibility in selecting the angle of rotation, application-specific angles possible on request
End position adjustability +3°/-3° (small) or +3°/-90° (large) can be selected
Middle position can be selected as pneumatic or locked The locked middle position can be unlocked when loaded. The two types of middle positions always allow further rotation in either direction.
Fluid feed-through can be used for gases, fluids, and vacuum therefore no interfering hoses
Electrical rotary feed-through for long-lasting, reliable feed-through of sensor, actuator or optionally bus signals
Choice of electronic magnetic sensors or inductive proximity sensors for absolute variability of position monitoring
Exchangeable screw-in guide sleeves (bushing) allow for easy maintenance and rapid exchange t after several million cycles.
Series extends downwards with the SRU-mini series, for a wide range of applications

## Slide 5
Technical data overview |  |  |  |  | 
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 20-W-90-3 | Spring-elastomer | 90 | 3.4 | 1.2 | 0.05
SRU-plus 20-W-90-3-EX | Spring-elastomer | 90 | 3.4 | 1.2 | 0.05
SRU-plus 20-S-90-3 | Damper-elastomer | 90 | 3.4 | 1.2 | 0.05
SRU-plus 20-W-180-3 | Spring-elastomer | 180 | 3.4 | 1.2 | 0.05
SRU-plus 20-W-180-3-EX | Spring-elastomer | 180 | 3.4 | 1.2 | 0.05
SRU-plus 20-S-180-3 | Damper-elastomer | 180 | 3.4 | 1.2 | 0.05
SRU-plus 20-W-180-90 | Spring-elastomer | 180 | 3.4 | 1.24 | 0.05
SRU-plus 20-W-180-90-EX | Spring-elastomer | 180 | 3.4 | 1.24 | 0.05
SRU-plus 20-S-180-90 | Damper-elastomer | 180 | 3.4 | 1.24 | 0.05
SRU-plus 20-S-180-3-M | Damper-elastomer | 180 | 3.4 | 1.55 | 0.05
SRU-plus 20-S-180-3-VM | Damper-elastomer | 180 | 3.4 | 1.76 | 0.05
Technical data

## Slide 6
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 20-S-180-90-M | Damper-elastomer | 180 | 3.4 | 1.6 | 0.05
SRU-plus 20-W-180-3-4 | Spring-elastomer | 180 | 3 | 1.4 | 0.05
SRU-plus 20-W-180-3-4-EX | Spring-elastomer | 180 | 3 | 1.4 | 0.05
SRU-plus 20-S-180-3-4 | Damper-elastomer | 180 | 3 | 1.4 | 0.05
SRU-plus 20-W-180-3-4-M8 | Spring-elastomer | 180 | 3 | 2.05 | 0.05
SRU-plus 20-W-180-3-4-M8-AS | Spring-elastomer | 180 | 3 | 2.05 | 0.05
SRU-plus 20-S-180-3-4-M8 | Damper-elastomer | 180 | 3 | 2.05 | 0.05
SRU-plus 20-S-180-3-4-M8-AS | Damper-elastomer | 180 | 3 | 2.05 | 0.05
SRU-plus 20-W-90-3-4 | Spring-elastomer | 90 | 3 | 1.4 | 0.05
SRU-plus 20-W-90-3-4-EX | Spring-elastomer | 90 | 3 | 1.4 | 0.05
SRU-plus 20-S-90-3-4 | Damper-elastomer | 90 | 3 | 1.4 | 0.05
SRU-plus 20-W-90-3-4-M8 | Spring-elastomer | 90 | 3 | 2.05 | 0.05
Technical data

## Slide 7
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 20-W-90-3-4-M8-AS | Spring-elastomer | 90 | 3 | 2.05 | 0.05
SRU-plus 20-S-90-3-4-M8 | Damper-elastomer | 90 | 3 | 2.05 | 0.05
SRU-plus 20-S-90-3-4-M8-AS | Damper-elastomer | 90 | 3 | 2.05 | 0.05
SRU-plus 20-W-180-90-4 | Spring-elastomer | 180 | 3 | 1.44 | 0.05
SRU-plus 20-W-180-90-4-EX | Spring-elastomer | 180 | 3 | 1.44 | 0.05
SRU-plus 20-S-180-90-4 | Damper-elastomer | 180 | 3 | 1.44 | 0.05
SRU-plus 20-W-180-90-4-M8 | Spring-elastomer | 180 | 3 | 2.09 | 0.05
SRU-plus 20-W-180-90-4-M8-AS | Spring-elastomer | 180 | 3 | 2.09 | 0.05
SRU-plus 20-S-180-90-4-M8 | Damper-elastomer | 180 | 3 | 2.09 | 0.05
SRU-plus 20-S-180-90-4-M8-AS | Damper-elastomer | 180 | 3 | 2.09 | 0.05
SRU-plus 20-S-180-3-M-4 | Damper-elastomer | 180 | 3 | 1.75 | 0.05
SRU-plus 20-S-180-3-M-4-M8 | Damper-elastomer | 180 | 3 | 2.4 | 0.05
Technical data

## Slide 8
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 20-S-180-3-M-4-M8-AS | Damper-elastomer | 180 | 3 | 2.4 | 0.05
SRU-plus 20-S-180-3-VM-4 | Damper-elastomer | 180 | 3 | 1.96 | 0.05
SRU-plus 20-S-180-3-VM-4-M8 | Damper-elastomer | 180 | 3 | 2.61 | 0.05
SRU-plus 20-S-180-3-VM-4-M8-AS | Damper-elastomer | 180 | 3 | 2.61 | 0.05
SRU-plus 20-S-180-90-M-4 | Damper-elastomer | 180 | 3 | 1.8 | 0.05
SRU-plus 20-S-180-90-M-4-M8 | Damper-elastomer | 180 | 3 | 2.45 | 0.05
SRU-plus 20-S-180-90-M-4-M8-AS | Damper-elastomer | 180 | 3 | 2.45 | 0.05
SRU-plus 25-W-90-3 | Hydr. damper | 90 | 5 | 1.6 | 0.05
Technical data

## Slide 9
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 25-W-90-3-EX | Hydr. damper | 90 | 5 | 1.6 | 0.05
SRU-plus 25-H-90-3 | Hydr. damper | 90 | 5 | 1.6 | 0.05
SRU-plus 25-H-90-3-EX | Hydr. damper | 90 | 5 | 1.6 | 0.05
SRU-plus 25-W-180-3 | Hydr. damper | 180 | 5 | 1.6 | 0.05
SRU-plus 25-W-180-3-EX | Hydr. damper | 180 | 5 | 1.6 | 0.05
SRU-plus 25-H-180-3 | Hydr. damper | 180 | 5 | 1.6 | 0.05
SRU-plus 25-H-180-3-EX | Hydr. damper | 180 | 5 | 1.6 | 0.05
SRU-plus 25-W-180-90 | Hydr. damper | 180 | 5 | 1.65 | 0.05
SRU-plus 25-W-180-90-EX | Hydr. damper | 180 | 5 | 1.65 | 0.05
SRU-plus 25-H-180-90 | Hydr. damper | 180 | 5 | 1.65 | 0.05
SRU-plus 25-H-180-90-EX | Hydr. damper | 180 | 5 | 1.65 | 0.05
Technical data

## Slide 10
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 25-W-180-3-M | Hydr. damper | 180 | 5 | 2.2 | 0.05
SRU-plus 25-W-180-3-VM | Hydr. damper | 180 | 5 | 2.6 | 0.05
SRU-plus 25-W-180-90-M | Hydr. damper | 180 | 5 | 2.25 | 0.05
SRU-plus 25-W-180-3-4 | Hydr. damper | 180 | 4.6 | 1.8 | 0.05
SRU-plus 25-W-180-3-4-EX | Hydr. damper | 180 | 4.6 | 1.8 | 0.05
SRU-plus 25-H-180-3-4 | Hydr. damper | 180 | 4.6 | 1.8 | 0.05
SRU-plus 25-H-180-3-4-EX | Hydr. damper | 180 | 4.6 | 1.8 | 0.05
SRU-plus 25-W-180-3-4-M8 | Hydr. damper | 180 | 4.6 | 2.45 | 0.05
SRU-plus 25-W-180-3-4-M8-AS | Hydr. damper | 180 | 4.6 | 2.45 | 0.05
SRU-plus 25-H-180-3-4-M8 | Hydr. damper | 180 | 4.6 | 2.45 | 0.05
SRU-plus 25-H-180-3-4-M8-AS | Hydr. damper | 180 | 4.6 | 2.45 | 0.05
Technical data

## Slide 11
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 25-W-90-3-4 | Hydr. damper | 90 | 4.6 | 1.8 | 0.05
SRU-plus 25-W-90-3-4-EX | Hydr. damper | 90 | 4.6 | 1.8 | 0.05
SRU-plus 25-H-90-3-4 | Hydr. damper | 90 | 4.6 | 1.8 | 0.05
SRU-plus 25-H-90-3-4-EX | Hydr. damper | 90 | 4.6 | 1.8 | 0.05
SRU-plus 25-W-90-3-4-M8 | Hydr. damper | 90 | 4.6 | 2.45 | 0.05
SRU-plus 25-W-90-3-4-M8-AS | Hydr. damper | 90 | 4.6 | 2.45 | 0.05
SRU-plus 25-H-90-3-4-M8 | Hydr. damper | 90 | 4.6 | 2.45 | 0.05
SRU-plus 25-H-90-3-4-M8-AS | Hydr. damper | 90 | 4.6 | 2.45 | 0.05
SRU-plus 25-W-180-90-4 | Hydr. damper | 180 | 4.6 | 1.85 | 0.05
SRU-plus 25-W-180-90-4-EX | Hydr. damper | 180 | 4.6 | 1.85 | 0.05
SRU-plus 25-H-180-90-4 | Hydr. damper | 180 | 4.6 | 1.85 | 0.05
Technical data

## Slide 12
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 25-H-180-90-4-EX | Hydr. damper | 180 | 4.6 | 1.85 | 0.05
SRU-plus 25-W-180-90-4-M8 | Hydr. damper | 180 | 4.6 | 2.5 | 0.05
SRU-plus 25-W-180-90-4-M8-AS | Hydr. damper | 180 | 4.6 | 2.5 | 0.05
SRU-plus 25-H-180-90-4-M8 | Hydr. damper | 180 | 4.6 | 2.5 | 0.05
SRU-plus 25-H-180-90-4-M8-AS | Hydr. damper | 180 | 4.6 | 2.5 | 0.05
SRU-plus 25-W-180-3-M-4 | Hydr. damper | 180 | 4.6 | 2.4 | 0.05
SRU-plus 25-W-180-3-M-4-M8 | Hydr. damper | 180 | 4.6 | 3.05 | 0.05
SRU-plus 25-W-180-3-M-4-M8-AS | Hydr. damper | 180 | 4.6 | 3.05 | 0.05
SRU-plus 25-W-180-90-M-4 | Hydr. damper | 180 | 4.6 | 2.45 | 0.05
SRU-plus 25-W-180-90-M-4-M8 | Hydr. damper | 180 | 4.6 | 3.1 | 0.05
SRU-plus 25-W-180-90-M-4-M8-AS | Hydr. damper | 180 | 4.6 | 3.1 | 0.05
Technical data

## Slide 13
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 25-W-180-3-VM-4 | Hydr. damper | 180 | 4.6 | 2.8 | 0.05
SRU-plus 25-W-180-3-VM-4-M8 | Hydr. damper | 180 | 4.6 | 3.45 | 0.05
SRU-plus 25-W-180-3-VM-4-M8-AS | Hydr. damper | 180 | 4.6 | 3.45 | 0.05
SRU-plus 30-W-90-3 | Hydr. damper | 90 | 9.5 | 2.4 | 0.05
SRU-plus 30-W-90-3-EX | Hydr. damper | 90 | 9.5 | 2.4 | 0.05
SRU-plus 30-H-90-3 | Hydr. damper | 90 | 9.5 | 2.4 | 0.05
SRU-plus 30-H-90-3-EX | Hydr. damper | 90 | 9.5 | 2.4 | 0.05
SRU-plus 30-W-180-3 | Hydr. damper | 180 | 9.5 | 2.4 | 0.05
SRU-plus 30-W-180-3-EX | Hydr. damper | 180 | 9.5 | 2.4 | 0.05
SRU-plus 30-H-180-3 | Hydr. damper | 180 | 9.5 | 2.4 | 0.05
Technical data

## Slide 14
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 30-W-180-90 | Hydr. damper | 180 | 9.5 | 2.4 | 0.05
SRU-plus 30-W-180-90-EX | Hydr. damper | 180 | 9.5 | 2.4 | 0.05
SRU-plus 30-H-180-90 | Hydr. damper | 180 | 9.5 | 2.4 | 0.05
SRU-plus 30-H-180-90-EX | Hydr. damper | 180 | 9.5 | 2.4 | 0.05
SRU-plus 30-W-180-3-M | Hydr. damper | 180 | 9.5 | 3.2 | 0.05
SRU-plus 30-W-180-3-VM | Hydr. damper | 180 | 9.5 | 3.4 | 0.05
SRU-plus 30-W-180-90-M | Hydr. damper | 180 | 9.5 | 3.3 | 0.05
SRU-plus 30-W-180-3-4 | Hydr. damper | 180 | 9 | 2.7 | 0.05
SRU-plus 30-W-180-3-4-EX | Hydr. damper | 180 | 9 | 2.7 | 0.05
SRU-plus 30-H-180-3-4 | Hydr. damper | 180 | 9 | 2.7 | 0.05
SRU-plus 30-H-180-3-4-EX | Hydr. damper | 180 | 9 | 2.7 | 0.05
Technical data

## Slide 15
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 30-W-180-3-4-M8 | Hydr. damper | 180 | 9 | 3.4 | 0.05
SRU-plus 30-W-180-3-4-M8-AS | Hydr. damper | 180 | 9 | 3.4 | 0.05
SRU-plus 30-H-180-3-4-M8 | Hydr. damper | 180 | 9 | 3.4 | 0.05
SRU-plus 30-H-180-3-4-M8-AS | Hydr. damper | 180 | 9 | 3.4 | 0.05
SRU-plus 30-W-90-3-4 | Hydr. damper | 90 | 9 | 2.7 | 0.05
SRU-plus 30-W-90-3-4-EX | Hydr. damper | 90 | 9 | 2.7 | 0.05
SRU-plus 30-H-90-3-4 | Hydr. damper | 90 | 9 | 2.7 | 0.05
SRU-plus 30-H-90-3-4-EX | Hydr. damper | 90 | 9 | 2.7 | 0.05
SRU-plus 30-W-90-3-4-M8 | Hydr. damper | 90 | 9 | 3.4 | 0.05
SRU-plus 30-W-90-3-4-M8-AS | Hydr. damper | 90 | 9 | 3.4 | 0.05
Technical data

## Slide 16
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 30-H-90-3-4-M8 | Hydr. damper | 90 | 9 | 3.4 | 0.05
SRU-plus 30-H-90-3-4-M8-AS | Hydr. damper | 90 | 9 | 3.4 | 0.05
SRU-plus 30-W-180-90-4 | Hydr. damper | 180 | 9 | 2.7 | 0.05
SRU-plus 30-W-180-90-4-EX | Hydr. damper | 180 | 9 | 2.7 | 0.05
SRU-plus 30-H-180-90-4 | Hydr. damper | 180 | 9 | 2.7 | 0.05
SRU-plus 30-H-180-90-4-EX | Hydr. damper | 180 | 9 | 2.7 | 0.05
SRU-plus 30-W-180-90-4-M8 | Hydr. damper | 180 | 9 | 3.4 | 0.05
SRU-plus 30-W-180-90-4-M8-AS | Hydr. damper | 180 | 9 | 3.4 | 0.05
SRU-plus 30-H-180-90-4-M8 | Hydr. damper | 180 | 9 | 3.4 | 0.05
SRU-plus 30-H-180-90-4-M8-AS | Hydr. damper | 180 | 9 | 3.4 | 0.05
SRU-plus 30-W-180-3-M-4 | Hydr. damper | 180 | 9 | 3.5 | 0.05
SRU-plus 30-W-180-3-M-4-M8 | Hydr. damper | 180 | 9 | 4.2 | 0.05
Technical data

## Slide 17
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 30-W-180-3-M-4-M8-AS | Hydr. damper | 180 | 9 | 4.2 | 0.05
SRU-plus 30-W-180-90-M-4 | Hydr. damper | 180 | 9 | 3.6 | 0.05
SRU-plus 30-W-180-90-M-4-M8 | Hydr. damper | 180 | 9 | 4.3 | 0.05
SRU-plus 30-W-180-90-M-4-M8-AS | Hydr. damper | 180 | 9 | 4.3 | 0.05
SRU-plus 30-W-180-3-VM-4 | Hydr. damper | 180 | 9 | 3.7 | 0.05
SRU-plus 30-W-180-3-VM-4-M8 | Hydr. damper | 180 | 9 | 4.4 | 0.05
SRU-plus 30-W-180-3-VM-4-M8-AS | Hydr. damper | 180 | 9 | 4.4 | 0.05
SRU-plus 35-W-90-3 | Hydr. damper | 90 | 14 | 2.65 | 0.05
SRU-plus 35-W-90-3-EX | Hydr. damper | 90 | 14 | 2.65 | 0.05
SRU-plus 35-W-180-3 | Hydr. damper | 180 | 14 | 2.65 | 0.05
SRU-plus 35-W-180-3-EX | Hydr. damper | 180 | 14 | 2.65 | 0.05
Technical data

## Slide 18
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 35-W-180-90 | Hydr. damper | 180 | 14 | 2.75 | 0.05
SRU-plus 35-W-180-90-EX | Hydr. damper | 180 | 14 | 2.75 | 0.05
SRU-plus 35-W-180-3-M | Hydr. damper | 180 | 14 | 3.65 | 0.05
SRU-plus 35-W-180-3-VM | Hydr. damper | 180 | 14 | 4.15 | 0.05
SRU-plus 35-W-180-90-M | Hydr. damper | 180 | 14 | 3.75 | 0.05
SRU-plus 35-W-180-3-4 | Hydr. damper | 180 | 13.4 | 2.95 | 0.05
SRU-plus 35-W-180-3-4-EX | Hydr. damper | 180 | 13.4 | 2.95 | 0.05
SRU-plus 35-W-180-3-4-M8 | Hydr. damper | 180 | 13.4 | 3.7 | 0.05
SRU-plus 35-W-180-3-4-M8-AS | Hydr. damper | 180 | 13.4 | 3.7 | 0.05
SRU-plus 35-W-90-3-4 | Hydr. damper | 90 | 13.4 | 2.95 | 0.05
SRU-plus 35-W-90-3-4-EX | Hydr. damper | 90 | 13.4 | 2.95 | 0.05
Technical data

## Slide 19
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 35-W-90-3-4-M8 | Hydr. damper | 90 | 13.4 | 3.7 | 0.05
SRU-plus 35-W-90-3-4-M8-AS | Hydr. damper | 90 | 13.4 | 3.7 | 0.05
SRU-plus 35-W-180-90-4 | Hydr. damper | 180 | 13.4 | 3.05 | 0.05
SRU-plus 35-W-180-90-4-EX | Hydr. damper | 180 | 13.4 | 3.05 | 0.05
SRU-plus 35-W-180-90-4-M8 | Hydr. damper | 180 | 13.4 | 3.8 | 0.05
SRU-plus 35-W-180-90-4-M8-AS | Hydr. damper | 180 | 13.4 | 3.8 | 0.05
SRU-plus 35-W-180-3-M-4 | Hydr. damper | 180 | 13.4 | 3.95 | 0.05
SRU-plus 35-W-180-3-M-4-M8 | Hydr. damper | 180 | 13.4 | 4.7 | 0.05
SRU-plus 35-W-180-3-M-4-M8-AS | Hydr. damper | 180 | 13.4 | 4.7 | 0.05
SRU-plus 35-W-180-90-M-4 | Hydr. damper | 180 | 13.4 | 4.05 | 0.05
SRU-plus 35-W-180-90-M-4-M8 | Hydr. damper | 180 | 13.4 | 4.8 | 0.05
Technical data

## Slide 20
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 35-W-180-90-M-4-M8-AS | Hydr. damper | 180 | 13.4 | 4.8 | 0.05
SRU-plus 35-W-180-3-VM-4 | Hydr. damper | 180 | 13.4 | 4.45 | 0.05
SRU-plus 35-W-180-3-VM-4-M8 | Hydr. damper | 180 | 13.4 | 5.2 | 0.05
SRU-plus 35-W-180-3-VM-4-M8-AS | Hydr. damper | 180 | 13.4 | 5.2 | 0.05
SRU-plus 40-W-90-3 | Hydr. damper | 90 | 20 | 4.2 | 0.05
SRU-plus 40-W-90-3-EX | Hydr. damper | 90 | 20 | 4.2 | 0.05
SRU-plus 40-H-90-3 | Hydr. damper | 90 | 20 | 4.2 | 0.05
SRU-plus 40-H-90-3-EX | Hydr. damper | 90 | 20 | 4.2 | 0.05
SRU-plus 40-W-180-3 | Hydr. damper | 180 | 20 | 4.2 | 0.05
SRU-plus 40-W-180-3-EX | Hydr. damper | 180 | 20 | 4.2 | 0.05
Technical data

## Slide 21
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 40-H-180-3 | Hydr. damper | 180 | 20 | 4.2 | 0.05
SRU-plus 40-H-180-3-EX | Hydr. damper | 180 | 20 | 4.2 | 0.05
SRU-plus 40-W-180-90 | Hydr. damper | 180 | 20 | 4.3 | 0.05
SRU-plus 40-W-180-90-EX | Hydr. damper | 180 | 20 | 4.3 | 0.05
SRU-plus 40-H-180-90 | Hydr. damper | 180 | 20 | 4.3 | 0.05
SRU-plus 40-H-180-90-EX | Hydr. damper | 180 | 20 | 4.3 | 0.05
SRU-plus 40-W-180-3-M | Hydr. damper | 180 | 20 | 5.5 | 0.05
SRU-plus 40-W-180-3-VM | Hydr. damper | 180 | 20 | 6.5 | 0.05
SRU-plus 40-W-180-90-M | Hydr. damper | 180 | 20 | 5.7 | 0.05
SRU-plus 40-W-180-3-8 | Hydr. damper | 180 | 19.2 | 4.9 | 0.05
SRU-plus 40-W-180-3-8-EX | Hydr. damper | 180 | 19.2 | 4.9 | 0.05
Technical data

## Slide 22
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 40-H-180-3-8 | Hydr. damper | 180 | 19.2 | 4.9 | 0.05
SRU-plus 40-H-180-3-8-EX | Hydr. damper | 180 | 19.2 | 4.9 | 0.05
SRU-plus 40-W-180-3-8-M8 | Hydr. damper | 180 | 19.2 | 6.45 | 0.05
SRU-plus 40-W-180-3-8-M8-AS | Hydr. damper | 180 | 19.2 | 6.45 | 0.05
SRU-plus 40-H-180-3-8-M8 | Hydr. damper | 180 | 19.2 | 6.45 | 0.05
SRU-plus 40-H-180-3-8-M8-AS | Hydr. damper | 180 | 19.2 | 6.45 | 0.05
SRU-plus 40-W-90-3-8 | Hydr. damper | 90 | 19.2 | 4.9 | 0.05
SRU-plus 40-W-90-3-8-EX | Hydr. damper | 90 | 19.2 | 4.9 | 0.05
SRU-plus 40-H-90-3-8 | Hydr. damper | 90 | 19.2 | 4.9 | 0.05
SRU-plus 40-H-90-3-8-EX | Hydr. damper | 90 | 19.2 | 4.9 | 0.05
SRU-plus 40-W-90-3-8-M8 | Hydr. damper | 90 | 19.2 | 6.45 | 0.05
SRU-plus 40-W-90-3-8-M8-AS | Hydr. damper | 90 | 19.2 | 6.45 | 0.05
Technical data

## Slide 23
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 40-H-90-3-8-M8 | Hydr. damper | 90 | 19.2 | 6.45 | 0.05
SRU-plus 40-H-90-3-8-M8-AS | Hydr. damper | 90 | 19.2 | 6.45 | 0.05
SRU-plus 40-W-180-90-8 | Hydr. damper | 180 | 19.2 | 5 | 0.05
SRU-plus 40-W-180-90-8-EX | Hydr. damper | 180 | 19.2 | 5 | 0.05
SRU-plus 40-H-180-90-8 | Hydr. damper | 180 | 19.2 | 5 | 0.05
SRU-plus 40-H-180-90-8-EX | Hydr. damper | 180 | 19.2 | 5 | 0.05
SRU-plus 40-W-180-90-8-M8 | Hydr. damper | 180 | 19.2 | 6.55 | 0.05
SRU-plus 40-W-180-90-8-M8-AS | Hydr. damper | 180 | 19.2 | 6.55 | 0.05
SRU-plus 40-H-180-90-8-M8 | Hydr. damper | 180 | 19.2 | 6.55 | 0.05
SRU-plus 40-H-180-90-8-M8-AS | Hydr. damper | 180 | 19.2 | 6.55 | 0.05
SRU-plus 40-W-180-3-M-8 | Hydr. damper | 180 | 19.2 | 6.2 | 0.05
Technical data

## Slide 24
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 40-W-180-3-M-8-M8 | Hydr. damper | 180 | 19.2 | 7.75 | 0.05
SRU-plus 40-W-180-3-M-8-M8-AS | Hydr. damper | 180 | 19.2 | 7.75 | 0.05
SRU-plus 40-W-180-90-M-8 | Hydr. damper | 180 | 19.2 | 6.4 | 0.05
SRU-plus 40-W-180-90-M-8-M8 | Hydr. damper | 180 | 19.2 | 7.95 | 0.05
SRU-plus 40-W-180-90-M-8-M8-AS | Hydr. damper | 180 | 19.2 | 7.95 | 0.05
SRU-plus 40-W-180-3-VM-8 | Hydr. damper | 180 | 19.2 | 7.2 | 0.05
SRU-plus 40-W-180-3-VM-8-M8 | Hydr. damper | 180 | 19.2 | 8.75 | 0.05
SRU-plus 40-W-180-3-VM-8-M8-AS | Hydr. damper | 180 | 19.2 | 8.75 | 0.05
SRU-plus 50-W-90-3 | Hydr. damper | 90 | 52 | 9.4 | 0.05
SRU-plus 50-W-90-3-EX | Hydr. damper | 90 | 52 | 9.4 | 0.05
Technical data

## Slide 25
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 50-H-90-3 | Hydr. damper | 90 | 52 | 9.4 | 0.05
SRU-plus 50-H-90-3-EX | Hydr. damper | 90 | 52 | 9.4 | 0.05
SRU-plus 50-W-180-3 | Hydr. damper | 180 | 52 | 9.4 | 0.05
SRU-plus 50-W-180-3-EX | Hydr. damper | 180 | 52 | 9.4 | 0.05
SRU-plus 50-H-180-3 | Hydr. damper | 180 | 52 | 9.4 | 0.05
SRU-plus 50-H-180-3-EX | Hydr. damper | 180 | 52 | 9.4 | 0.05
SRU-plus 50-W-180-90 | Hydr. damper | 180 | 52 | 9.8 | 0.05
SRU-plus 50-W-180-90-EX | Hydr. damper | 180 | 52 | 9.8 | 0.05
SRU-plus 50-H-180-90 | Hydr. damper | 180 | 52 | 9.8 | 0.05
SRU-plus 50-H-180-90-EX | Hydr. damper | 180 | 52 | 9.8 | 0.05
SRU-plus 50-W-180-3-M | Hydr. damper | 180 | 52 | 12.2 | 0.05
Technical data

## Slide 26
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 50-W-180-90-M | Hydr. damper | 180 | 52 | 12.6 | 0.05
SRU-plus 50-W-180-3-8 | Hydr. damper | 180 | 50.3 | 9.6 | 0.05
SRU-plus 50-W-180-3-8-EX | Hydr. damper | 180 | 50.3 | 9.6 | 0.05
SRU-plus 50-W-180-3-8-M8 | Hydr. damper | 180 | 50.3 | 11.55 | 0.05
SRU-plus 50-W-180-3-8-M8-AS | Hydr. damper | 180 | 50.3 | 11.55 | 0.05
SRU-plus 50-H-180-3-8-M8 | Hydr. damper | 180 | 50.3 | 11.55 | 0.05
SRU-plus 50-H-180-3-8-M8-AS | Hydr. damper | 180 | 50.3 | 11.55 | 0.05
SRU-plus 50-W-90-3-8 | Hydr. damper | 90 | 50.3 | 9.6 | 0.05
SRU-plus 50-W-90-3-8-EX | Hydr. damper | 90 | 50.3 | 9.6 | 0.05
SRU-plus 50-H-180-3-8 | Hydr. damper | 180 | 50.3 | 9.6 | 0.05
SRU-plus 50-H-180-3-8-EX | Hydr. damper | 180 | 50.3 | 9.6 | 0.05
Technical data

## Slide 27
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 50-W-90-3-8-M8 | Hydr. damper | 90 | 50.3 | 11.55 | 0.05
SRU-plus 50-H-90-3-8 | Hydr. damper | 90 | 50.3 | 9.6 | 0.05
SRU-plus 50-W-90-3-8-M8-AS | Hydr. damper | 90 | 50.3 | 11.55 | 0.05
SRU-plus 50-H-90-3-8-EX | Hydr. damper | 90 | 50.3 | 9.6 | 0.05
SRU-plus 50-H-90-3-8-M8 | Hydr. damper | 90 | 50.3 | 11.55 | 0.05
SRU-plus 50-H-90-3-8-M8-AS | Hydr. damper | 90 | 50.3 | 11.55 | 0.05
SRU-plus 50-W-180-90-8 | Hydr. damper | 180 | 50.3 | 10 | 0.05
SRU-plus 50-W-180-90-8-EX | Hydr. damper | 180 | 50.3 | 10 | 0.05
SRU-plus 50-H-180-90-8 | Hydr. damper | 180 | 50.3 | 10 | 0.05
SRU-plus 50-H-180-90-8-EX | Hydr. damper | 180 | 50.3 | 10 | 0.05
SRU-plus 50-W-180-90-8-M8 | Hydr. damper | 180 | 50.3 | 11.95 | 0.05
Technical data

## Slide 28
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 50-W-180-90-8-M8-AS | Hydr. damper | 180 | 50.3 | 11.95 | 0.05
SRU-plus 50-H-180-90-8-M8 | Hydr. damper | 180 | 50.3 | 11.95 | 0.05
SRU-plus 50-H-180-90-8-M8-AS | Hydr. damper | 180 | 50.3 | 11.95 | 0.05
SRU-plus 50-W-180-3-M-8 | Hydr. damper | 180 | 50.3 | 12.4 | 0.05
SRU-plus 50-W-180-3-M-8-M8 | Hydr. damper | 180 | 50.3 | 14.35 | 0.05
SRU-plus 50-W-180-3-M-8-M8-AS | Hydr. damper | 180 | 50.3 | 14.35 | 0.05
SRU-plus 50-W-180-90-M-8 | Hydr. damper | 180 | 50.3 | 12.8 | 0.05
SRU-plus 50-W-180-90-M-8-M8 | Hydr. damper | 180 | 50.3 | 14.75 | 0.05
SRU-plus 50-W-180-90-M-8-M8-AS | Hydr. damper | 180 | 50.3 | 14.75 | 0.05
SRU-plus 50-W-180-3-VM-8 | Hydr. damper | 180 | 50.3 | 13 | 0.05
Technical data

## Slide 29
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 50-W-180-3-VM-8-M8-AS | Hydr. damper | 180 | 50.3 | 14.95 | 0.05
SRU-plus 60-W-90-3 | Hydr. damper | 90 | 72 | 12.8 | 0.05
SRU-plus 60-W-180-3 | Hydr. damper | 180 | 72 | 12.8 | 0.05
SRU-plus 60-W-180-90 | Hydr. damper | 180 | 72 | 13.5 | 0.05
SRU-plus 60-W-180-3-M | Hydr. damper | 180 | 72 | 16.8 | 0.05
SRU-plus 60-W-180-3-VM | Hydr. damper | 180 | 72 | 17.8 | 0.05
SRU-plus 60-W-180-90-M | Hydr. damper | 180 | 72 | 17.5 | 0.05
SRU-plus 60-W-180-3-8 | Hydr. damper | 180 | 70 | 13 | 0.05
SRU-plus 60-W-180-3-8-M8 | Hydr. damper | 180 | 70 | 14.95 | 0.05
SRU-plus 60-W-180-3-8-M12 | Hydr. damper | 180 | 70 | 14.95 | 0.05
Technical data

## Slide 30
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 60-W-180-3-8-M8-AS | Hydr. damper | 180 | 70 | 14.95 | 0.05
SRU-plus 60-W-180-3-8-M12-AS | Hydr. damper | 180 | 70 | 14.95 | 0.05
SRU-plus 60-W-90-3-8 | Hydr. damper | 90 | 70 | 13 | 0.05
SRU-plus 60-W-90-3-8-M8 | Hydr. damper | 90 | 70 | 14.95 | 0.05
SRU-plus 60-W-90-3-8-M8-AS | Hydr. damper | 90 | 70 | 14.95 | 0.05
SRU-plus 60-W-180-90-8 | Hydr. damper | 180 | 70 | 13.7 | 0.05
SRU-plus 60-W-180-90-8-M8 | Hydr. damper | 180 | 70 | 15.65 | 0.05
SRU-plus 60-W-180-90-8-M12 | Hydr. damper | 180 | 70 | 15.65 | 0.05
SRU-plus 60-W-180-90-8-M8-AS | Hydr. damper | 180 | 70 | 15.65 | 0.05
SRU-plus 60-W-180-90-8-M12-AS | Hydr. damper | 180 | 70 | 15.65 | 0.05
SRU-plus 60-W-180-3-M-8 | Hydr. damper | 180 | 70 | 17 | 0.05
Technical data

## Slide 31
Designation (soft damping) | End position damping | Angle of rotation | Torque | Weight | Repeat accuracy
 |  | [°] | [Nm] | [kg] | [°]
SRU-plus 60-W-180-3-M-8-M8 | Hydr. damper | 180 | 70 | 18.95 | 0.05
SRU-plus 60-W-180-3-M-8-M8-AS | Hydr. damper | 180 | 70 | 18.95 | 0.05
SRU-plus 60-W-180-90-M-8 | Hydr. damper | 180 | 70 | 17.7 | 0.05
SRU-plus 60-W-180-90-M-8-M8 | Hydr. damper | 180 | 70 | 19.65 | 0.05
SRU-plus 60-W-180-90-M-8-M8-AS | Hydr. damper | 180 | 70 | 19.65 | 0.05
SRU-plus 60-W-180-3-VM-8 | Hydr. damper | 180 | 70 | 18 | 0.05
SRU-plus 60-W-180-3-VM-8-M8 | Hydr. damper | 180 | 70 | 19.95 | 0.05
SRU-plus 60-W-180-3-VM-8-M8-AS | Hydr. damper | 180 | 70 | 19.95 | 0.05
SRU-plus 63-W-90-3-8-L | Hydr. damper | 90 | 115 | 26.5 | 0.05
SRU-plus 63-W-90-3-8-R | Hydr. damper | 90 | 115 | 26.5 | 0.05
SRU-plus 63-W-180-3-8 | Hydr. damper | 180 | 115 | 26.5 | 0.05
Technical data

## Slide 32
2018-09-20 14:16:30
Jens Lehmann, German goalkeeper legend, SCHUNK brand ambassador since 2012 for safe, precise gripping and holding.
schunk.com/Lehmann