## Slide 1
Product presentation
KTG
Gripper for small components

## Slide 2
Gripper for small components
2-finger parallel gripper with center bore

## Slide 3
Compact. Cost-effective. Flexible.

## Slide 4
Principle of function
Drive
3
Center bore
2
Kinematics
1
Profiled rail guide
4
Housing
5
By pressurizing the first or second piston, the base jaws which are individually guided by a carrier on the piston, are moved.
The movement is synchronized by means of lever kinematics.
Functional description

## Slide 5
Advantages – Your benefits
Low weight for weight-optimized handling solutions
Long stroke in proportion to the size
Base jaws guided on roller bearings for precise gripping
Center through-hole for workpiece feeding, sensor systems or actuators
Air supply via hose-free direct connection or screw connections for flexible pressure supply in all automated systems

## Slide 6
Technical data
Technical data overview
Size | Stroke per jaw | Closing force | Opening force | Recommended workpiece weight | Weight | Max. permissible finger length
 | [mm] | [N] | [N] | [kg] | [kg] | [mm] |  |  | 
50 | 4.5 | 13 | 13 | 0.07 | 0.08 | 50