## Slide 1
Product presentation
PFH-mini
Long-stroke gripper

## Slide 2
Long-stroke gripper
2-finger parallel gripper with long jaw stroke for large parts and/or a broad range of parts

## Slide 3
Loadable. Flexible. Reliable.

## Slide 4
Principle of function
Sliding guide
3
Dust cover
2
Base Jaw
1
Centering and mounting possibilities
4
Kinematics
5
By pressure actuation of the opposing piston, the base jaws, everyone is guided by a carrier on the piston, are set in motion.
The jaw stroke is synchronized by means of rack and pinion kinematics.
Housing
6
Functional description

## Slide 5
Advantages – Your benefits
Robust sliding guide for the precise handling of different workpieces
High maximum moments possible suitable for using long gripper fingers
Double piston rack and pinion principle for centric clamping
Mounting from two sides in three screw directions for universal and flexible gripper assembly
Air supply via hose-free direct connection or screw connections for flexible pressure supply in all automated systems

## Slide 6
Technical data
Technical data overview
Size | Stroke per jaw | Closing force | Opening force | Recommended workpiece weight | Weight | Max. permissible finger length
 | [mm] | [N] | [N] | [kg] | [kg] | [mm] |  |  | 
30 | 30 .. 60 | 630 .. 720 | 570 | 3.15 | 2.65 .. 3.5 | 100 .. 150
40 | 40 .. 80 | 1260 .. 1540 | 1100 .. 1380 | 5.5 .. 6.3 | 4.6 .. 6.2 | 150 .. 200
50 | 50 .. 100 | 2600 .. 2950 | 2330 .. 2680 | 11.65 .. 13 | 9.6 .. 12.6 | 200 .. 250