## Slide 1
Product presentation
PZB-plus
Universal gripper

## Slide 2
Universal gripper
Universal 3-finger centric gripper with large gripping force and high maximum moments per finger, plus center bore

## Slide 3
Robust. Flexible. Precise.

## Slide 4
Principle of function
Wedge-hook design
3
Center bore
2
Base Jaw
1
Multi-tooth guidance
4
Housing
5
The piston is moved up and down by compressed air.
The angled active surfaces of the wedge-hook produce a synchronized, centric jaw movement.
Functional description

## Slide 5
Advantages – Your benefits
Robust multi-tooth guidance for precise handling
High maximum moments possible suitable for using long gripper fingers
High gripping forces achievable for a wide range of applications
Center through-hole available with fitting and female thread, which facilitates assembly of customer attachments. Moreover, the center bore is used for feed-through of supply hoses and others.
Air supply via hose-free direct connection or screw connections for flexible pressure supply in all automated systems
Manifold options optional with mechanic gripping force maintenance

## Slide 6
Technical data
Technical data overview
Size | Stroke per jaw | Closing force | Opening force | Recommended workpiece weight | Weight | Max. permissible finger length
 | [mm] | [N] | [N] | [kg] | [kg] | [mm] |  |  | 
50 | 2.5 | 340 .. 460 | 360 .. 500 | 1.7 | 0.26 .. 0.36 | 54 .. 58
64 | 2 .. 4 | 450 .. 1080 | 500 .. 1160 | 2.2 .. 5 | 0.51 .. 0.63 | 64 .. 72
80 | 3 .. 6 | 730 .. 1560 | 830 .. 1750 | 3.6 .. 6 | 0.8 .. 1.1 | 80 .. 90
100 | 4 .. 8 | 1600 .. 4050 | 1700 .. 4900 | 8 .. 15 | 1.5 .. 2.3 | 100 .. 110
125 | 5 .. 10 | 2700 .. 5050 | 3000 .. 5700 | 13 .. 25 | 2.5 .. 4 | 120 .. 130
160 | 13 | 4500 .. 5400 | 5800 .. 7300 | 22 | 4.8 .. 7.3 | 135 .. 160
200 | 14 .. 25 | 6400 .. 13950 | 6800 .. 16200 | 32 .. 55 | 11.5 .. 15.8 | 200 .. 280
240 | 17 .. 30 | 8700 .. 22500 | 9200 .. 24900 | 45 .. 90 | 20.5 .. 24 | 200 .. 300
300 | 20 .. 35 | 11400 .. 27400 | 12200 .. 27600 | 57 .. 100 | 38 .. 53 | 200 .. 250