## Slide 1
Product presentation
GSW-B
Gripper with shaft interface

## Slide 2
Gripper with shaft interface
The simplest solution for the integration of SCHUNK grippers in the machine tools.
Up to 1,740 N gripping force
Universal gripper PGN-plus/PZN-plus with GSW-B shank interface

## Slide 3
High flow rate. Cost-effective. Powerful.

## Slide 4
Principle of function
Multi-tooth guidance
3
Adapter plate with integrated pressure distributor
2
Mounting
1
Base Jaw
4
Wedge-hook design
5
The pressure generated by the central machine coolant supply is reduced by the pressure distributor, which is integrated in the adapter plates. The gripper can then be actuated and can actuate the base jaws correspondingly via the piston and wedge hook.
During the gripping operation the gripper continuously supplies coolant or compressed air via the lateral pressure control valve.
Housing
6
Functional description

## Slide 5
Advantages – Your benefits
Low-cost module from a universal gripper PGN-plus/PZN-plus and a shank interface
Fast, automated gripper changeover from the gripper to the storage rack
Fully automated workpiece changeover without robot or gantry system

## Slide 6
Technical data
Technical data overview
Size | Weight | Max. permissible speed | Nominal operating pressure compressed air | Nominal operating pressure coolant
 | [kg] | [1/min] | [bar] | [bar] |  |  | 
50 | 0.2 | 20 | 6 | 40
64 | 0.23 | 20 | 6 | 40
80 | 0.31 | 20 | 6 | 40
100 | 0.42 | 20 | 6 | 40