## Slide 1
Product presentation
GSW-V
Vacuum Gripper

## Slide 2
Vacuum Gripper
The simplest solution for the integration of suction grippers in the machine tools.
Up to 4.9 kg workpiece weight
Vacuum gripper for spindle interfaces for handling flat components

## Slide 3
Compact. Cost-effective. Productive.

## Slide 4
Principle of function
Media supply
3
Intake duct
2
Vacuum suction cup
1
Venturi nozzle
4
Outlet opening
5
The gripper can be used in any machine which provides compressed air or lubricating coolants supply via the toolholder mounting.
The vacuum gripper is equipped with an integrated Venturi nozzle, and therefore does not require a vacuum connection to generate negative pressure.
During the gripping operation the gripper continuously supplies coolant or compressed air.
Functional description

## Slide 5
Advantages – Your benefits
Low-cost module for flexible automation in your machine
Fast, automated gripper changeover from the gripper to the storage rack
Fully automated workpiece changeover without robot or gantry system
Universally suitable for many different workpieces

## Slide 6
Technical data
Technical data overview
Size | Weight | Recommended workpiece weight | Suction force | Max. permissible speed | Nominal operating pressure compressed air | Nominal operating pressure coolant
 | [kg] | [kg] | [N] | [1/min] | [bar] | [bar] |  |  | 
20 | 0.12 .. 0.28 | 0.28 .. 4.9 | 55 .. 980 | 20 | 6 | 40
25 | 0.15 .. 0.31 | 0.28 .. 4.9 | 55 .. 980 | 20 | 6 | 40
32 | 0.23 .. 0.39 | 0.28 .. 4.9 | 55 .. 980 | 20 | 6 | 40