## Slide 1
Product presentation
Beta
Linear axis

## Slide 2
Linear axis
The most comprehensive modular system for linear axes.
22 profile sizes are selectable
Universal linear module with optional toothed belt or spindle drive and various guiding options

## Slide 3
Flexible. Modular. Compact.
New Beta ZSE variant as a cost-effective standard solution
Defined scope of functions and variants for fast delivery and competitive price
Proven Beta ZSS technology
Available in sizes 60, 80 and 110

## Slide 4
Principle of function
Covering tape made of plastic
3
Profiled rail guide
2
Aluminum profile
1
Toothed belt
4
Ball screw spindle
5
The slide is driven by a toothed belt or a ball screw spindle and precisely guided by a (double) profiled rail guide. The cover band runs through the slide and covers the drive and guidance. The servomotor is usually connected to the profile via the drive shaft.
Functional description

## Slide 5
Advantages – Your benefits
Adaptable drive motor for versatile approach and easy integration into existing control concepts
Optional belt or spindle driven for the optimum drive for your application
Various guide options for optimal adaption to your application
Cost-effective basic version with basic functions for simple and cost-effective applications
Compact dimensions for less interfering contours
Integrated cover tape for versatility and a long tool life
Fixing via T-nuts or slot nut possible for flexibility in the integration

## Slide 6
Technical data
Technical data overview |  |  | 
Size | Max. driving force | Max. stroke | Max. acceleration
 | [N] | [mm] | [m/s²]
40 | 500 .. 1000 | 890 .. 1850 | 20 .. 30
50 | 700 .. 1000 | 860 .. 7710 | 20 .. 30
60 | 750 .. 4000 | 5220 .. 7670 | 20 .. 30
70 | 900 .. 2000 | 3725 .. 7640 | 20 .. 30
80 | 1100 .. 4000 | 5020 .. 7600 | 20 .. 40
100 | 1500 .. 4000 | 5260 .. 7720 | 20 .. 60
110 | 2000 .. 6000 | 5120 .. 7520 | 20 .. 60
120 | 4000 .. 12000 | 5120 .. 7520 | 20 .. 60
140 | 2500 .. 6000 | 4920 .. 7540 | 20 .. 60
165 | 10000 .. 18000 | 5010 .. 6920 | 20 .. 60
180 | 3500 .. 12000 | 5030 .. 5500 | 20 .. 60