## Slide 1
Product presentation
GFS
Swivel finger

## Slide 2
Swivel finger
Rotary finger for turning workpieces that are held by a gripper or can also be used as a special swivel unit

## Slide 3
Productive. Flexible. Compact.

## Slide 4
Principle of function
Damping
3
Kinematics
2
Drive
1
Rotary flange
4
Centering and mounting possibilities
5
The piston, subjected to compressed air on both sides, moves in a straight line. With its serrations, it turns the first gear. The rotary movement is transferred to the output flange by means of further gears.
Functional description

## Slide 5
Advantages – Your benefits
Integrated hydraulic end position dampers for fast swiveling cycles
scope-free end positions for highest positioning accuracy
Counter-bearing without drive or damping as a cost-efficient version of the second bearing position

## Slide 6
Technical data
Technical data overview
Size | Angle of rotation | Torque | Weight | Repeat accuracy
 | [°] | [Nm] | [kg] | [°] |  |  | 
16 | 90 .. 180 | 0.64 | 0.55 .. 0.69 | 0.07
25 | 90 .. 180 | 2.35 | 1.25 .. 1.6 | 0.07
32 | 90 .. 180 | 5 | 2.4 .. 3 | 0.07
40 | 90 .. 180 | 10 | 4 .. 5 | 0.07