## Slide 1
Product presentation
SFL
Vane swivel unit

## Slide 2
Vane swivel unit
Miniature vane swivel unit for light swiveling tasks up to 180°

## Slide 3
Flexible. Freely adjustable swivel angle.

## Slide 4
Principle of function
Fine adjustment of the angle of rotation
3
Rotary table
2
Pre-adjustment of rotating angle
1
End position damping
4
Vane swivel unit
5
The drive is pneumatic and based on the rotor principle.
The complete module can be supplied via a central, base-side connection using the direct connection.
Functional description

## Slide 5
Advantages – Your benefits
Compact design due to the almost cube shaped design several modules can be mounted in parallel
Flexible adjustment of the swivel angle from 0 -180° this results in a versatile range of applications
Fine adjustment of the angle of rotation for sensitive adjustment of end positions
Powerful for even greater masses and inertias due to the variant with hydraulic shock absorbers
High life time and excellent synchronization due to machining of the running surfaces

## Slide 6
Technical data
Technical data overview
Size | Angle of rotation | Torque | Weight | Repeat accuracy
 | [°] | [Nm] | [kg] | [°] |  |  | 
25 | 90 .. 180 | 0.1 | 0.09 | 0.05
40 | 90 .. 180 | 0.5 | 0.24 | 0.05
64 | 90 .. 180 | 3.6 | 0.71 | 0.05