## Slide 1
Product presentation
AGE-F
Compensation unit AGE-F

## Slide 2
Compensation unit AGE-F
With adjustable spring reset and compensation stroke
Up to 32 kg handling weight
Compensation unit with X-Y lateral compliance and integrated spring return

## Slide 3
Flat. Flexible. Compact.

## Slide 4
Principle of function
Slot for magnetic switch
3
Spring-actuated reset
2
Linear guide
1
Housing
4
The compensation unit AGE-F enables the activation of the linear movement in the X and Y axis of the robots or handling units. For example, this allows axis offset of workpieces to be compensated and centrically aligned again.
Functional description

## Slide 5
Advantages – Your benefits
Spring reset in three different spring strengths. for a defined, centric position at a repeat accuracy of 0.02 mm
Direct assembly of grippers no need for additional adapter plates
Cross roller guides for smooth compensation at low compensation forces
Adjustable compensation stroke for minimizing interfering contours

## Slide 6
Technical data
Technical data overview
Size | Compensation XY | Weight
 | [mm] | [kg] |  |  | 
31 | 1.5 | 0.123
40 | 2 | 0.23
63 | 4 | 0.78
80 | 5 | 3.13