## Slide 1
Product presentation
MWS
Miniature change system

## Slide 2
Miniature change system
Manual tool change system with integrated air feed-through and optional electric feed-through

## Slide 3
Modular. Compact. Flexible.

## Slide 4
Principle of function
Anti-twist protection
3
Drive ring
2
Screw surface
1
Locking mechanism
4
Pneumatic feed-through
5
The miniature change system (MWS) consists of a miniature change master (MWK) and a miniature change adapter (MWA). A form-fit connection is established between the miniature change master (MWK) and the miniature change adapter (MWA) by actuating the locking ring. An integrated pneumatic feed-through safely provides the tool with electricity.
Electric feed-through
6
Functional description

## Slide 5
Advantages – Your benefits
Extremely flat design for less interfering contours
Easy handling without additional tools quickly and easily removable at any time
Center bore for feed-through of parts, camera, laser beams, etc.
Integrated feed-through for six pneumatic or four electrical signals
Suitable storage rack to ensure the optimum adaption to each application
ISO mounting pattern for simple assembly; in compliance with DIN 32565 level 4

## Slide 6
Technical data
Technical data overview
Size | Recommended handling weight | Weight | Min./max. distance when locking | No. of fluid feed-throughs | Number of electrical feed-throughs
 | [kg] | [g] | [mm] |  |  |  |  | 
20 | 0.5 | 7 .. 9 | 0.25 | 2 | 4
30 | 1 | 12 .. 16 | 0.25 | 2 | 4 .. 6