## Slide 1
Product presentation
ERS
Universal rotary unit

## Slide 2
Universal rotary unit
The flattest torque motor with the highest torque for industrial automation.
77 mm design height for 27 Nm torque
Electrical rotary unit with torque motor and angle of rotation > 360° as well as the optional pneumatic brake and rotary feed-through, and if desired increased protection class (IP54)

## Slide 3
Compact. Flexible. Fast.

## Slide 4
Principle of function
External rotor with center bore
3
Stator
2
Base support stator
1
Pneumatic holding brake
4
Electrical coupling flange with plug connectors
5
The rotary module ERS is based on a permanently energized torque motor, whose large center bore ensures a media feed-through. The position is ensured using a four point bearing, which is designed for high maximum moments.
Micro valve
6
Functional description

## Slide 5
Advantages – Your benefits
Integrated torque drive for high torque and flexible use by controlled position, velocity and torque
Large center bore for feed-through lines and media hoses
Compact design for minimal interfering contours and for use in confined spaces
Easy system integration by standard encoder interface (Sin/Cos)
Versatile actuation options for simple integration into existing control concepts using different external third-party controllers (e.g. Bosch Rexroth IndraDrive or Siemens SINAMICS)
Optional pneumatic holding brake for maintaining the position in downtime

## Slide 6
Technical data
Technical data overview
Size | Nominal torque | Peak torque | Nominal speed | Max. mass moment of inertia | Repeat accuracy | Weight
 | [Nm] | [Nm] | [1/min] | [kgm²] | [°] | [kg] |  |  | 
135 | 2.5 | 8 | 1000 | 0.07 | 0.01 | 2.7
170 | 4.7 .. 5 | 17 | 250 .. 700 | 0.2 | 0.01 | 4.2 .. 6.3
210 | 9.3 .. 10 | 27 | 250 .. 600 | 0.6 | 0.01 | 7.4 .. 10.9