## Slide 1
Product presentation
ERM
Heavy-duty rotary module

## Slide 2
Heavy-duty rotary module
The most powerful modular rotary module for use in automated systems.
75 Nm torque for high loads
Electric rotary module for high loads with adaptable servomotor, rotary angle > 360°, center bore, and optional feed-throughs

## Slide 3
Adaptable. Strong. Loadable.

## Slide 4
Principle of function
2-step hypoid gear speed
3
Bevel gear
2
Drive shaft
1
Output flange
4
Integrated air supply with mounting holes
5
The torque of the motor is transferred from the driving shaft via the two stage hypoid gearing to the output flange. Via the rotary feed-through compressed air can be fed through to the distributor flange for connection of the output flange. The orientation of the transmission housing can be adjusted in 4 x 90° steps (for fastening the module or the attachment).
Functional description

## Slide 5
Advantages – Your benefits
Modular drive concept for adaption of common servomotors for example from Bosch or Siemens
Easy system integration by use of a preferred motor with available fieldbus and safety technology
90° swivel-mounted drive for flexible adaptation to gantries or robots
High torque and precision for the positioning of heavy loads with high precision
Center bore and integrated feed-through for cable and media feed-through
High robustness and large loading area for demanding applications

## Slide 6
Technical data
Technical data overview
Size | Peak drive moment | Peak output moment | Repeat accuracy | Weight
 | [Nm] | [Nm] | [°] | [kg] |  |  | 
160 | 2.3 | 75 | 0.035 | 15.5 .. 21.5