## Slide 1
Product presentation
ERD
Universal rotary unit

## Slide 2
Universal rotary unit
The most compact torque motor with integrated electric and pneumatic rotary feed-through.
0.01° repeat accuracy
Powerful torque motor with absolute encoder and electric and pneumatic rotary feed-through

## Slide 3
Fast. Compact. Flexible.

## Slide 4
Principle of function
Fixed primary part
3
Absolute encoder plug
2
Motor plug
1
Secondary component
4
Energy feed-through
5
The unit is driven by a 3-phase brushless synchronous motor with permanent excitation.
As it is a direct drive, it no longer needs mechanical transmission elements such as gears, eliminating the resulting inaccuracies.
Housing
6
Functional description

## Slide 5
Advantages – Your benefits
With absolute position measurement system Less programming effort and time saving when commissioning and in operation
High dynamics for shorter cycle times therefore a high productivity is achieved
Integrated air and electric feed-through for safe energy supply of grippers
Almost no wear parts For long service life and reliability of the system
No mechanical play between the drive components for flexible response behavior and high positioning accuracy
Optionally certified safety devices according to SIL2/PLd with the HIPERFACE® and DRIVE-CliQ interfaces for applications with high standards in the area of machine safety

## Slide 6
Technical data
Technical data overview
Size | Nominal torque | Peak torque | Max. RPM | Max. mass moment of inertia | Repeat accuracy | Weight
 | [Nm] | [Nm] | [1/min] | [kgm²] | [°] | [kg] |  |  | 
4 | 0.4 | 1.2 | 600 | 0.008 | 0.01 | 1.2
8 | 0.8 | 2.4 | 600 | 0.009 | 0.01 | 1.5 .. 1.55
12 | 1.2 | 3.6 | 600 | 0.011 | 0.01 | 1.8