## Slide 1
Product presentation
LOG
Internal hole gripper

## Slide 2
Internal hole gripper
Light gripper made of very resistant polyamide with closed diaphragm system

## Slide 3
Cost-effective. Smooth. Reliable.

## Slide 4
Principle of function
Gripping surface
3
Mounting threads
2
Air connection thread
1
O-ring seal
4
Membrane
5
The membrane expands when pressure is applied, creating a synchronized movement of the gripping surfaces.
Internal stop/overload protection
6
Functional description

## Slide 5
Advantages – Your benefits
Low weight allows high dynamics in the application
Closed membrane system and internal stop protect the expansion membrane against damage
Short delivery time for customized measurements
Long service life enables long-lasting economical use
Air supply via hose-free direct connection or screw connections for flexible pressure supply in all automated systems

## Slide 6
Technical data
Technical data overview
Size | Gripper Ø D ±0.2 | Height H | Opening force for Ø Dmin | Opening force for Ø Dmax | Weight | Recommended workpiece weight
 | [mm] | [mm] | [N] | [N] | [kg] | [kg] |  |  | 
20 | 19.8 | 29 | 107.2 | 27.3 | 0.008 | 0.55
40 | 39.6 | 47 | 241.4 | 66.7 | 0.034 | 1.23
60 | 59.4 | 70.5 | 596.7 | 190.5 | 0.108 | 3.04
80 | 79.2 | 94 | 972.7 | 433.3 | 0.238 | 4.96
99 | 98.01 | 116.33 | 2516.7 | 1166.7 | 0.44 | 12.83