## Slide 1
Product presentation
DPG-plus
Sealed gripper

## Slide 2
Sealed gripper
The most proven sealed gripper on the market for wet and dirt-intensive environments.
Protection class IP 67
Dense 2-finger parallel gripper that meets the requirements of IP67 and does not allow substances to enter the working environment

## Slide 3
Reliable. Fully encapsulated. Loadable.

## Slide 4
Principle of function
Lip seal
3
External round base jaw
2
Inner base jaw with multi-tooth guidance
1
Oval piston with rod and wedge-hook
4
Centering and mounting possibilities
5
The piston is moved up and down by compressed air.
The angled active surfaces of the wedge-hook produce a synchronized, parallel jaw motion.
Functional description

## Slide 5
Advantages – Your benefits
Robust interior multi-tooth guidance for the precise handling of different workpieces
Lip seal at the outside round guidance for permanent, secure gripper sealing
High maximum moments possible suitable for using long gripper fingers
Sealed 2-Finger Parallel Gripper complies to IP67 requirements despite a high moment load
Drive concept oval piston for maximum gripping forces
Mounting from two sides in three screw directions for universal and flexible gripper assembly
Air supply via hose-free direct connection or screw connections for flexible pressure supply in all automated systems
Compact dimensions for minimal interfering contours in handling

## Slide 6
Technical data
Technical data overview |  |  |  |  |  | 
Size | Stroke per jaw | Closing force | Opening force | Recommended workpiece weight | Weight | Max. permissible finger length
 | [mm] | [N] | [N] | [kg] | [kg] | [mm]
40 | 2.5 | 110 .. 145 | 120 .. 165 | 0.55 | 0.12 .. 0.14 | 40
50 | 2 .. 4 | 125 .. 424 | 130 .. 453 | 0.6 .. 2.3 | 0.25 .. 0.34 | 30 .. 50
64 | 3 .. 6 | 225 .. 780 | 240 .. 834 | 1.1 .. 4.2 | 0.39 .. 0.55 | 40 .. 64
80 | 4 .. 8 | 375 .. 1270 | 415 .. 1406 | 1.8 .. 6.9 | 0.68 .. 0.95 | 50 .. 80
100 | 5 .. 10 | 625 .. 2120 | 685 .. 2318 | 3.1 .. 11.7 | 1.1 .. 1.61 | 64 .. 100
125 | 6 .. 13 | 1025 .. 3486 | 1110 .. 3760 | 5.1 .. 19.1 | 1.9 .. 2.9 | 64 .. 125
160 | 8 .. 16 | 1560 .. 4995 | 1680 .. 5402 | 7.8 .. 27.3 | 3.65 .. 8 | 80 .. 160
200 | 14 .. 25 | 2565 .. 5940 | 2730 .. 6490 | 12.8 .. 22.1 | 7.3 .. 9.5 | 125 .. 200
240 | 17 .. 30 | 3780 .. 7500 | 4000 .. 7835 | 18.9 .. 29.25 | 11.5 .. 14.6 | 150 .. 240
300 | 20 .. 35 | 5400 .. 11250 | 5635 .. 11700 | 27 .. 46.35 | 19.6 .. 23.6 | 150 .. 300
380 | 45 | 8140 .. 11240 | 8460 .. 11430 | 40.7 | 42 .. 52 | 300 .. 380