## Slide 1
Product presentation
SRU-plus
Universal swivel unit

## Slide 2
Universal swivel unit
The universal swivel unit on the market - with a wide range of variants for industrial automation.
Swiveling times from 0.3 seconds
Universally usable unit for pneumatic swivel and turning movements

## Slide 3
Robust. Fast. High Performance.

## Slide 4
Principle of function
Housing
3
Pinion
2
Drive
1
Sleeve technology
4
Damping
5
When subjected to pressure, the two pneumatic pistons move their end faces in a straight line in their respective bores thus turning the pinion by means of the serrations on their sides.
Functional description

## Slide 5
Advantages – Your benefits
Finely graded series with a steady increase in torque for multiple cases of application, the correct size as a standard product is available
Swivel angle can be selected as either 90° or 180° complete flexibility in selecting the angle of rotation, application-specific angles possible on request
End position adjustability +3°/-3° (small) or +3°/-90° (large) can be selected
Middle position can be selected as pneumatic or locked The locked middle position can be unlocked when loaded. The two types of middle positions always allow further rotation in either direction.
Fluid feed-through can be used for gases, fluids, and vacuum therefore no interfering hoses
Electrical rotary feed-through for long-lasting, reliable feed-through of sensor, actuator or optionally bus signals
Choice of electronic magnetic sensors or inductive proximity sensors for absolute variability of position monitoring
Exchangeable screw-in guide sleeves (bushing) allow for easy maintenance and rapid exchange t after several million cycles.
Series extends downwards with the SRU-mini series, for a wide range of applications

## Slide 6
Technical data
Technical data overview
Size | Angle of rotation | Torque | Weight | Repeat accuracy
 | [°] | [Nm] | [kg] | [°] |  |  | 
20 | 90 .. 180 | 3 .. 3.4 | 1.2 .. 2.61 | 0.05
25 | 90 .. 180 | 4.6 .. 5 | 1.6 .. 3.45 | 0.05
30 | 90 .. 180 | 9 .. 9.5 | 2.4 .. 4.4 | 0.05
35 | 90 .. 180 | 13.4 .. 14 | 2.65 .. 5.2 | 0.05
40 | 90 .. 180 | 19.2 .. 20 | 4.2 .. 8.75 | 0.05
50 | 90 .. 180 | 50.3 .. 52 | 9.4 .. 14.95 | 0.05
60 | 90 .. 180 | 70 .. 72 | 12.8 .. 19.95 | 0.05
63 | 90 .. 180 | 115 | 26.5 | 0.05