## Slide 1
Superior Clamping and Gripping
SRU-plus
Technical Presentation

## Slide 2: Contents
Video
Functionality
Catalog Pages
Moment of Inertia
Shock Absorber Adjustability
End Position Adjustability
Pneumatic Intermediate Position
Locked Intermediate Position
Fluid Feed-through Option
Electric Feed-through Option
Sensors
Ordering Code
Maintenance

## Slide 3: SRU-plus

## Slide 4: SRU-plus Functionality
180 degrees
90 degrees

## Slide 5: SRU-plus Functionality

## Slide 6: SRU-plus Functionality
Powerful, double piston pneumatic drive
Robust pinion to output rotary motion
Hard anodized, light-weight, aluminum alloy housing
Replaceable sleeves for radial adjustability and easy maintenance
Integrated hydraulic shock absorbers for high energy absorbtion
Middle bore for utility pass-thru

## Slide 7: SRU-plus Sizes
SRU-plus 20
SRU-plus 25
SRU-plus 30
SRU-plus 35
SRU-plus 40
SRU-plus 50
Chart: Torque [Nm]
| SRU-plus 20 | SRU-plus 25-EDF | SRU-plus 25 | SRU-plus 30-EDF | SRU-plus 30 | SRU-plus 35-EDF | SRU-plus 35 | SRU-plus 40-EDF | SRU-plus 40 | SRU-plus 50-EDF | SRU-plus 50
Torque (Nm) | 2.05 | 4.6 | 5 | 9 | 9.5 | 13.4 | 14 | 19.2 | 20 | 50.3 | 52
Torque range from 3 to 50 Nm

## Slide 8: SRU-plus Catalog Pages

## Slide 9: SRU-plus Catalog Pages
W= Soft shock absorbers
H= Hard shock absorbers

## Slide 10: Moment of Inertia
The property of a distribution of mass in space that measures its resistance to rotational acceleration about an axis.
ls
lL
J1= J0+m*l2
J1= Final moment of inertia
J0= Initial Moment of inertia
m= mass
l= radius

## Slide 11: Moment of Inertia
Assume J0=0.02
J1=J0+m*l2
J1=0.02+(1+0.7)*02
J1=0.02 kg*m2
Workpiece = 1 kg
PGN+80-1 with fingers = 0.7 kg
l=0
J1=J0+m*l2
J1=0.02+(1+0.7)*0.22
J1=0.02+0.0428
J1= 0.0628 kg*m2
l=200mm

## Slide 12: Moment of Inertia
SRU plus 25
J1=0.02
J1= 0.0628
W= Soft shock absorbers
H= Hard shock absorbers

## Slide 13: Setting the Shock Absorbers
Remove the shock cover
(Pos. 101a)
Secure stop „A“ (Pos. /1/) with a wrench and loosen the nut
(Pos. 101b)
Secure stop „A“ and unscrew the stop pin A (Pos. 89/79)
Test the unit
Secure stop pin „A“ (Pos. 89/79)
Replace cover
Repeat the process for the opposite side

## Slide 14: SRU-plus – End Position Adjustability

## Slide 15: Setting the End Position
Loosen the lock nut (Pos. 35)
Pressurize port „A“
Rotate in/out the end stop „B“ (Pos. /2/)
Tighten the lock nut (Pos. 35)
Verify end position „B“
Ventilate port „A“ and pressurize port „B“
Rotate in/out end stop „A“ (Pos. /1/)
Verify end position „A“
Tighten lock nut (Pos. 35)

## Slide 16: SRU-plus – Intermediate Positions
SRU-plus-M
pneumatic middle position
Advantages
+/- 3o mid-position adjustability
Compensating middle position
Easy Operation

## Slide 17: SRU-plus – Intermediate Positions
SRU-plus-VM
locked middle position
Advantages
+/- 3o mid-position adjustability
Locked middle position
No over travel
Can hold against gravity

## Slide 18: SRU-plus with Fluid Feed-through
Fluid Feed-through
Direct Connection
Gases
Vacuum
Liquids
8 bar

## Slide 19: Options for Fluid Feed-through
Pneumatic Distributor
for Fluid feed-through

## Slide 20: SRU-plus with Electric Feed-through (EDF)
Electric Feed-through
10 leads
24 Volts
1 amp
Ideal for gripper sensors

## Slide 21: SRU-plus Sensors
Electronic Magnetic Sensors
Magnets on the piston
End position sensing
Middle position sensing
Inductive Proximity Sensors
Additional kit required
End position sensing
Middle position sensing
Functional with EDF

## Slide 22: SRU-plus Ordering Code

## Slide 23: SRU-plus Maintenance Intervals
After 2 million cycles:
Replace and lubricate the seals
Lubricate the SRU-plus  rack and pinion, sleeves
Shock Absorbers:
Regularly check them for wear
If wear is apparent, adjust the shock absorbers
If adjusting does not work, replace the shock absorbers
Lubrication Points | Lubricant
Serrations and pinion | Molykote BR 2 plus
Metal Sliding Surfaces | Renolit HLT 2
All Seals | 
Consult the Assembly and Operating Manual
shipped with the unit/Sales Tool Box/Internet

## Slide 24: SRU-plus Application Examples

## Slide 25
www.schunk.com
Jens Lehmann, a German goalkeeper legend,
brand ambassador for SCHUNK since 2012