## Slide 1
Product presentation
EZN
Centric Grippers

## Slide 2
Centric Grippers
The only electric 3-finger centric gripper with multi-tooth guidance.
Servo-electric 3-finger centric gripper with high gripping force and high maximum moment due to multi-tooth guidance

## Slide 3
Robust. Flexible. Strong.

## Slide 4
Principle of function
Housing
3
Base Jaw
2
Wedge-hook design
1
Spindle nut
4
Drive
5
The spindle nut which is mounted on bearings, transfers the rotary motion of the servomotor into an axial motion.
The oblique surfaces of the wedge-hook generate a synchronous jaw movement.
Functional description

## Slide 5
Advantages – Your benefits
Drive design of servomotor for flexible use
With external electronics for simple integration into existing servo-controlled concepts via PROFINET, PROFIBUS or CAN
Pre-positioning capability to reduce cycle times through a short working stroke
Robust multi-tooth guidance for precise handling
High maximum moments possible suitable for using long gripper fingers
Fastening at one gripper side in two screw directions for universal and flexible gripper assembly

## Slide 6
Technical data
Technical data overview
Size | Stroke per jaw | Min. gripping force | Max. gripping force | Max. permissible finger length | Recommended workpiece weight | Weight | Nominal voltage
 | [mm] | [N] | [N] | [mm] | [kg] | [kg] | [V DC] |  |  | 
64 | 6 | 140 | 500 | 80 | 2.5 | 0.98 .. 1.08 | 24
100 | 10 | 300 | 800 | 125 | 4 | 2.3 .. 2.48 | 24