## Slide 1
Product presentation
EGN
Universal gripper

## Slide 2
Universal gripper
The first electric 2-finger parallel gripper with multi-tooth guidance.
Up to 1,000 N gripping force
Servo-electric 2-finger parallel gripper with high gripping force and moment loads due to the multi-tooth guidance

## Slide 3
Robust. Flexible. Strong.

## Slide 4
Principle of function
Housing
3
Multi-tooth guidance
2
Wedge-hook design
1
Spindle nut
4
Drive
5
The spindle nut which is mounted on bearings, transfers the rotary motion of the servomotor into an axial motion.
The angled active surfaces of the wedge-hook produce a synchronized, parallel jaw motion.
Functional description

## Slide 5
Advantages – Your benefits
Drive design of servomotor for flexible use
With external electronics for simple integration into existing servo-controlled concepts via PROFINET, PROFIBUS or CAN
Pre-positioning capability to reduce cycle times through a short working stroke
Robust multi-tooth guidance for precise handling
High maximum moments possible suitable for using long gripper fingers
Mounting from two sides in three screw directions for universal and flexible gripper assembly

## Slide 6
Technical data
Technical data overview
Size | Stroke per jaw | Min. gripping force | Max. gripping force | Max. permissible finger length | Recommended workpiece weight | Weight | Nominal voltage
 | [mm] | [N] | [N] | [mm] | [kg] | [kg] | [V DC] |  |  | 
80 | 8 | 170 | 400 | 100 | 2 | 0.84 .. 0.94 | 24
100 | 10 | 170 | 720 | 125 | 3.6 | 1.35 .. 1.53 | 24
160 | 16 | 250 | 1000 | 220 | 5 | 3 .. 3.4 | 24