## Slide 1
ROTA HSA
Compensation Chucks

## Slide 2: Product overview
Clamping Technology
Gripping Systems
Manual Lathe Chucks
Power Lathe Chucks with Through-hole
Power Lathe Chucks with Jaw Quick-change System
Power Lathe Chucks without Through-hole
Pneumatic Power Chucks
Steady Rests
Quick-change Systems
Customized Solutions
Chuck Jaws
Toolholders
Hydraulic Expansion Technology
Stationary Workholding
Lathe Chucks

## Slide 3: ROTA overview Customized Solutions
ROTA BEV
ROTA HSA
ROTA NCM-L
ROTA 4B
ROTA NCM
ROTA DFF
ROTA HSH

## Slide 4: ROTA HSA Example of application
Clamping device:
HSA 250.
Features/Application:
The workpiece is clamped between the tips. The transmission of torque is performed by three compensational clamping jaws.

## Slide 5: ROTA HSA
Center point
Base jaw with fine serration
Floating piston
Hardened chuck body
2
1
3
4
2
1
3
4

## Slide 6: Variants ROTA HSA
Technical Data | Max. RPM [min-1] | Max. clamping force [kN] | Actuating force [kN] | Stroke/jaw [mm] | Piston stroke [mm] | Compensation in ∅ [mm]
ROTA HSA 160 | 3600 | 50 | 25 | 4.8 | 18 | 3
ROTA HSA 200 | 3200 | 72 | 36 | 5.5 | 18 | 4
ROTA HSA 250 | 3000 | 110 | 46 | 6.5 | 25 | 4
ROTA HSA 315 | 2500 | 120 | 50 | 7.5 | 25 | 5
ROTA HSA 400 | 1800 | 150 | 61 | 9 | 30 | 5
ROTA HSA 500 | 1000 | 250 | 125 | 12 | 40 | 8

## Slide 7: SCHUNK Services
Engineering
Dimensioning of special plates designed to the manufacturing specifications
Development of special solutions together with the customer
FEM analysis for critical components
Testing
Endurance tests with all new developments
Abrasion checking
Measurement of accuracy
Service
Initial operation of customer´s solution
Inspection and maintenance
Repairs