## Slide 1
Product presentation
SHS
Gripper change system

## Slide 2
Gripper change system
The world's first change system with integrated presence and locking monitoring.
up to a handling weight of 58 kg
Manual tool change system with integrated air feed-through, locking monitoring, and optional electric feed-through.

## Slide 3
Flexible. Compact. Intuitive.
Convenient manual operation using a simple locking lever
Six sizes are available
Sensor technology is optionally available for monitoring locking and presence monitoring
Integrated pneumatic feed-through
Wide range of electric, pneumatic, and fluid modules

## Slide 4
Principle of function
Locking bolt
3
Lock sensing
2
Locking lever
1
Air feed-through
4
The manual change system (SHS) consists of a manual change head (SHK) and a manual change adapter (SHA). The manual change head (SHK) is form-fit locked with the manual change adapter (SHA), and due to the patented locking it is free from play. A pin is pushed forward or backward via a locking lever for locking or unlocking. An integrated pneumatic feed-through supplies the tool with energy.
Functional description

## Slide 5
Advantages – Your benefits
Series with six unit sizes for optimal size selection and a broad application range
Integrated pneumatic feed-through for a safe power supply of the handling modules and tools
The locking lever is opened sideways this allows the changer to be easily operated even in confined spaces
Optional locking and presence monitoring thus increased process reliability
Wide range of electric, pneumatic, and fluid modules for universal energy transmission possibilities
ISO mounting pattern for easy assembly to most types of robots without needing additional adapter plates

## Slide 6
Technical data
Technical data overview |  |  |  |  |  | 
Size | Recommended handling weight | Lock sensing | Weight | Number of pneumatic feed-throughs | Feed-throughs for radial use | Connection flange according to
 | [kg] |  | [kg] |  |  | 
40 | 9 | optionally via attachment kit | 0.075 .. 0.14 | 4 | 2 .. 4 | ISO 9409-1-40-4-M6
50 | 11 | optionally via attachment kit | 0.1 .. 0.25 | 6 | 3 .. 6 | ISO 9409-1-50-4-M6
63 | 18 | optionally via attachment kit | 0.2 .. 0.41 | 6 | 3 .. 6 | ISO 9409-1-63-4-M6
80 | 36 | optionally via attachment kit | 0.35 .. 0.74 | 9 | 4 .. 9 | ISO 9409-1-80-6-M8
100 | 43 | optional | 0.55 .. 1.3 | 12 | 6 .. 12 | ISO 9409-1-100-6-M8
125 | 58 | optional | 1.2 .. 2.8 | 12 | 6 .. 12 | ISO 9409-1-125-6-M10