## Slide 1
Product presentation
ELP
Linear axis

## Slide 2
Linear axis
There is no other electric linear module on the market that is as user-friendly to configure
Ready for takeoff in only 2 work steps!
Electric linear module with direct drive and integrated controller, scope-free guided using pre-loaded roller guideü

## Slide 3
Easy. Fast. Reliable.
Module operating mode now freely selectable (M1 or Auto-Learn function)
Manual speed configuration using rotary switches
Also suitable for use in cam-controlled systems
Control via digital I/O
Rotary switch optically improved

## Slide 4
Principle of function
Control electronics
3
Drive
2
Roller guide
1
End position adjustability
4
Connection plug
5
The electric drive consists of a primary part (motor coil) and a secondary part (permanent magnets). Inside the controller the phase and amplitude of the applied electric current are controlled. This sets the profile, which is fitted with magnets, in motion.
Mounting pattern
6
Functional description

## Slide 5
Advantages – Your benefits
Control via digital I/O for easy commissioning and rapid integration into existing systems.
10 independent extension and retraction speeds for high flexibility in cycle times
Linear direct drive for almost wear-free use and a long service life
Robust bearing guidance for high load capacities and end-position accuracy in all installation positions
Maintenance-free for high machine uptime and low operating costs
Compact dimensions for less interfering contours
Standardized mounting bores for numerous combinations with other components from the modular system

## Slide 6
Technical data
Technical data overview
Size | Max. stroke | Nominal force | Max. useful load (horizontal) | Max. useful load (vertical)
 | [mm] | [N] | [kg] | [kg] |  |  | 
25 | 30 .. 80 | 17 | 1 | 0.75
50 | 40 .. 100 | 45 | 3 | 2
100 | 80 .. 200 | 104 | 6 | 4