## Slide 1
Detail presentation technics
Electric Linear Module ELP

## Slide 2: Sizes and stroke versions
Stroke 50
Stroke 80
Stroke 60
Stroke 100
Stroke 80
Stroke 120
Stroke 200
ELP100
ELP50
ELP25
Stroke 40
Stroke 30

## Slide 3: Allocation of payload
 | Payload vertical | Payload horizontal
ELP 25 | 0,75 kg | 1 kg
ELP 50 | 2 kg | 3 kg
ELP 100 | 4 kg | 6 kg

## Slide 4: Calculation of cycle times
Travel times in horizontal installation position
With maximum playload
Speed levels 1 – 10
ELP 25
ELP 50
ELP 100

## Slide 5: Internal construction
Secondary part as a biprism guidance
Motor
Housing
Electronics cover
Roller cage with forced guidance
Measuring system
Electronics

## Slide 6: End position adjustability
Overstroke of +2mm
on both sides
Adjusting screw end position back
stop plate
Adjusting screw end position front

## Slide 7: Electrical connection
Control (SPS)
M8, 4 pole
Power supply
M12, 4 pole, T-coded

## Slide 8: Control panel
LED display
Learn Mode
Error display
Ready
Speed adjustment
retracting
Speed adjustement
extending

## Slide 9: Sensors
Monitoring with magnetic switches MMS
Flush-mounted in the sensor groove
Monitoring position
retracted
Monitoring position
extended

## Slide 10: Sensors
Monitoring with inductive proximity switches IN
Attachment kit necessary
Bracket for IN 80
Cam switch
You can find further information in the catalog

## Slide 11: Attachment accessory
Load compensation - retrofittable with attachment kit
Pneumatic clamping device (no standard availability)
Load compensation for ELP 100
MagSpring 37
Load compensation for ELP 25
MagSpring 20

## Slide 12: Strain relief accessory
Power cable
Signal cable
Mounting
ridge
Strain relief for electrical supply lines
Directly mountable

## Slide 13: Strain relief accessory
Cables for sensors and other actuators can be fastened directly on the strain relief as well

## Slide 14: Strain relief accessory

## Slide 15: Possible Combinations
4x Screws
2x Centering sleeves
Modules can be assembled in many combinations among themselves without any adapter plates
You can find more informations in the operating manual