## Slide 1
Product presentation
Co-act EGP-C
Collaborating gripper for small components

## Slide 2
Collaborating gripper for small components
The world's first certified industrial gripper for collaborative operation.
Certified in accordance with ISO/TS 15066.
Electric 2-finger parallel gripper certified for collaborative operation with actuation via 24 V and digital I/O

## Slide 3
Collaborative. Powerful. Certified.
Plug & Work! Pre-assembled gripping unit with robot interface for quick and easy assembly. Directly compatible with cobots from Universal Robots, KUKA, FANUC, Techman Robot, OMRON, Doosan Robotics, Mitsubishi and ABB.
Integrated status display
DGUV certified for collaborative operation
Attachment fingers as accessories

## Slide 4
Principle of function
Flange
3
Gripper for small components EGP
2
Collision protection
1
LED strip light
4
Integrated sensor system
5
The Co-act EGP-C gripper is electrically driven and has an integrated current limitation and collision protective cover. The current limitation ensures that the gripping force does not exceed a defined value. The collision protective cover serves for minimizing the risk of injury during the use in collaborative operations.
Service flap sensor system
6
Service flap gripping force
7
Functional description

## Slide 5
Advantages – Your benefits
Certified gripping unit saves effort for safety assessment of the application
Plug & Work for a variety of different cobots
Control via digital I/O for easy commissioning and rapid integration into existing systems.
Functional safety ensured due to inherent safety with current limitation
Pre-assembled gripping unit with robot interface for a easy and fast integration
Integrated status display For a visual indicator of the application state
Service flaps in the collision protection cover fitted to adjust the gripping force and the sensor system
Brushless DC servomotor for almost wear-free use and a long service life
Attachment fingers available with three different inserts

## Slide 6
Technical data
Technical data overview |  |  |  |  |  | 
Size | Stroke per jaw | Min. gripping force | Max. gripping force | Recommended workpiece weight | Max. permissible finger length | Weight
 | [mm] | [N] | [N] | [kg] | [mm] | [kg]
40 | 6 | 35 | 140 | 0.7 | 50 | 0.59 .. 0.89
64 | 10 | 65 | 230 | 1.15 | 80 | 1.11 .. 1.38