## Slide 1
New products 2019
Product presentation
March 2019

## Slide 2
Universal gripper
The world's most proven gripper on the market – with permanent lubrication in the multi-tooth guidance.
Lifelong maintenance-free Guaranteed!
Universal 2-finger parallel gripper with permanent lubrication, high gripping force, and high maximum moments due to the use of a multi-tooth guidance.

## Slide 3
Reliable. Robust. Flexible.
Perfected multi-tooth guidance
Lubricant pockets in the mult-tooth guidance
Dust-tight version SD
ATEX version EX
Portfolio expansion - new sizes PGN-plus-P 40, 160 and 240

## Slide 4
Principle of function
Bracket for sensors
3
Base Jaw
2
Multi-tooth guidance
1
Housing
4
Centering and mounting possibilities
5
Functional description
The piston is moved up and down by compressed air.
The angled active surfaces of the wedge-hook produce a synchronized, parallel jaw motion.
Wedge-hook design
6
Piston
7
Spring for gripping force maintenance
8

## Slide 5
Advantages – Your benefits
Robust multi-tooth guidance for precise handling
High maximum moments possible suitable for using long gripper fingers
Lubricant pockets in the mult-tooth guidance ensure process reliability and extended maintenance intervals
Maximum piston surface area for maximum gripping forces
Mounting from two sides in three screw directions for universal and flexible gripper assembly
Air supply via hose-free direct connection or screw connections for universal and flexible gripper assembly
Comprehensive sensor accessory program for versatile querying possibilities and stroke position monitoring
Manifold options for special optimization for your specific case of application (dust-tight, high-temperature, corrosion-protected, and much more)

## Slide 6
Availability of variants & options
Size | PGN-plus | PGN-plus-P [€]
40 | 510€ | 444€
50-1 | 535€ | 467€
64-1 | 580€ | 509€
80-1 | 645€ | 564€
100-1 | 735€ | 643€
125-1 | 855€ | 750€
160-1 | 1122€ | 1010€
200-1 | 1470€ | 1291€
240-1 | 1791€ | 1612€
300-1 | 2353€ | 2118€
380-1 | 3070€ | 2762€
PGN-plus-P will be released in all sizes, variants and with all options from July 2019!
German list prices:

## Slide 7
Technical data
Technical data overview |  |  |  |  |  |  | 
Size | Stroke per jaw | Closing force | Opening force | Recommended workpiece weight | Weight | Max. permissible finger length | Repeat accuracy
 | [mm] | [N] | [N] | [kg] | [kg] | [mm] | [mm]
160 | 8 .. 16 | 2200 .. 6200 | 2375 .. 6500 | 11 .. 22.5 | 3 .. 3.8 | 215 .. 245 | 0.01
240 | 17 .. 30 | 5000 .. 11400 | 5300 .. 12300 | 25 .. 43.5 | 9 .. 12 | 260 .. 355 | 0.01
300 | 20 .. 35 | 6600 .. 15600 | 6800 .. 16000 | 33 .. 59 | 13.9 .. 17.2 | 250 .. 350 | 0.05
380 | 26 .. 45 | 10300 .. 26100 | 10800 .. 27000 | 51.5 .. 97.5 | 28 .. 37.5 | 300 .. 400 | 0.05

## Slide 8
Technical data
Technical data overview |  |  |  |  |  | 
Size | Stroke per jaw | Closing force | Opening force | Recommended workpiece weight | Weight | Max. permissible finger length
 | [mm] | [N] | [N] | [kg] | [kg] | [mm]
40 | 2.5 | 180 .. 235 | 200 .. 260 | 0.9 | 0.08 .. 0.12 | 60 .. 65
50 | 2 .. 4 | 220 .. 490 | 235 .. 520 | 1.1 .. 1.9 | 0.17 .. 0.24 | 70 .. 80
64 | 3 .. 6 | 350 .. 920 | 375 .. 1050 | 1.75 .. 3.6 | 0.27 .. 0.42 | 85 .. 100
80 | 4 .. 8 | 550 .. 1500 | 610 .. 1600 | 2.75 .. 5.5 | 0.51 .. 0.7 | 105 .. 125
100 | 5 .. 10 | 870 .. 2200 | 930 .. 2400 | 4.35 .. 8.75 | 0.9 .. 1.22 | 130 .. 160
125 | 6 .. 13 | 1400 .. 4200 | 1520 .. 4450 | 7 .. 15 | 1.4 .. 2.1 | 170 .. 200
200 | 14 .. 25 | 3800 .. 8750 | 4050 .. 9350 | 19 .. 32.5 | 5.4 .. 7.6 | 220 .. 310

## Slide 9
PGN-plus-P 160 & 240
The strength of the usual aluminium lids is not sufficient
In the endurance test this led to several broken lids and thus to a failure of the gripper
For this reason, the covers of sizes 160 and 240 are made of steel, burnished and dyed black
The corrosion protection of the basic version is not affected by this
Weight [kg] | 160-1 | 240-1
PGN-plus | 2.6 | 8.5
PGN-plus-P | 3 | 9
ZIMMER GPP5000 | 2.9 | 9.2
 SCHUNK does not release grippers which do not reach the specified technical data!

## Slide 10
PGN-plus-P 300 & 380
Multi-tooth guidance with lubricant pockets
Higher gripping force
Screw connection with fits for customized attachment
Improved switching-cam concept
New concept of the dust-tight version
Dynamic bevel
Notes: Schmierstofftaschen in der Vielzahnführung (keine neue Vielzahnführung)
  Höhere Lebensdauer
Höhere Greifkraft
  Bei der Vermessung der Baugrößen 300 und 380 erzielten die Greifer deutlich höhere Greifkräfte, als aktuell beim PGN-plus angegeben. Die Katalogangaben des PGN-plus-P 300 und 380 orientieren sich an den gemessen Werten und sind folglich höher als beim PGN-plus.
Befestigungsmöglichkeiten unter dem Abdeckblech
  Zur Montage kundenspezifischer Anbauten
Optimiertes Schaltnockenkonzept mit Einstell- und Klemmspindel
  Einfaches Einstellen der Schaltnocken
Neues SD-Konzept
  Optimierte Dichtwirkung und einfachere Montage
Dynamische Phase
  Hoher Wiedererkennungswert der PGN-plus-P Baureihe

## Slide 11
PDF-Overview
in STB
Gripping force

## Slide 12
Dust-tight version -SD
 The dust cover mounting kit “SAD PGN-plus-P” can be purchase separately as well, so the customer can retrofit the gripper by himself.

## Slide 13
Sales release accesories

## Slide 14
Gripper for small components
The most affordable SCHUNK gripper for small components for handling and assembly
6 sizes for workpiece weights of up to 1.85 kg
Easily built up 2-finger parallel gripper with good price-performance ratio

## Slide 15
Easy. Economical. Cost-effective.
Variety of sizes
Cost-efficient basic gripper with basic functionalities
Low-cost sensor system

## Slide 16
Principle of function
Drive
3
Housing
2
Base Jaw
1
Guidance
4
Kinematics
5
Functional description
The base jaws are actuated with compressed air by the fixed piston and in turn the gripper is opened or closed. The kinematics synchronizes the movement of the base jaws.
Sensor system
6

## Slide 17
Advantages – Your benefits
Cost-efficient basic gripper with basic functionalities specially suitable for simple applications in small components handling
Series with six unit sizes for a broad range of applications from small to mid-sized workpieces
Technically and financially compatible sensor system for a simple, functional gripping system completely from a single source
Housing and guidance made of high-strength aluminum therefore exposed to high physical loads and is weight optimized

## Slide 18
Technical data
Technical data overview |  |  |  |  |  |  | 
Size | Stroke per jaw | Closing force | Opening force | Recommended workpiece weight | Weight | Max. permissible finger length | Repeat accuracy
 | [mm] | [N] | [N] | [kg] | [kg] | [mm] | [mm]
25 | 2.5 | 16 | 16 | 0.08 | 0.05 | 30 | 0.02
40 | 4 | 50 | 50 | 0.25 | 0.14 | 35 | 0.02
75 | 7.5 | 110 | 110 | 0.55 | 0.21 | 35 | 0.02
100 | 10 | 170 | 170 | 0.85 | 0.34 | 40 | 0.02
120 | 12 | 240 | 240 | 1.2 | 0.54 | 45 | 0.02
150 | 15 | 370 | 370 | 1.85 | 0.94 | 60 | 0.02

## Slide 19
Strategic objective
Replacement product for RH grippers
Occupy the SCHUNK basic segment for small part grippers / product segmentation
Support the SCHUNK brand and the premium grippers MPG-plus
 Inexpensive grippers especially for Asian market

## Slide 20
Replacement product for RH
025 040 075 100 120 150
RH
MPC
MPC series is comparable to these RH grippers in stroke per jaw and gripping force, but not direct compatible in connection and outside dimensions.

## Slide 21
Segmentation small part grippers
MPG
Price
100 %
~ 50 %
Performance
MPC
MPG-plus
Target
The right
price/performance ratio
for every application worldwide

## Slide 22
Chart: Gripping force
| MPG-plus 20 | MPC 025 | MPG-plus 25 | MPC 040 | MPG-plus 32 | MPG-plus 40 | MPC 075 | MPG-plus 50 | MPC 100 | MPG-plus 64 | MPC 120 | MPC 150 | 2 | 2,5 | 3 | 4 | 6 | 7,5 | 8 | 10 | 12 | 15
Ergebnis | 34 | 16 | 38 | 50 | 80 | 135 | 110 | 215 | 170 | 300 | 240 | 370
Segmentation small part grippers
6 sizes = 6 number of materials (no variants)
Warranty: 12 months or 7 million cycles
Scope of delivery: gripper, manual, Accessory Bag (6 Dowel pins)
Air connection A+B (Open and Close) – no direct air connection
Maintenance of gripping force possible via SDV-P – no version with spring force
New, low-priced magnetic switches – not SCHUNK MMS
Chart: German list price
| MPG-plus 20 | MPC 025 | MPG-plus 25 | MPC 040 | MPG-plus 32 | MPG-plus 40 | MPC 075 | MPG-plus 50 | MPC 100 | MPG-plus 64 | MPC 120 | MPC 150 | 2 | 2,5 | 3 | 4 | 6 | 7,5 | 8 | 10 | 12 | 15
Ergebnis | 225 | 100 | 240 | 120 | 250 | 260 | 145 | 299 | 165 | 362 | 190 | 220

## Slide 23
Support MPG-plus
Comparable with the successful story of PGN-plus and JGP, the MPC gripper is supposed to support the MPG-plus and not to replace it.
Sales target should always be to convince the customer of the superior MPG-plus gripper.
If a sales argumentation for MPG-plus fails due to the price, MPC can be offered proactive.
In competitor situations with cost-sensitive applications, MPC grippers can be successful.

## Slide 24
Main sales market Asia
MPC: Percentage distribution on regions
Especially in Asia, the MPC grippers are supposed to achieve high quantities.
For example in electronic mass production, some assembly systems are bulid up for only 1 year lifetime. In such assembly systems, grippers are mainly chosen by the price.
MPC grippers are manufactured and assembled in South Korea.
For Germany and other countries, MPC offers the opportunity to penetrate into new applications, e.g. plastic injection moulding.
Chart: 
| Deutschland | Rest of Europe | Asien/Pazifik | Americas | Weitere Regionen
 | 0.15 | 0.15 | 0.5 | 0.18 | 0.02
Notes: Zum Vergleich: MPG hat einen Deutschland-Anteil von > 50%

## Slide 25
Availability & Price
Size | Price | Availability
025 | 100 € | available
050 | 120 € | available
075 | 145 € | available
100 | 165 € | available
120 | 190 € | available
150 | 220 € | available

## Slide 26
Sensors
Less expensive sensors for MPC
Magnetic switches for C-slot
Different technologies and switching types available (Reed or PNP/NPN)
Versions with 30cm cable and M8-plug or 2 m cable and open wires
List prices sensors |  | 
Name | Version | Price (Plug/Cable)
J02N/J02P | NPN / PNP | 28 € / 23 €
J02R | Reed | 20 € / 15 €
Technical differences to existing products:
No high-flexible cable, only for permanently installation (no cable-chain)
Molded sensor housing, no high mechanic load possible

## Slide 27
Accessories
In case of pressure failure, venting of the module will be prevented by the pressure maintenance valve. Therefore a temporary force or position maintenance can be implemented via different actuators. This is particularly suitable for grippers which cannot be equipped with a mechanical gripping force maintenance.

## Slide 28
Principle of function
Thread for pneumatic connection
3
Mounting option
2
Housing
1
Piston
4
check valve
5
Functional description
Two check valves are parallely switches, and automatically open and ventilate the return flow direction on alternating sides. In the event of a pressure failure, the supply lines close the return flow valves and prevent a loss in pressure.

## Slide 29
Advantages – Your benefits
Prevention of pressure drop in the pneumatic actuator in the case of pressure failure of the entire system for greater operational safety when pneumatic components are used
well-proven in industrial automation
Robust design for long term reliable applications
Universally applicable can be combined with almost any pneumatic actuator
Variant with manual venting for greater operating comfort
Variant for direct mounting on parallel grippers as a result, space-saving and no additional fastening is necessary

## Slide 30
Technical data
Technical data overview |  |  |  |  |  |  | 
Size | Manual quick ventilation | Rate of flow | Flow rate, hose Ø 6mm | Flow rate, hose Ø 8mm | Flow rate, hose Ø 10mm | Valve switching time | Weight
 |  | [l/min] | [l/min] | [l/min] | [l/min] | [ms] | [kg]
4 | 0 .. 1 |  | 200 | 250 | 340 | 15 | 0.1
7 | 0 .. 1 |  | 350 | 500 | 600 | 10 | 0.2
10 | 1 |  | 400 | 1000 | 1400 | 10 | 0.4
64 | 1 | 150 |  |  |  | 10 | 0.12
80 | 1 | 150 |  |  |  | 20 | 0.16
100 | 1 | 180 |  |  |  | 20 | 0.23
125 | 1 | 200 |  |  |  | 30 | 0.33

## Slide 31
Pressure maintenance valve SDV-P
Standard:
Hosing of the grippers with pressure maintenance valves SDV-P
size 04, 07, 10
Direct mounting:
Variant SDV-P-E-P for direct mounting on SCHUNK parallel gripper size 64, 80, 100, 125
Pressure maintenance valve SDV-P

## Slide 32
Catalog
Website
Selection of the appropriate SDV-P
Optional calculation
If the assignment recommended by SCHUNK is not possible for the customer (e.g. because hose-Ø 6 mm is prescribed), the catalogue specifications can be used to calculate individually which SDV-P is suitable.
for PGN-plus-P 100-1
for PGN-plus-P 100-1-AS

## Slide 33
Improved manual ventilation
SDV-P …-E-P Pressure maintenance valve for direct mounting
SDV-P …-E Pressure maintenance valve SDV-P
old:
new:
old:
new: (not for 64)

## Slide 34
Inscription SDV-P E-P for direct mounting
wrong
right
This issue is fixed,
see also the news entry in the Sales Tool Box

## Slide 35
Sealed Gripper
The most proven sealed gripper on the market for wet and dirt-intensive environments.
Protection class IP 67
Despite the high moment load of the base jaws, this sealed 2-finger parallel gripper meets the IP67 requirements, and does not permit the ingress of any substances from the working environment into the interior of the unit

## Slide 36
Principle of function
Lip seal
3
External round base jaw
2
Inner base jaw with multi-tooth guidance
1
Oval piston with rod and wedge-hook
4
Centering and mounting possibilities
5
Functional description
The piston is moved up and down by compressed air.
The angled active surfaces of the wedge-hook produce a synchronized, parallel jaw motion.

## Slide 37
Advantages – Your benefits
Robust interior multi-tooth guidance for the precise handling of different workpieces
Lip seal at the outside round guidance for permanent, secure gripper sealing
High maximum moments possible suitable for using long gripper fingers
Sealed 2-Finger Parallel Gripper complies to IP67 requirements despite a high moment load
Drive concept oval piston for maximum gripping forces
Mounting from two sides in three screw directions for universal and flexible gripper assembly
Air supply via hose-free direct connection or screw connections for flexible pressure supply in all automated systems
Compact dimensions for minimal interfering contours in handling

## Slide 38
Technical data
Technical data overview |  |  |  |  |  | 
Size | Stroke per jaw | Closing force | Opening force | Recommended workpiece weight | Weight | Max. permissible finger length
 | [mm] | [N] | [N] | [kg] | [kg] | [mm]
40 | 2.5 | 110 .. 145 | 120 .. 165 | 0.55 | 0.12 .. 0.14 | 40
50 | 2 .. 4 | 125 .. 470 | 130 .. 505 | 0.6 .. 2.3 | 0.25 .. 0.34 | 30 .. 50
64 | 3 .. 6 | 225 .. 850 | 240 .. 915 | 1.1 .. 4.2 | 0.39 .. 0.55 | 40 .. 64
80 | 4 .. 8 | 375 .. 1395 | 415 .. 1550 | 1.8 .. 6.9 | 0.68 .. 0.95 | 50 .. 80
100 | 5 .. 10 | 625 .. 2340 | 685 .. 2560 | 3.1 .. 11.7 | 1.1 .. 1.61 | 64 .. 100
125 | 6 .. 13 | 1025 .. 3835 | 1110 .. 4140 | 5.1 .. 19.1 | 1.9 .. 2.9 | 64 .. 125
160 | 8 .. 16 | 1560 .. 5470 | 1680 .. 5920 | 7.8 .. 27.3 | 3.65 .. 8 | 80 .. 160
200 | 14 .. 25 | 2565 .. 5940 | 2730 .. 6490 | 12.8 .. 22.1 | 7.3 .. 9.5 | 125 .. 200
240 | 17 .. 30 | 3780 .. 7500 | 4000 .. 7835 | 18.9 .. 29.25 | 11.5 .. 14.6 | 150 .. 240
300 | 20 .. 35 | 5400 .. 11250 | 5635 .. 11700 | 27 .. 46.35 | 19.6 .. 23.6 | 150 .. 300
380 | 45 | 8140 .. 11240 | 8460 .. 11430 | 40.7 | 42 .. 52 | 300 .. 380

## Slide 39
Seal optimization
BG 40 - 200
BG 240 - 300
BG 40 - 380
New Version
Only available with size 380 for lubrication
Old Version
Rubber cork seal
Rubber cork seal
Flat seal
Flat sealing ring
Form seal
Filling piece
Filling piece
O-Ring

## Slide 40
Seal optimization
Adjustments:
100% exchange compatible: Same dimensions and connections
The seal kit is not compatible (improved seal)
  No retrofitting possible
  There‘s a new Mat. No. for the grippers and the seal kit
Prices remain unchanged
NEW: High temperature version DPG-plus…-V available  for use up to 130 °C
Catalogue data sheets are updated and show the new Mat. No.
Comparison New/Old Mat. No. in Sales Tool Box
Release status New Version |  | 
Size | Release status DPG-plus | Release status DPZ-plus
40 | released | In Preparation
50 | released | In Preparation
64 | released | In Preparation
80 | released | In Preparation
100 | released | In Preparation
125 | released | In Preparation
160 | released | In Preparation
200 | 01.04.2019 | In Preparation
240 | 01.04.2019 | In Preparation
300 | 01.04.2019 | In Preparation
380 | released | In Preparation
The old version of DPG-plus is no longer produced. But the existing stock will be sold off.

## Slide 41
Pneumatic connection
DPG-plus/DPZ-plus must be operated with a third pneumatic hose (ventilation or air purge connection)
A warning notice is intended to make the operator aware of this. Details can be found in the operating manual for the product.
Nevertheless, defective grippers occur because the warning notices are ignored and grippers are operated without a third hose.
Dirt can be sucked into the gripper via open air purge connection and lead to failure.  The customer is dissatisfied, although he is responsible for the failure himself.
Air purge connection

## Slide 42
Coming soon…
Delivery condition with sinter filter screwed into the purged air connection:  Prevents the suction of dirt particles (>0,12 mm) when the gripper is operated without a 3rd pneumatic hose.
The gripper with sinter filter then does not comply with protection class IP 67!  For IP 67, an additional hose (ventilation or air purge connection) must still be connected.
Air purge connection
Sinter filter at air purge connection

## Slide 43
Available communication interfaces
Forecast of market shares of industrial networks (source: HMS)
  A large variety of interfaces, technologies and protocols exists to control actors and sensors on field level.
  The customer chooses a PLC, which implicitely defines the communication interface.

## Slide 44
Interface Strategy Customer chooses communication interface
Forecast of market shares of industrial networks (source: HMS)
  Focus on future-oriented techology:
  Industrial Ethernet:
      PROFINET,
      EtherNet/IP und
      EtherCAT
Supported natively
Supported through IO-Link
  IO-Link:
      Additional interface technologies through compatible IO-Link Master
  Digital I/O
      Supports easiest control
      Direct pneumatic replacement

## Slide 45
SIEMENS
PLC / Motor control / periphery
SCHUNK
System components
SIMATIC S7-1500
SITOP PSU 8600
24 V power supply
PROFINet
PROFINet
PROFINet
Digital I/O
SIMATIC ET 200 AL
Digital I/O
Industrial Ethernet
System-design with SCHUNK products
IO-Link class B
SIMATIC
ET 200 eco PN IO-Link Master
IO-LINK
IO-Link class A

## Slide 46
Basic functionality
 | Digital I/O | IO-Link | Industrial Ethernet
Gripping and releasing For gripping and releasing workpieces | ü | ü | ü
Gripping force adjustment to preserve sensitive workpieces | ü (manual) |  | 
Positioning for optimizing cycle time by pre-positioning |  |  | 
Fine–tuning motor control to solve complex gripping tasks |  |  | 

## Slide 47
Basic functionality
 | Digital I/O | IO-Link | Industrial Ethernet
Gripping and releasing For gripping and releasing workpieces | ü | ü | ü
Gripping force adjustment to preserve sensitive workpieces | ü (manual) | ü | ü
Positioning for optimizing cycle time by pre-positioning |  |  | 
Fine–tuning motor control to solve complex gripping tasks |  |  | 

## Slide 48
Basic functionality
 | Digital I/O | IO-Link | Industrial Ethernet
Gripping and releasing For gripping and releasing workpieces | ü | ü | ü
Gripping force adjustment to preserve sensitive workpieces | ü (manual) | ü | ü
Positioning for optimizing cycle time by pre-positioning | - | ü | ü
Fine–tuning motor control to solve complex gripping tasks |  |  | 

## Slide 49
Basic functionality
 | Digital I/O | IO-Link | Industrial Ethernet
Gripping and releasing For gripping and releasing workpieces | ü | ü | ü
Gripping force adjustment to preserve sensitive workpieces | ü (manual) | ü | ü
Positioning for optimizing cycle time by pre-positioning | - | ü | ü
Fine–tuning motor control to solve complex gripping tasks | - | - | ü

## Slide 50
Integrated sensor- und diagnostic functions
 | Digital I/O | IO-Link | Industrial Ethernet
Position feedback e.g. open, closed, workpiece gripped | ü (external) |  | 
Continuous position feedback for workpiece identification and verification | - |  | 
Diagnosic und maintenance information e.g. cycle counter, input power, temperature, etc. | - |  | 
Device identification e.g. material number, SN, HW and FW Version | - |  | 
Additional Sensor data e.g. Jaw velocity, motorcurrent, etc. | - |  | 

## Slide 51
Integrated sensor- und diagnostic functions
 | Digital I/O | IO-Link | Industrial Ethernet
Position feedback e.g. open, closed, workpiece gripped | ü (external) | ü | 
Continuous position feedback for workpiece identification and verification | - | ü | 
Diagnosic und maintenance information e.g. cycle counter, input power, temperature, etc. | - | ü | 
Device identification e.g. material number, SN, HW and FW Version | - | ü | 
Additional Sensor data e.g. Jaw velocity, motorcurrent, etc. | - | - | 

## Slide 52
Integrated sensor- und diagnostic functions
 | Digital I/O | IO-Link | Industrial Ethernet
Position feedback e.g. open, closed, workpiece gripped | ü (external) | ü | ü
Continuous position feedback for workpiece identification and verification | - | ü | ü
Diagnosic und maintenance information e.g. cycle counter, input power, temperature, etc. | - | ü | ü
Device identification e.g. material number, SN, HW and FW Version | - | ü | ü
Additional Sensor data e.g. Jaw velocity, motorcurrent, etc. | - | - | ü

## Slide 53
Interfaces and integration
 | Digital I/O | IO-Link | Industrial Ethernet
PLC connection without mediating hardware For decentralized system control | - (I/O Modul) | - (IO-Link Master) | ü

## Slide 54
Interfaces and integration
 | Digital I/O | IO-Link | Industrial Ethernet
PLC connection without mediating hardware For decentralized system control | - (I/O Modul) | - (IO-Link Master) | ü
Real-time capability for time sensitive applications | ü | - | (ü)

## Slide 55
Interfaces and integration
 | Digital I/O | IO-Link | Industrial Ethernet
PLC connection without mediating hardware For decentralized system control | - (I/O Modul) | - (IO-Link Master) | ü
Real-time capability for time sensitive applications | ü | - | (ü)
Webserver for easy and comfortable integration | - | - | ü

## Slide 56
Interfaces and integration
 | Digital I/O | IO-Link | Industrial Ethernet
PLC connection without mediating hardware For decentralized system control | - (I/O Modul) | - (IO-Link Master) | ü
Real-time capability for time sensitive applications | ü | - | (ü)
Webserver for easy and comfortable integration | - | - | ü
Transmission rate and bandwidth for smart factory and cloud applications | - | + | ++++

## Slide 57
Gripper for small components
The electric gripper with the easiest commissioning and most reliable maintenance of gripping force capability on the market
Over 90% of gripping force maintained in the event of a voltage drop
Servo-electric 2-finger parallel gripper with sensitive gripping force control and long stroke

## Slide 58
Intelligent. Sensitive. Reliable.
Long stroke and finely adjustable gripping force
Control via 24 V power supply
Redesigned maintenance of gripping force
Certified PROFINET interface
Integrated web server

## Slide 59
Principle of function
Drive
3
Encoder
2
Integrated electronics
1
Brake
4
Kinematics
5
Functional description
The brushless servomotor drives the toothed belt drive via the bevel gear. The base jaws mounted on the profiled rail guides are connected to the toothed belt. The rotary movement is transferred into a linear movement of the base jaws via the gear and the toothed belt.
Finger connection
6
Electrical connection
7

## Slide 60
Advantages – Your benefits
Gripping force control for the delicate gripping of sensitive workpieces
Long and freely programmable stroke for flexible workpiece handling
Fully integrated control and power electronics for creating a decentralized control system
Almost complete maintenance of gripping force for a high process reliability
Integrated web server for parameterization, commissioning and diagnostics with any standard web browser
Connectors in industrial standard for easy electrical connection

## Slide 61
Technical data
Technical data overview |  |  |  |  | 
Size | Stroke per jaw | Min. gripping force | Max. gripping force | Recommended workpiece weight | Weight
 | [mm] | [N] | [N] | [kg] | [kg]
80 | 57.5 | 5 | 100 | 0.5 | 1.6

## Slide 62
Universal gripper
The first simple electric gripper with reliable multi-tooth guidance.
Multi-tooth guidance, digital actuation and 24 V drive with permanent lubrication.
Universal electric 2-finger parallel gripper with permanent lubrication, high gripping force, and a high maximum moment due to the use of a multi-tooth guidance.

## Slide 63
Reliable. Robust. Flexible.
New variant with IO-link interface
Four-step adjustable gripping force
Lifelong maintenance-free

## Slide 64
Principle of function
Sensor system
3
Base Jaw
2
Multi-tooth guidance
1
Housing
4
Centering and mounting possibilities
5
Functional description
The brushless servomotor forces the wedge-hook up or down via a ball-and-screw spindle drive.
Through its angled active surfaces, the wedge-hook transforms this motion into the horizontal, synchronous movement of the base jaws.
Wedge-hook design
6
Spindle nut
7

## Slide 65
Advantages – Your benefits
Robust multi-tooth guidance for precise handling
High maximum moments possible suitable for using long gripper fingers
Lubricant pockets in the mult-tooth guidance ensure process reliability and extended maintenance intervals
Brushless DC servomotor for almost wear-free use and a long service life
Control via digital I/O for easy commissioning and rapid integration into existing systems
Four-step adjustable gripping force for simple adaption to sensitive workpieces
Mounting from two sides in three screw directions for universal and flexible gripper assembly
Integrated sensor system and comprehensive sensor accessory program for versatile querying possibilities and stroke position monitoring
Control via IO-Link enables the prepositioning of the gripper finger and the evaluation of the gripper condition

## Slide 66
Technical data
Technical data overview |  |  |  |  |  | 
Size | Stroke per jaw | Min. gripping force | Max. gripping force | Recommended workpiece weight | Max. permissible finger length | Weight
 | [mm] | [N] | [N] | [kg] | [mm] | [kg]
80 | 8 | 110 | 530 | 2.85 | 125 | 1.01 .. 1.08
100 | 10 | 200 | 810 | 4.05 | 160 | 1.73 .. 1.85

## Slide 67
Gripper for small components
The electric gripper for small components with the highest power density on the market.
Up to 300 N gripping force at a weight of 0.8 kg
Electric 2-finger parallel gripper with smooth-running base jaws guided on roller bearings

## Slide 68
High Performance Density. Fast. Compact.
New variant with IO-link interface
Flexible gripping force adjustment software-controlled
Variable position adjustment for pre-positioning the gripper fingers
Position detection over the entire range of stroke due to integrated sensor system
Maintenance and diagnostics reporting via IO-link interface

## Slide 69
Principle of function
Gear
3
Cross roller guidance
2
Base Jaw
1
Drive
4
Control electronics
5
Functional description
The brushless servomotor drives the base jaw via the gear mechanism.
The jaw stroke is synchronized by means of rack and pinion kinematics.

## Slide 70
Advantages – Your benefits
Highest performance density for the use of smaller grippers sizes
Control via digital I/O for easy commissioning and rapid integration into existing systems
Two to four stage adjustable gripping force for simple adaption to sensitive workpieces
Backlash-free, pre-loaded cross roller guide for precise gripping with nearly constant force for all permissible finger lengths
Very high maximum cycles per minute for highest productivity
Compact dimensions for minimal interfering contours in the application
Proven a thousand times MPG-plus basis for equal gripping forces and strokes with identically high efficiency
Brushless DC servomotor for almost wear-free use and a long service life
Control via IO-Link enables the prepositioning of the gripper finger and the evaluation of the gripper condition

## Slide 71
Technical data
Technical data overview |  |  |  |  |  | 
Size | Stroke per jaw | Min. gripping force | Max. gripping force | Recommended workpiece weight | Max. permissible finger length | Weight
 | [mm] | [N] | [N] | [kg] | [mm] | [kg]
25 | 3 | 12 .. 20 | 12 .. 40 | 0.07 .. 0.2 | 32 | 0.11 .. 0.12
40 | 6 | 30 .. 35 | 30 .. 140 | 0.15 .. 0.7 | 50 | 0.3 .. 0.34
50 | 8 | 54 | 215 | 1.05 | 64 | 0.51
64 | 10 | 75 | 300 | 1.25 | 80 | 0.8

## Slide 72
Sensors
A magnetic switch is used for monitoring the status of automation components.They detect the magnets fixed inside the component without contact. In addition to further process data, the sensor outputs the process of the magnetic field via the IO-Link interface.

## Slide 73
Advantages – Your benefits
Control via IO-Link for the evaluation of data such as temperature, evaluation quality or the sensor identification
Integrated electronics leads to a compact design and enables the use of cables with standard plug connectors
Suitable for narrow installation spaces due to teaching via IO-Link interface
Version with LED display is used to indicate the status of the IO-Link connection
C-slot sensor for space-saving, easy, and fast assembly on the product

## Slide 74
Technical data
Technical data overview |  |  |  |  | 
Description | Measuring principle | Cable length | Communication interface | Teach function | Cable connector/cable end
 |  | [cm] |  |  | 
MMS 22-IOL-M08 | magnetic | 30 | IO-Link | 1 | M8, 4-pin Male Connector
MMS 22-IOL-M12 | magnetic | 30 | IO-Link | 1 | M12 connector, 4-pin

## Slide 75
Pricing
Electric gripper pricing |  |  | 
Product | Interface | Sales release | Price
EGI 80 | PROFINET | Q3 / 2019 | € 3000 - € 3500
EGI 40 & 80 | PROFINET & Ethernet/IP | Q4 / 2019 | € 2500 - € 3500
PGN-plus-E all sizes | Digital I/O & IO-Link | Released | € 1565 - € 2355
EGP 40 | IO-Link | Released | € 878
EGP 50 & 64 | IO-Link | Q3 / 2019 | € 1009 - € 1220
MMS | IO-Link | Released | € 95
EMH all sizes | Digital I/O | Q1 / 2019 | € 1170 - € 2290

## Slide 76
Magnetic gripper
The first compact electropermanent magnetic gripper with integrated electronics.
3:1 ratio of workpiece weight to dead weight
Electric permanent magnetic gripper for energy-efficient handling of ferromagnetic workpieces with integrated electronics and feedback functions.

## Slide 77
Compact. Strong. Fast.
Integrated electronics reduces the interfering contour. No external controllers required.
Response on magnetization condition and workpiece presence
Control via 24 V power supply
Short cycle time! Magnetization in just 300 ms for more gripping cycles in less time.

## Slide 78
Principle of function
Control electronics
3
Connection plug
2
Connecting plug for PLC
1
LED display
4
Copper coil
5
Functional description
The function of the magnetic gripper bases on the combination of AlNiCo and neodymium magnets. The magnetic flux of the AlNiCo magnets passes the neodymium magnet in the deactivated state, and closes the magnetic circuit over the gripper base body made of steel. To activate the system, an electric current pulse is conducted through the coil, which reverses the polarity of the AlNiCo magnets accordingly.
Polarity reversible AlNiCo-magnet
6
Non-pole reversing neodymium permanent magnets
7

## Slide 79
Advantages – Your benefits
High holding forces at lowest space for reliable part handling in compact machines
Low weight for high dynamics in challenging applications
Reliable holding force maintenance to ensure process reliable operation even in scenarios with emergency stop
The gripping force can be adjusted in four stages ensures gripping of various workpieces
Control via 24 V power supply saves energy and simplifies the connection and the wiring
Workpiece accessibility from five sides free from interfering contours by unnecessary gripper fingers
Integrated electronics Compact design, as no additional controller is required
Response on magnetization condition and workpiece presence saves time and simplifies the programming

## Slide 80
Technical data
Technical data overview |  |  | 
Size | Weight | Payload for horizontal magnet surface | Total force
 | [kg] | [kg] | [daN]
36 | 1 | 8.5 | 53
45 | 1.5 | 22.5 | 136
84 | 6.5 | 89.5 | 537
114 | 8 | 175.5 | 1055

## Slide 81
Technical data
Commercial data overview |  |  |  | 
Size | Technical release | Sales release | Price (EGM unit) | Availability
 |  |  | [€] | 
36 | 01/2019 | End of 03/2019 | 1.170,- (3.360,-) | End of 04/2019
45 | 01/2019 | End of 03/2019 | 1.340,- (3.360,-) | End of 04/2019
84 | 01/2019 | End of 03/2019 | 2.130,- (3.616,-) | End of 04/2019
114 | 01/2019 | End of 03/2019 | 2.290,- (4.870,-) | End of 04/2019

## Slide 82
Project status
Sales releases
Available variants
Accessories
Sizes 25 & 40 released for sales
Sizes 50 & 64 released for sales since week 12
Five variants for three cobots available as standard products
Fourteen variants for nine cobots as certified semi-standard products available
Fingers with single our doubled stroke available for every size

## Slide 83
Collaborating long-stroke gripper
Electric 2-finger parallel gripper certified for collaborative operation.
The world’s first certified industrial long-stroke gripper for collaborative operation.
Secure gripping in HRC-applications with up to 450 N of gripping force.
Communication via ethernet-based bus systems and with 24V power supply.

## Slide 84
Chart: Greifkraft [N]
| 30
Weiss CRG 30-50 | 50
Weiss CRG 200-85 | 85
Robotiq Hand-E | 50
Robotiq 2F-85 | 85
Robotiq 2F-140 | 140
OnRobot RG2 | 110
OnRobot RG6 | 160
Zimmer HRC-01 | 120
Zimmer HRC-03 | 20
Zimmer HRC-04 | 12
Dahl DAG-M | 60
Co-act EGP-C 25 | 6
Co-act portfolio
Complete stroke [mm]
Gripping force [N]

## Slide 85
Chart: Greifkraft [N]
| 30
Weiss CRG 30-50 | 50
Weiss CRG 200-85 | 85
Robotiq Hand-E | 50
Robotiq 2F-85 | 85
Robotiq 2F-140 | 140
OnRobot RG2 | 110
OnRobot RG6 | 160
Zimmer HRC-01 | 120
Zimmer HRC-03 | 20
Zimmer HRC-04 | 12
Dahl DAG-M | 60
Co-act EGP-C 25 | 6
Co-act portfolio vs. competitor
Complete stroke [mm]
Gripping force [N]

## Slide 86
Principle of function
LED strip light
3
Collision protection
2
Force-measuring jaws
1
Flange
4
Stroke measuring system
5
The servomotor drives the base jaws with a gear mechanism and a rack-and-pinion-principle.
The stroke is sensed by a doubled encoder system at the end of the servomotor
A force measurement is integrated in each base jaw. The electronic for power and logic is completely integrated in the gripper
Drive with gear
6
Electronics
7
Functional description

## Slide 87
I can grip safe!
Functional safe - Certification under preparation!
Gripping force of 450N is over the limits of ISO/TS 15066
Risk minimizing measures necessary
Co-act EGL-C is equipped with safety function „Safe gripping“
Safe gripping - Combination of several safety functions
Safe limited speed
Safe limited force / Safe limited motor torque
Safe force monitoring
Safe temperature monitoring
Safe brake control
 Redundant sensors and electronics necessary!

## Slide 88
EXKURS - Biomechanical limits
Source: ISO/TS 15066:2016(E)

## Slide 89
The "gripping force" specification in the catalog refers to the arithmetic sum of the forces acting on each jaw individually at distance P (see illustration). For evaluation of the biomechanical limit values in accordance with ISO/TS 15066, only the gripping force acting on each gripper jaw must be used. Furthermore, the information in the operating manual is referred to.
Co-act EGP-C gripper
Gripper jaws (customized)
Gripping force applied to each gripper jaw
Workpiece
EXKURS - Gripping force and HRC
1
2
3
4

## Slide 90
I can grip safe!
Gripping force not reduced!
Gripping force safely reduced!
Distance between workpiece and fingers smaller than 4 mm
Gripping force higher 140N
Distance between workpiece and fingers bigger than 4 mm
Gripping force under 140N

## Slide 91
YouTube - #HMI2019
YouTube - Next Robotics - Hannover Messe 2019 Weltneuheit! Flexibler Cobot-Greifer von Schunk

## Slide 92
Advantages – Your benefits
Certified gripping unit saves effort for safety assessment of the application
Safe gripping for workpiece weights of up to 2.25 kg guaranteed by integrated force and distance measurement
Pre-assembled gripping unit with robot interface for a easy and fast integration
Integrated status display to the visibility of the application state at the operator’s eye level
Actuation via various bus systems for easy commissioning and rapid integration into existing systems
Our advantages compared to our competitors!
Gripper will be certified- We face the challenge!
Gripping force of max. 450N- We can handle heavy things!
Gripping force maintenance up to 450N - We grip safe in every situation!
Integration of three bus systems- We are more communicative!
Price 5.000€ - 5.500€
Available Q4/2019

## Slide 93
Linear axis
There is no other electric linear module on the market that is as user-friendly to configure
Ready for takeoff in only 2 work steps!
Electric linear module with direct drive and integrated controller, scope-free guided using pre-loaded roller guide

## Slide 94
Easy. Fast. Reliable.
New variant without auto-learn function for pressing and jointing applications
Manual speed configuration using rotary switches
Also suitable for use in cam-controlled systems
Control via digital I/O
Standardized mounting bores

## Slide 95
Principle of function
Control electronics
3
Drive
2
Roller guide
1
End position adjustability
4
Connection plug
5
Functional description
The electric drive consists of a primary part (motor coil) and a secondary part (permanent magnets). Inside the controller the phase and amplitude of the applied electric current are controlled. This sets the profile, which is fitted with magnets, in motion.
Mounting pattern
6

## Slide 96
Advantages – Your benefits
Control via digital I/O for easy commissioning and rapid integration into existing systems
10 independent extension and retraction speeds for high flexibility in cycle times
Linear direct drive for almost wear-free use and a long service life
Robust bearing guidance for high load capacities and end-position accuracy in all installation positions
Maintenance-free for high machine uptime and low operating costs
Compact dimensions for less interfering contours
Standardized mounting bores for numerous combinations with other components from the modular system

## Slide 97
Technical data
Technical data overview |  |  |  | 
Size | Max. stroke | Nominal force | Max. useful load (horizontal) | Max. useful load (vertical)
 | [mm] | [N] | [kg] | [kg]
25 | 30 .. 80 | 17 | 1 | 0.75
50 | 40 .. 100 | 45 | 3 | 2
100 | 80 .. 200 | 104 | 6 | 4

## Slide 98
Applications in assembly automation
Handling
Pick&Place
Providing
Measuring / Testing
Mating
Injecting
Moving
Cam-controlled applications
No or slight process forces
ELP M1 variant
(New as a standard version)
Process forces in movement direction
ELP with Auto-Learn
(Bearer of technology and standard solution for handling)
Application field

## Slide 99
Innovations
Mayr piston rod brake
Safety brake with fail-safe principle (closed-circuit principle)
Suitable for emergency stop brakes
Infinitely and free from play clamping of the piston rod
Two sizes (10 and 20)

## Slide 100
Availability & price
Designation | Price | Availability
ROBA-Linearstop-10 | 195 € | March 2019
ROBA-Linearstop-20 | 525 € | March 2019
ROBA-Brake-checker | 95 € | March 2019
AS-ELP025-HB-10 | 190 € | March 2019
AS-ELP050-HB-10 | 190 € | March 2019
AS-ELP100-HB-20 | 210 € | March 2019

## Slide 101
Future prospect
Remanent storage No new Auto-Learn after loosing actor- and logic voltage
Adjustment of the operation modes by the costumer Switching between operation mode Auto-learn and M1

## Slide 102
Universal swivel unit
No other electric swivel unit on the market is as easy to adjust
Ready for takeoff in only 2 work steps!
Electrical universal swivel unit with direct drive and integrated control for angles of rotation of 45°, 90° or 180°

## Slide 103
Easy. Fast. Reliable.
Control via digital I/O
Revolutionary auto-learn function with storable movement profile
Speed can be adjusted in 10 stages for both rotational directions
Rotational direct drive
Pinion and fastening identical to the pneumatic swivel unit SRM

## Slide 104
Principle of function
End position adjustment
3
Control electronics
2
Drive
1
Sensor system
4
Connection plug
5
Functional description
The electric drive consists of a primary part (motor coil) and a secondary part (permanent magnets). Inside the controller the phase and amplitude of the applied electric current are controlled. This causes the rotary table, which is fitted with magnets, to move.
Output flange
6

## Slide 105
Advantages – Your benefits
Control via digital I/O for easy commissioning and rapid integration into existing systems
Speed can be adjusted in 10 stages for both rotational directions for high flexibility in cycle times
Direct drive for almost wear-free use and a long service life
Large center bore for feed-through of cables and hoses with the same unit height
The swivel angle can be selected as either 45°, 90° or 180° complete flexibility in selecting the angle of rotation, application-specific angles possible on request
Maintenance-free for high machine uptime and low operating costs
Modular attachment to various options for individual adjustment to various cases of application

## Slide 106
Technical data
Technical data overview |  |  |  | 
Size | Torque | Swivel angle | Mass moment of inertia | Weight
 | [Nm] | [°] | [kgm²] | [kg]
25 | 2 | 45 .. 180 | 0.1 | 3.61

## Slide 107
Innovations
Remanent storage No new Auto-Learn after loosing actor- and logic voltage
Adjustment of the operation modes by the costumer Switching between operation mode Auto-learn and M1
Inductive proximity switches for end position monitoring and mountable with an attachment kit
45° swivel angle Now available as standard variant

## Slide 108
Availability & price
Size | Price | Availability
25 | 1.625 € | April 2019

## Slide 109
Linear axis
The most comprehensive modular system for linear axes.
22 profile sizes are selectable
Universal linear module with optional toothed belt or spindle drive and various guiding options

## Slide 110
Flexible. Modular. Compact.
New Beta ZSE variant as a cost-effective standard solution
Defined scope of functions and variants for fast delivery and competitive price
Proven Beta ZSS technology
Available in sizes 60, 80 and 110

## Slide 111
Principle of function
Covering tape made of plastic
3
Profiled rail guide
2
Aluminum profile
1
Toothed belt
4
Ball screw spindle
5
Functional description
The slide is driven by a toothed belt or a ball screw spindle and precisely guided by a (double) profiled rail guide. The cover band runs through the slide and covers the drive and guidance. The servomotor is usually connected to the profile via the drive shaft.

## Slide 112
Advantages – Your benefits
Adaptable drive motor for versatile approach and easy integration into existing control concepts
Optional belt or spindle driven for the optimum drive for your application
Various guide options for optimal adaption to your application
Cost-effective basic version with basic functions for simple and cost-effective applications
Compact dimensions for less interfering contours
Integrated cover tape for versatility and a long tool life
Fixing via T-nuts or slot nut possible for flexibility in the integration

## Slide 113
Technical data
Technical data overview |  |  | 
Size | Max. driving force | Max. stroke | Max. acceleration
 | [N] | [mm] | [m/s²]
40 | 500 .. 1000 | 850 .. 890 | 20 .. 30
50 | 700 .. 1000 | 860 .. 7710 | 20 .. 30
60 | 750 .. 4000 | 5220 .. 7670 | 20 .. 30
70 | 900 .. 2000 | 3725 .. 7640 | 20 .. 30
80 | 1000 .. 4000 | 5020 .. 7600 | 20 .. 40
100 | 1500 .. 4000 | 5260 .. 7720 | 20 .. 60
110 | 2000 .. 6000 | 5120 .. 7520 | 20 .. 60
120 | 4000 .. 12000 | 5120 .. 7520 | 20 .. 60
140 | 2500 .. 6000 | 4920 .. 7540 | 20 .. 60
165 | 10000 .. 18000 | 5010 .. 6920 | 20 .. 60
180 | 3500 .. 12000 | 5030 .. 5500 | 20 .. 60

## Slide 114
Initial situation
Strong competition in Low-Cost sector!!!
HIWIN HM-B 60/80/120
FESTO ELGA-TB-KF 70/80/120

## Slide 115
Flexible.Modular.Compact.
New Beta ZSE variant as a cost-effective standard solution
Defined scope of functions and variants for fast delivery and competitive price
Proven Beta ZSS technology
Available in sizes 60, 80 and 110
Beta ZSE

## Slide 116
Compared with Beta ZSS
Differences:
Just toothed belt with profiled rail guide
Without slide plate (available as accessories)
One drive bearing case
No cover strip possible
Advantages Beta ZSE:
Well known technology
standardized Units
Faster availability
20% cost efficient
Beta ZSE

## Slide 117
Availability
Size | Availability | Delivery time
60 | March 2019 | 4 weeks
80 | March 2019 | 4 weeks
110 | March 2019 | 4 weeks
Beta ZSE

## Slide 118
Quick change system
The only automatic self-locking change system without additional spring force on the market
Up to 10 integrated air feed-throughs on pneumatic grippers
Pneumatic tool changing system with patented locking system

## Slide 119
Modular. Robust. Flexible.
Simple direct connection with robot flange without additional adapter plate.
Integrated pneumatic feed-through
Integrated piston stroke monitoring
Patented fail-safe locking mechanism
Portfolio expansion - new size 007

## Slide 120
Principle of function
Drive
3
Housing
2
Sensor monitoring of the locking device
1
Locking mechanism
4
Air feed-through
5
Functional description
The quick-change system (SWS) consists of a quick-change master (SWK) and a quick-change adapter (SWA). The SWK is mounted onto the robot, and couples the SWA mounted onto your tool. A pneumatically driven locking piston, with its patented design, ensures that the connection is secure. After coupling, pneumatic and electric feed-throughs automatically supply your robot tool.

## Slide 121
New size SWS-046
Quick change system SWS-046 with 50 kg handling weight like SWS-040Q
No integrated pneumatic feed-through
4 flats for feed-through modules to mount up to 5 modules (On Flat C can be 2 modules mounted)
Integrated piston stroke monitoring with inductive switches
ISO mounting pattern 9409-1-100-6-M8 for direct mount on master side

## Slide 122
Application - Your benefit
High flexibility thanks to a variety of different feed-through possibilities
Great number of various modules to transfer different electrical signals & currents as well as fluidic media
Operational area for example in metal industry for welding applications
Example configuration blowtorch(welding):
  2 modules for welding current
  1 module for 19 digital signals
  1 module for 8 pneumatic feed-throughs
  1 module with 4 self-sealing ports to transfer cooling liquid to the blowtorch

## Slide 123
Application - Your benefit
Well suitable for high number of signals and/or air requirement on customer tooling
Up to 160 signals with 5x signal modules or up to 40 pneumatic feed-throughs with 5x pneumatic modules without additional adapter plate
Operational area for example in plastics industry for parts removal
Example configuration removal-gripper:
  2 modules for ultrasonic welding
  3 modules for 83 digital signals
  1 module for ethernet communication
  1 module for 6 pneumatic feed-throughs

## Slide 124
Advantages – Your benefits
Complete series of 14 sizes for optimal size selection and a broad application range
Patented fail-safe locking mechanism for secure connection between the quick-change master and adapter
Manual emergency unlocking possible no counter-forces from springs
All functional components made from hardened steel for high mechanical resilience of the changing system
Wide range of electric, pneumatic, and fluid modules for universal energy transmission possibilities
Integrated pneumatic feed-through for a safe power supply of the handling modules and tools
Possibility of transmission of fluid systems with self-sealing couplings possible
Adapter side coding via plug connector possible
Suitable storage racks for all sizes to ensure the optimum adaption to each application
ISO mounting pattern for easy assembly to most types of robots without needing additional adapter plates

## Slide 125
Technical data
Technical data overview |  |  |  |  |  | 
Size | Recommended handling weight | Locking force | Weight | Air connection thread pneumatic feed-through | Lock/unlock main connection | Max. distance when locking
 | [kg] | [N] | [kg] |  |  | [mm]
1 | 1.4 | 170 | 0.02 .. 0.08 | 4x M5 | M3 | 1
5 | 8 | 690 | 0.09 .. 0.27 | 6x M5 | M5 | 3
7 | 16 | 1100 | 0.08 .. 0.16 | 5x M5 | M5 | 3
11 | 16 | 1100 | 0.09 .. 0.29 | 6x M5 | M5 | 3
20 | 25 | 2300 | 0.32 .. 0.69 | 12x M5 | M5 | 3
21 | 25 | 2300 | 0.3 .. 0.7 | 8x G1/8" | M5 | 3
40 | 50 | 4500 .. 5650 | 0.6 .. 1.27 | 8x G1/8" | G1/8" | 3
41 | 50 | 4500 | 0.7 .. 1.4 | 6x G3/8" | G1/8" | 3
46 | 50 | 5800 | 1.03 .. 1.95 |  | G1/8" | 2.5
60 | 75 | 7400 | 0.7 .. 1.3 | 8x G1/8" | G1/8" | 3
71 | 79 | 8100 | 1.3 .. 1.8 | 8x G1/4" | G1/8" | 3
76 | 100 | 12000 | 1.4 .. 2.25 | 5x G3/8" | G1/8" | 2
110 | 150 | 12000 | 2.2 .. 4 | 8x G3/8" | G1/8" | 3
160 | 300 | 31000 | 2.86 .. 6.44 | 5x G3/8" | G1/8" | 2.54

## Slide 126
6-axis force/torque sensors
The first compact force/torque sensor with two calibrations and integrated electronics.
2 measurement ranges for selection
Rigid 6-axis force/torque sensor for precision measuring in all six degrees of freedom

## Slide 127
Precise. Reliable. Robust.
Compact design due to completely integrated electronics and status display via LEDs.
Simple configuration - two calibrations can be controlled in the sensor via web interface.
Plug & Work directly compatible for KUKA and Universal Robots via software module
Robust and durable even with short-term overloading, the sensor is protected from damage

## Slide 128
Principle of function
Resistance strain gauges
2
Electronics
1
Functional description
The strain gauges (DMS) of the 6-axis force/torque sensors measure the strain applied in all six degrees of freedom (Fx, Fy, Fz, Mx, My and Mz). The signals of the DMS are evaluated in the sensor and provided.

## Slide 129
Additional calibrations
Two additional dual-calibrations:
  SI-75-4/SI-150-8
  SI-480-20/SI-1200-50
New applications:
  Sensitive applications with low attacking forces and moments like weighing
  Applications with low attacking forces and moments like polishing and assembly processes
NEW SI-480-20/SI-1200-50
NEW SI-75-4/SI-150-8
Force[N]
Moment[Nm]
Existing
SI-200-8/SI-500-20

## Slide 130
Serial Communictaion
Communication via serial RS-485 protocol
Plug & Work via USB
Plug & Work for Universal Robot E-Series, especially for sensitive applications in case the integrated force-torque sensoris not sufficient
Three dual-calibrations:
  SI-75-4/SI-150-8
  SI-200-8/SI-500-20
  SI-480-20/SI-1200-50
NEW SI-480-20/SI-1200-50
NEW SI-75-4/SI-150-8
Force[N]
Moment[Nm]
NEW SI-200-8/SI-500-20
FTR-AXIA

## Slide 131
Advantages – Your benefits
Compact design due to space-saving set-up with integrated electronics
Two calibrations are available whereby two measurement ranges can be controlled via web interface
Plug & Work directly compatible for KUKA and Universal Robots via software module
Cost saving despite high precision due to optimized manufacturing
Robust design ensures due to a high overload range with protection against damage even with short-term overload
Version with LED display for status display on the sensor without evaluation via the controller

## Slide 132
Salestoolbox
Overview for our FT products and also competitive products available on Salestoolbox (Also on the iPad)
UR Cap available to downlaod or to mail directly from the Salestoolbox

## Slide 133
Technical data
Technical data overview |  |  |  |  |  |  |  |  |  |  | 
evaluation via | Weight | Calibration 1 | Range of measurement Fx, Fy | Range of measurement Fz | Range of measurement Mx, My | Range of measurement Mz | Calibration 2 | Max. range of measurement Fx, Fy | Range of measurement Fz | Range of measurement Mx, My | Range of measurement Mz
 | [kg] |  | [N] | [N] | [Nm] | [Nm] |  | [N] | [N] | [Nm] | [Nm]
EtherCAT | 0.3 | SI-200-8 | 200 | 360 | 8 | 8 | SI-500-20 | 500 | 900 | 20 | 20
EtherNet | 0.3 | SI-200-8 | 200 | 360 | 8 | 8 | SI-500-20 | 500 | 900 | 20 | 20

## Slide 134
Compensation unit XYZ
The world's first angular adjustment unit for robots for simultaneous rotational and angular adjustment.
Compensation in all 6 degrees of freedom
Compensation unit with rotation and angle compensation for adaptation of end effector to the position of the component

## Slide 135
Compensation unit XYZ
Compensation in all 6 degrees of freedom
Compensation unit with rotation and angle compensation for adaptation of end effector to the position of the component
X-Y-axis
lateral* angular
Z-axis
axial torsional
X
Y
Z
*During lateral compliance, the compliant plate moves toward the master body along the Z‑axis

## Slide 136
Principle of function
Integrated piston stroke monitoring
3
Locking piston
2
Housing
1
Spring for pre-clamping
4
Functional description
The compensation unit enables compensation of angle and rotation. Workpieces can be gripped despite positional offset and locational uncertainty. The flexibility of the unit can be pressurized with compressed air and adjusted via the air connection. The unit can be locked centrally and rigidly at maximum pressure.

## Slide 137
Principle of function
Functional description
The compensation unit enables compensation of angle and rotation. Workpieces can be gripped despite positional offset and locational uncertainty. The flexibility of the unit can be pressurized with compressed air and adjusted via the air connection. The unit can be locked centrally and rigidly at maximum pressure.
0,3
air pressure [bar]
2,1
4,1
6,9
Stiffness adjustment
Locked
compressed air

## Slide 138
Principle of function
Functional description
The compensation unit enables compensation of angle and rotation. Workpieces can be gripped despite positional offset and locational uncertainty. The flexibility of the unit can be pressurized with compressed air and adjusted via the air connection. The unit can be locked centrally and rigidly at maximum pressure.
0,3
2,1
4,1
6,9
No sensor function
Sensor function
Minimal pressure of 0.3 bar for proper sensor function
Monitoring of the centered home position from the compensation unit. Detection of the end position from the piston with a MMS magnetic switch. Once the piston is moved out of the end position (due to compensation of the unit) the sensor turns off.
 Monitoring of ‘touching’ a workpiece
compressed air
air pressure [bar]

## Slide 139
Applications - your benefits
Bin-Picking applications
Handling of parts from inclined planes

## Slide 140
Advantages – Your benefits
Deflection both while in rotation and at an angle compensate for inaccuracies in the position of the workpiece and saves time, cost and effort by simplifying robot programming
Centric reset allows components to be placed in a defined position
Spring-supported reset of the unit can be adjusted via compressed air for optimum deflection
ISO mounting pattern equipped with ISO standard both robot-side and tool-side A direct screw connection to conventional robot types is possible without an additional adapter plate
Monitoring of locking increases the process reliability and simplifies commissioning

## Slide 141
Technical data
Technical data overview |  |  |  |  |  | 
Size | Recommended handling weight | Compensation XY | Compensation Z | Angular deflection | Deflection rotatory | Weight
 | [kg] | [mm] | [mm] | [°] | [°] | [kg]
50 | 5 | 2.7 | 6.1 | 3 | 8 | 0.6

## Slide 142
End-of-Arm Modular System
The most comprehensive modular gripping system for all Universal Robots on the market.
Up to 36 product combination possibilities.
The modular gripping system consists of electrically and pneumatically controlled grippers, quick-change modules, and force/torque sensors, that are specifically adapted to robot arms from Universal Robots.

## Slide 143
Introduction
Universal Robots is a robot manufacturer with their headquarter in Odense, Denmark
Founded in 2005
approx. 550 employees (worldwide)
26.000 cobots in use (worldwide)
approx. 65 patents
approx. 58% market share (Cobots)
22 branches in total (worldwide) with their headquarter in Odense, Denmark
Focus on small and medium size companies and Human-Robot-Collaboration
Products:
Robots UR 3, 5 and 10 (CB and e-Series)

## Slide 144
Principle of function
Co-act EGP-C 40
3
SHS 50
2
FT-AXIA 80
1
EGP 40
4
KGG 100-80
5
Functional description
The components of the modular system are prepared for mechanic and electric direct connection to the Universal Robots sizes 3, 5, and 10. The pneumatic gripping units additionally include integrated micro valves, meaning no external valves are required.
PSH 22-1
6
JGP 80-1
7
JGP 100-1
8
PGN-plus-P 80-1
9
PGN-plus-P 100-1
10
PZN-plus 64
11

## Slide 145
Modular. Flexible. Easy.
Modular program comprises gripping and changing, as well as measuring of forces and torques
36 combination possibilities
Micro valves for actuating the pneumatic modules are already integrated into the SCHUNK adapters
FT-sensor (AXIA80)
Manual toolchanger (SHS)
Gripping System Plug & Work to the robot interface
Roboter UR 3, 5 oder 10 (Compatible to the CB and e-Series)
Adapter robot side
Adapter tool side

## Slide 146
Possiblities of combinations
Universalgripper PGN-plus-P Direct mount
Collaborative small part gripper Co-act EGP-C + manual toolchanger SHS
Centric gripper PZN-plus + 6-axis Force-Torque-Sensor FT-AXIA
Longstroke gripper PSH + manual toolchanger SHS + 6-axis Force-Torque-Sensor FT-AXIA

## Slide 147
Functionality Plug & Work
Electrical connection (M8, 8 pin) Pneumatic connection (connector 6 mm)
Tubeless direct connection between the housing and the gripper
Electrical interface for sensors (Standard MMS, inductive proximity switches possible)
Full usage of the UR robots electrical interface for sensors, micro valves and electric gripper. (A bypass is only necessary for the FT-Sensor and pneumatic tube)
Integrated micro valves (no external valves necessary)

## Slide 148
URcap Plugin
The term „URcap“ refers to software components that can be used together with the respective UR+ product on a robot from Universal Robots.
Included in the scope of delivery (USB-Stick or download)
Simplifies programming, especially with complex control of the tool
Support by a graphical interface (frontend)

## Slide 149
UR+ Showroom
SCHUNK is represented in the UR+ Showroom with a total of five categories.
www.universal-robots.com/plus
Electric Grippers
Co-act Grippers
Pneumatic Grippers
Force/Torque Sensors
Tool Changers

## Slide 150
Information market launch
Products are released for sale since December 2018
Category in the STB is available (catalog, flyer, manuals, pictures, animation and short presentation)
3D models and configurator in the Cadenas PartCommunity is available
Prices and Intec discounts are available inside in the SAP system
Availibility is given (some modules are on stock, production is working)
Sales model for UR integrators & dealers is available and communicated (only Germany)
For further questions, please contact the respective sales team or the TaskForce UR.
Sales team: Product line gripping system solutions Head TaskForce: Jochen Krieger Members TaskForce: Tobias Behringer, Galib Krdzalic, Simon Achauer, Benjamin Schell

## Slide 151
Advantages – Your benefits
Comprehensive modular systems consisting of grippers, change system and force/torque sensor for fast and easy entry into automation
Pre-assembled gripping unit with robot interface therefore no mounting kits or external valves required
Plug & Work with the interfaces to match Universal Robots
UR plug-in installation modules included in the scope of delivery for fast and easy commissioning
Up to 36 combination possibilities cover all automation applications

## Slide 152
Technical data
Technical data overview |  |  |  | 
Standard components | Stroke per jaw | Max. gripping force | Weight | Recommended workpiece weight
 | [mm] | [N] | [kg] | [kg]
Co-act EGP-C 40-N-N-URID | 6 | 140 | 0.6 | 0.7
EGP 40 | 6 | 140 | 0.7 | 0.7
KGG 100-80 | 40 | 175 | 1.2 | 0.9
PSH 22-1 | 28 | 320 | 1.7 | 1.6
JGP 80-1 | 8 | 415 | 1.33 | 2.1
JGP 100-1 | 10 | 660 | 1.72 | 3.3
PGN-plus-P 80-1 | 8 | 550 | 1.38 | 2.75
PGN-plus-P 100-1 | 10 | 870 | 1.8 | 4.35
PZN-plus 64-1 | 6 | 580 | 1.22 | 2.9
FT-AXIA 80 |  |  | 0.51 | 
SHS 50 |  |  | 0.35 | 11
SHS 50 |  |  | 0.14 | 11

## Slide 153
Universal swivel unit
The most robust swivel module with the highest power density on the market
25% higher torque
Universally usable unit for pneumatic swivel and turning movements

## Slide 154
Robust. Fast. High Performance.
Largest center bore also in version with media feed-through
Pre-adjusted shock absorber stroke
Density, play-free pre-loaded bearing
Modular design and can be combined in any way with options
Equipped with FKM seals as standard

## Slide 155
Principle of function
Swivel angle adjustment
3
Pinion
2
Housing
1
Damping
4
Drive
5
Functional description
When subjected to pressure, the two pneumatic pistons move their end faces in a straight line in their respective bores thus turning the pinion by means of the serrations on their sides.
Bearing
6

## Slide 156
Advantages – Your benefits
Finely graded series with a steady increase in torque for multiple cases of application, the correct size as a standard product is available
Large center bore for feed-through of cables and hoses with the same unit height
Pre-adjusted shock absorber stroke for fast and easy commissioning
Swivel angle can be selected as either 90° or 180° complete flexibility in selecting the angle of rotation, application-specific angles possible on request
Selectable end position adjustability either small or large for flexible adjustability of the swivel angle
Optionally attachable fluid feed-through and electrical feed-through for permanently safe feed-through of gases, vacuum, and electrical sensor and actuator signals
Modular attachment to various options for individual adjustment to various cases of application
Choice of electronic magnetic sensors or inductive proximity sensors for absolute variability of position monitoring

## Slide 157
Technical data
Technical data overview |  |  |  | 
Size | Torque | Swivel angle | Mass moment of inertia | Weight
 | [Nm] | [°] | [kgm²] | [kg]
14 | 1.13 | 90 .. 180 | 0.006 .. 0.014 | 0.44 .. 0.61
16 | 1.47 | 90 .. 180 | 0.08 | 0.62
25 | 5.95 | 90 .. 180 | 0.5 | 1.71
40 | 23.7 | 90 .. 180 | 7 | 5.93

## Slide 158
Information in detail

## Slide 159
Customer benefit calculation
Calculation and selection

## Slide 160
Customer benefit calculation
Calculation:  SSE

## Slide 161
Customer benefit design
Status design:  CADENAS adapter plates to PGN-plus and PZN-plus can be easily integrated
Under construction

## Slide 162
Customer benefit commisioning
Installation and commisioning Coloured connectors for simple identification of the signal transfer
Larger distance of screwing threads
Preset damper stroke
Simple setup of end position

## Slide 163
Customer benefit commisioning
Installation and commisioning Coloured connectors for simple identification of the signal transfer
Larger distance of screwing threads
Preset damper stroke
Simple setup of end position

## Slide 164
Installation and commisioning Coloured connectors for simple identification of the signal transfer
Larger distance of screwing threads
Preset damper stroke
Simple setup of end position
Customer benefit commisioning

## Slide 165
Customer benefit operation
Operation more cycles / h

## Slide 166
Customer benefit service
Service: Bouncing sensor can detect wear

## Slide 167
ETP sealing kit
ETP sealing FFT
ETP shock absorber
WZG disassembly tool sealing kit
Spare part kits & service

## Slide 168
Sales release (HMI 2019)
SRM | Basis | +3/-93° | MFT | EFT | SI/SF | Ext. damper
14 |  | Integrated in basis |  | - | - | 
16 |  |  |  |  |  | -
25 |  |  |  |  |  | -
40 |  |  |  |  |  | -

## Slide 169
Availability
Production of parts is started
Assemblies will be stored
Special purchase parts (pinion, damper) are ordered and partly delivered
Important: Availability of the main assembly capacities

## Slide 170
Support by head quarter
Pattern suitcase

## Slide 171
Support by head quarter
Customer list SRU plus (on demand)

## Slide 172
Jens Lehmann, German goalkeeper legend, SCHUNK brand ambassador since 2012 for safe, precise gripping and holding.
schunk.com/Lehmann