## Slide 1
Product presentation
RCV
Deburring tool

## Slide 2
Deburring tool
The deburring spindle that is the most robust and quickest to maintain on the market.
Up to 40,000 RPM
Pneumatic deburring spindle with radial compensation for deburring workpieces

## Slide 3
Compliant. Flexible. Robust.

## Slide 4
Principle of function
Air connection
3
Gimballed system
2
Rotating piston air engine
1
Tool holder
4
Air connection
5
The unit is driven by a pneumatic rotating piston air engine. Its speed of rotation depends on the unit size. The motor is driven by filtered and oiled air. The spindle is gimbal-mounted to compensate for tolerances on the workpiece contour. The Y-axis can optionally be fixed by a set screw. This means that pendulum compensation is only possible in the X axis. The compliance force is controlled via a second air connection. Depending on the pressure setting, a variable pressure force acts on the tool.
Functional description

## Slide 5
Advantages – Your benefits
The compensation force can be adjusted means of compressed air. for high-quality deburring results in any installation position
Flexible use on the robot arm or as a stationary unit
Rotating piston air engine with high torque for high feed rates and a reduced machining time
Flexibility in radial direction for a simplified robot programming
Lock function for the Y axis for an oscillating compensation only in the X-axis
Simple exchange of wear parts for maximum system availability and minimum spare parts requirements
Robust bearing for an optimized service life

## Slide 6
Technical data
Technical data overview
Size | Power | Idle speed | Max. compensation X | Max. compensation Y | Min. radial compensation force | Max. radial compensation force | Tool holder | Weight
 | [W] | [1/min] | [mm] | [mm] | [N] | [N] |  | [kg] |  |  | 
250 | 250 | 40000 | 7.1 | 7.1 | 9 | 54 | Collet chuck ER-11 6 mm and 8 mm | 1.71
490 | 490 | 30000 | 8.3 | 8.3 | 7 | 53 | Collet chuck ER-11 6 mm and 8 mm | 3.36