## Slide 1
Product presentation
MFT-R
Deburring tool

## Slide 2
Deburring tool
The most robust polishing spindle with radial compensation on the market
Up to 5,600 RPM
Radially compliant pneumatic polishing spindle, perfect for polishing and brushing workpieces

## Slide 3
Compliant. Flexible. Robust.

## Slide 4
Principle of function
Air connection
3
Gimballed system
2
Rotating piston air engine
1
Tool holder
4
Air connection
5
The unit is driven by a vane-type air motor. The motor is driven by filtered and oiled air. The spindle is gimbal-mounted to compensate for tolerances on the workpiece contour. The Y-axis can be optionally fixed by axis fixation set screws. This means that pendulum compensation is only possible in the X axis. The compliance force is controlled via a second air connection. Depending on the pressure setting, a variable pressure force acts on the tool.
Functional description

## Slide 5
Advantages – Your benefits
Adjustable stiffness of the spindle via air pressure for high-quality deburring results in any installation position
Flexible use on the robot arm or as a stationary unit
Rotating piston air engine with high torque for short stopping times and reduced processing times
Radial compliance for machining processes with radial compensation
Gimballed system for a robust set-up with compensation function and reduced programming effort of the robot
Lock function for the Y axis for an oscillating compensation only in the X-axis

## Slide 6
Technical data
Technical data overview
Size | Power | Idle speed | Max. compensation X | Max. compensation Y | Min. radial compensation force | Max. radial compensation force | Tool holder | Weight
 | [W] | [1/min] | [mm] | [mm] | [N] | [N] |  | [kg] |  |  | 
490 | 390 | 5600 | 7.1 | 7.1 | 9.4 | 70 | Collet chuck DA 6 mm and 8 mm | 4.42