## Slide 1
ROTA TB2
Pneumatic Power Chucks

## Slide 2: Product overview
Clamping Technology
Gripping Systems
Manual Lathe Chucks
Power Lathe Chucks with Through-hole
Power Lathe Chucks with Jaw Quick-change System
Power Lathe Chucks without Through-hole
Pneumatic Power Chucks
Steady Rests
Quick-change Systems
Customized Solutions
Chuck Jaws
Toolholders
Hydraulic Expansion Technology
Stationary Workholding
Lathe Chucks

## Slide 3: Pneumatic Power Chucks Application

## Slide 4: ROTA overview Pneumatic Power Chucks
ROTA TB2-LH
ROTA TB2
ROTA TB-LH
ROTA TB
ROTA TP

## Slide 5: ROTA TB2 Example of application
Clamping device:
ROTA TB2 600-275.
Features/Application:
Pneumatic power chuck with integrated cylinder of the newest generation. Optimized sealing prevents the penetration of dirt, coated functional components ensure a long service life and fast ventilation allow shorter cycle times.
Extra large through-hole for O.D. clamping of pipes with big diameter.

## Slide 6: ROTA TB2
Wedge hook drive
Corrosion-resistant, coated and extremely rigid base body
Very large through-hole
Mounting threads
Optimized lubrication system
Sealed base jaw guidance
Pneumatic cylinder integrated in the chuck
Static distributor ring
Pressure maintenance valve
2
1
3
4
5
6
7
8
2
1
3
4
6
7
8
5
9
9

## Slide 7: ROTA TB2
Base jaw guidance
Corrosion resistant components
RSS-P1: Wireless Clamping Pressure Control
1
1
2
2
Pressure sensor connected with the cylinder
Transmitter unit
Protection cover
Receiver antenna
Receiver
Chuck body ROTA TB2 made out of steel
Channel bores
3
4
5
3
4
5
1
1
2
2
3
3
Body
Piston
Center sleeve
7
7
6
6

## Slide 8: ROTA TB2
Exchangeable valve
Fast ventilation
Sealed base jaw guidance
Optimized lubrication system
1
1
2
2
Front-end profile sealing element
Sealing element
O-ring
3
3
1
1
2
2
Escaping air
Escaping air
1
1
Chuck body
Valve insert
Pressure maintenance valve
Sealing cap
2
2
3
3
4
4

## Slide 9: ROTA TB2
Pressure monitoring via sensor (optional)
1
2
Sufficient operating pressure is present
Pressure loss
1
2

## Slide 10: ROTA TB2

## Slide 11: Variants ROTA TB2
Technische Daten | Max. RPM [min-1] | Max. clamping force (at 6 bar) [kN] | stroke/jaw [mm] | Through-hole [mm]
ROTA TB2 470-140 | 1700 | 180 | 7 | 140
ROTA TB2 470-185 | 1700 | 115 | 7 | 185
ROTA TB2 570-230 | 1300 | 220 | 11.7 | 230
ROTA TB2 600-275 | 1300 | 200 | 11.7 | 275
ROTA TB2 685-325 | 1000 | 280 | 10 | 325
ROTA TB2 850-375 | 750 | 240 | 11.8 | 375
ROTA TB2 1000-560 | 500 | 240 | 12.8 | 560

## Slide 12: SCHUNK Services
Engineering
Dimensioning of special plates designed to the manufacturing specifications
Development of special solutions together with the customer
FEM analysis for critical components
Testing
Endurance tests with all new developments
Abrasion checking
Measurement of accuracy
Service
Initial operation of customer´s solution
Inspection and maintenance
Repairs