## Slide 1
ROTA TP
Pneumatic Power Chucks

## Slide 2: Product overview
Clamping Technology
Gripping Systems
Manual Lathe Chucks
Power Lathe Chucks with Through-hole
Power Lathe Chucks with Jaw Quick-change System
Power Lathe Chucks without Through-hole
Pneumatic Power Chucks
Steady Rests
Quick-change Systems
Customized Solutions
Chuck Jaws
Toolholders
Hydraulic Expansion Technology
Stationary Workholding
Lathe Chucks

## Slide 3: Pneumatic Power Chucks Application

## Slide 4: ROTA overview Pneumatic Power Chucks
ROTA TB2-LH
ROTA TB2
ROTA TB-LH
ROTA TB
ROTA TP

## Slide 5: ROTA TP Example of application
Clamping device:
ROTA TP 315-115 LH incl. special center sleeve.
Features/Application:
Pneumatic power chuck with integrated cylinder for O.D. clamping of pipes. Special center sleeve with feed chamfer and high dual stroke system enable save loading of the workpieces.

## Slide 6: ROTA TP
Distributor ring
Distributor ring cover
Profile sealing rings
Pneumatic cylinder integrated in the chuck
Very stable base jaw
Very large through-hole
Very stable wedge hook
Long piston guidance
Integrated safety valve
One-piece, rigid chuck body
2
1
3
4
5
6
7
8
9
2
1
3
4
6
7
8
9
5
10
10

## Slide 7: ROTA TP
Also available for stationary applications
The SCHUNK profile seal lifts itself through its own elasticity
Control of the self-contained power chucks
Clamping and opening is only possible at standstill
1
1
2
2
Double check valve
Profile sealing ring
Profile sealing ring
Distributor ring
Distributor ring cover
3
4
5
3
4
5

## Slide 8: ROTA TP/TB

## Slide 9: Variants ROTA TP
Technical Data | Max. RPM 1 [min-1] | Max. clamping force (at 6 bar) [kN] | Stroke/jaw [mm] | Through-hole [mm]
ROTA TP 125-26 | 4000 | 22 | 3 | 26
ROTA TP 160-38 | 3500 | 39 | 4.2 | 38
ROTA TP 200-52 | 2800 | 68 | 4.2 | 52
ROTA TP 250-68 | 2200 | 105 | 5 | 68
ROTA TP 315-90 | 1800 | 140 | 5 | 90
ROTA TP 315-105 | 2200 | 100 | 5 | 105
ROTA TP 350-115 | 2200 | 90 | 5 | 115
ROTA TP-LH 350-115 | 2200 | 90 | 15 | 115

## Slide 10: SCHUNK Services
Engineering
Dimensioning of special plates designed to the manufacturing specifications
Development of special solutions together with the customer
FEM analysis for critical components
Testing
Endurance tests with all new developments
Abrasion checking
Measurement of accuracy
Service
Initial operation of customer´s solution
Inspection and maintenance
Repairs