## Slide 1
VERO-S NSE3
Quick-change Pallet System

## Slide 2: Product Overview
Chuck Jaws
VERO-S
Toolholders
Hydraulic Expansion Technology
Stationary Workholding
KONTEC
TANDEM
ROTA
MAGNOS
PLANOS
Lathe Chucks
Clamping Technology
Gripping Systems

## Slide 3: Challenges
zukünftig
heute
Time
Variants
Time
Quantities
Time
Product life cycle
Time
Demand
Time
Global competition
Time
Required accuracy
Increasing relevance of the set-up process

## Slide 4: VERO-S – the set-up time optimizer

## Slide 5: Potential for savings
Chart: 
| 50 | 100 | 150 | 200
Rüstkosten mit VERO-S [€] | 250 | 500 | 750 | 1000
Rüstkosten ohne VERO-S [€] | 1250 | 2500 | 3750 | 5000
Number of set-up procedures
Set-up costs [€]
0
Set-up costs
without VERO-S
Set-up costs
with VERO-S
Notes: 5 min Rüstzeit pro Rüstvorgang mit VERO-S
25 min Rüstzeit pro Rüstvorgang ohne VERO-S
60€/h Maschinenkosten

## Slide 6: Amortisation
Even for older machines, the investment in SCHUNK VERO-S quick change pallet system amortizes within a minimum of time.
Thanks to the consistent interface of the clamping pin, the existing clamping devices can easily be integrated in the new system.
Calculation for set-up costs | Case 1 | Case 2
Investment in SCHUNK VERO-S [€] | 5.000 | 10.000
Time per set-up procedure without VERO-S [min] | 25 | 
Time per set-up procedure with VERO-S [min] | 5 | 
Machine costs [€/h] | 60 | 
Number of set-up procedures per day | 5 | 
Working days per month | 20 | 
Working days per year | 240 | 
Payback Time |  | 
Set-up procedures | 250 | 500
Working days | 50 | 100
Months | 2,5 | 5
Years | 0,21 | 0,42

## Slide 7: Consistency of pull-down and holding forces
 | Pull-down force [N] |  | Holding force [N] |  |  |  |  |  |  | Recommended machines
 | Without Turbo | With Turbo | SPx mikro 10 |  | SPx mini 20 |  | SPx 40 |  |  | 
 |  |  | M3 | M4 | M6 | M8 | M10 | M12 | M16 | 
NSE mikro | 150 | 400 | 3.000 | 5.000 |  |  |  |  |  | 
NSE mini 90 | 500 | 1.500 |  |  | 15.000 | 25.000 |  |  |  | 
NSE mini 90-25 | 1.500 | 6.000 |  |  |  |  |  |  |  | 
NSE3 138 | 8.000 | 28.000 |  |  |  |  | 35.000 | 50.000 | 75.000 | 
NSE mikro
FHold
Fpull-down
NSE mini 90
NSE3 138
32
50
63
80
100
40
HSK-Size

## Slide 8: VERO-S modular system

## Slide 9: SCHUNK Services
Engineering
Dimensioning of special plates designed to the manufacturing specifications
Development of special solutions together with the customer
FEM analysis for critical components
Testing
Endurance tests with all new developments
Abrasion checking
Measurement of accuracy
Service
Initial operation of customer´s solution
Inspection and maintenance
Repairs

## Slide 10: VERO-S Overview
Milling and turning applications
Easy milling applications
Direct workpiece clamping
Automated machine loading
General milling applications
Further applications

## Slide 11: VERO-S NSE3 Example of application
VERO-S:
Standard 6-way clamping station with NSE plus 138 modules.
Clamping device:
Manual chuck ROTA-S plus 2.0, KONTEC single-acting vise KSG.
Features/Application:
High variety of processing thanks to large variances of clamping devices.

## Slide 12: VERO-S NSE3
Optional cone seal
Patented dual stroke system
Turbo function
Large surfaces
Completely sealed system
Large flat surfaces
Monitoring of the clamping slide position „open condition“ and „locked position“
Flat seal to protect the interface during machining
Cover caps for fastening screws
Sliding bearings in force flow
Lower-lying countersunk screws
2
1
3
4
5
6
7
8
9
11
10
2
1
3
4
5
6
7
8
9
11
10
5
5

## Slide 13: VERO-S NSE3
Locking via clamping slides
Centering via short taper
Exchangeability of the plug against a cone seal
Easy positioning – more user-friendly

## Slide 14: VERO-S NSE3
Spring force
Additional force, resulting from the turbo function
2
1
2
1
Control of the quick-change pallet system
Lower-lying countersunk screws
Integrated turbo function
Rolling friction between piston and clamping slide

## Slide 15: VERO-S NSE3
Monitoring of the clamping slide position via the dynamic pressure
Opened condition
Locked condition
Hermetically sealed – maintenance-free
NSE3 138-V1 – the quick-change pallet module with integrated anti-rotation protection
NSE-T3 – the tombstone module of the third generation

## Slide 16: VERO-S NSE3
Optional sensor variants
AFS3 138 PMI:
Open condition
Locked condition with clamping pin
Error message at locked condition without clamping pin
AFS3 138 MMS:
Open condition
Locked condition with clamping pin
Optional cone seal

## Slide 17: VERO-S NSE3
Clamping stroke
Fast stroke
Force
Travel
Actuation force
Force on the clamping slide:
Pull-down force: 5x higher than the actuation force
2
1
3
4
2
1
3
4
7
5
6
5
6
6
5
7
Turbo function
max. 28 kN
Spring force clamping
max. 8 kN
Actuation pressure of the turbo function
Pull-down force
Comparison: Pull-down force spring clamping and turbo funtion
The patented fast and clamping stroke

## Slide 18: VERO-S NSE3
Standard clamping pins |  |  | Compensation pins | Accuracy pin | Dove tail pins | Clamping pins without centering collar | Heavy duty pins | Indexing pin IXB V1
SPA | SPB | SPC | SPA-X / SPA-XY | SPG | SPx-S | SPx-OB | SPA-F / SPC-F | IXB V1
Clamping pin | Positioning pin | Holding pin | Compensation of pitch fluctuations +/- 1 mm | Repeat accuracy < 0.002 mm | Fastening depth 3.5 mm | Mounting via fitting screw | Holding force of 75 kN | Position orientation of clamping pallets or devices
3
1
2
3
1
2
3
Typ A fixed
Typ B positioned
Typ C with a centering play
Configuration of clamping pins type A, B and C

## Slide 19: VERO-S NSE3

## Slide 20: Variants of VERO-S NSE3
Technical Data | NSE3 | NSE3 138-V1 | NSE3-T3 138 | NSE3-T3 138-V
Diameter [mm] | 138 | 138 | 138 | 138
Pull-down force [kN] | 8 | 8 | 7 | 7
Pull-down force with turbo [kN] | 28 | 28 | 24 | 24
Unlocking pressure [bar] | 6 | 6 | 6 | 6
Repeat accuracy [mm] | < 0.005 | < 0.005 | < 0.005 | < 0.005
Weight [kg] | 4.4 | 4.4 | 3.5 | 3.5
* All Variants are available with cone seal

## Slide 22: VERO-S Application
VERO-S:
Special 4-Way clamping station with NSE plus 138 clamping modules.
Clamping device:
TANDEM clamping force blocks.
Features/Application:
The actuation of the modules via the machine table allows a high level of automation.

## Slide 23: VERO-S Application
VERO-S:
Standard 6-Way clamping station with NSE plus 138 clamping modules.
Clamping device:
Clamping pallet with 4 KSC2 centric clamping vises.
Features/Application:
The application of clamping pallets allows a high arrangement of clamping devices and workpieces.

## Slide 24: VERO-S Application
VERO-S:
Special 10-Way tombstone with NSE plus 138 clamping modules.
Clamping device:
KSM clamping rail.
Features/Applications:
The vibration-damping construction of the tombstones enables the machining of highly complex setups.

## Slide 25: VERO-S Application
VERO-S:
Special 8-Way clamping station with NSE plus 138 clamping modules.
Clamping device:
Clamping pyramid with NSE plus 138 clamping modules, KSC centric clamping vise and colle chuck mounting.
Features/Application:
Maximum utilization of the processing space of the machine.

## Slide 26: VERO-S Application
VERO-S:
Special 8-Way clamping station with NSE plus 138 clamping modules.
Clamping device:
KSG clamping vise.
Features/Application:
Integration of the modules in the machine table by the machine manufacturer.

## Slide 27: VERO-S Application
VERO-S:
Special 8-Way clamping station with NSE plus 138 clamping modules.
Clamping device:
PLANOS vacuum matrix plates.
Features/Application:
Clamping of non-ferromagnetic materials by PLANOS modular system.

## Slide 28: VERO-S Application
VERO-S:
Special 8-Way clamping station with NSE plus 138 clamping modules.
Clamping device:
KSX 5-Axis clamping vise.
Features/Application:
Height alignment of the multi-parted clamping station.

## Slide 29: VERO-S Application
VERO-S:
Special 6-Way clamping station with NSE plus 138 clamping modules.
Clamping device:
Direct workpiece clamping combined with clamping pin extension.
Features/Application:
Increased accessibility to the workpiece.

## Slide 30: VERO-S Application
VERO-S:
Special 24-Way clamping station with NSE plus 138 clamping modules
Clamping device:
Clamping jaw boxes Direct workpiece clamping
Features/Application:
OP10 Clamping jaw boxes OP20 Direct workpiece clamping

## Slide 31: VERO-S Application
VERO-S:
Direct workpiece clamping 2-Way NSE plus 138 clamping modules.
Clamping device:
Direct workpiece clamping MAGNOS magnetic chuck
Features/Application:
Flexibility and position accuracy thanks to the combination of VERO-S and MAGNOS.

## Slide 32: VERO-S Application
VERO-S:
Direct workpiece clamping 2-Way NSE plus 138 clamping modules.
Clamping device:
Direct workpiece clamping.
Features/Application:
Flexible adjustment of the height and position of the modules. Very good accessibility of all sides.