## Slide 1
VERO-S NSA plus
The specialist for automated production

## Slide 2: Product Overview
Chuck Jaws
VERO-S
Toolholders
Hydraulic Expansion Technology
Stationary Workholding
KONTEC
TANDEM
ROTA
MAGNOS
PLANOS
Lathe Chucks
Clamping Technology
Gripping Systems

## Slide 3: Challenges
zukünftig
heute
Time
Variants
Time
Quantities
Time
Product life cycle
Time
Demand
Time
Global competition
Time
Required accuracy
Increasing relevance of the set-up process

## Slide 4: VERO-S – the set-up time optimizer

## Slide 5: Potential for savings
Chart: 
| 50 | 100 | 150 | 200
Rüstkosten mit VERO-S [€] | 250 | 500 | 750 | 1000
Rüstkosten ohne VERO-S [€] | 1250 | 2500 | 3750 | 5000
Number of set-up procedures
Set-up costs [€]
0
Set-up costs
without VERO-S
Set-up costs
with VERO-S
Notes: 5 min Rüstzeit pro Rüstvorgang mit VERO-S
25 min Rüstzeit pro Rüstvorgang ohne VERO-S
60€/h Maschinenkosten

## Slide 6: Amortisation
Even for older machines, the investment in SCHUNK VERO-S quick change pallet system amortizes within a minimum of time.
Thanks to the consistent interface of the clamping pin, the existing clamping devices can easily be integrated in the new system.
Calculation for set-up costs | Case 1 | Case 2
Investment in SCHUNK VERO-S [€] | 5.000 | 10.000
Time per set-up procedure without VERO-S [min] | 25 | 
Time per set-up procedure with VERO-S [min] | 5 | 
Machine costs [€/h] | 60 | 
Number of set-up procedures per day | 5 | 
Working days per month | 20 | 
Working days per year | 240 | 
Payback Time |  | 
Set-up procedures | 250 | 500
Working days | 50 | 100
Months | 2,5 | 5
Years | 0,21 | 0,42

## Slide 7: Consistency of pull-down and holding forces
 | Pull-down force [N] |  | Holding force [N] |  |  |  |  |  |  | Recommended machines
 | Without Turbo | With Turbo | SPx mikro 10 |  | SPx mini 20 |  | SPx 40 |  |  | 
 |  |  | M3 | M4 | M6 | M8 | M10 | M12 | M16 | 
NSE mikro | 150 | 400 | 3.000 | 5.000 |  |  |  |  |  | 
NSE mini 90 | 500 | 1.500 |  |  | 15.000 | 25.000 |  |  |  | 
NSE mini 90-25 | 1.500 | 6.000 |  |  |  |  |  |  |  | 
NSE3 138 | 8.000 | 28.000 |  |  |  |  | 35.000 | 50.000 | 75.000 | 
NSE mikro
FHold
Fpull-down
NSE mini 90
NSE3 138
32
50
63
80
100
40
HSK-Size

## Slide 8: VERO-S modular system

## Slide 9: SCHUNK Services
Engineering
Dimensioning of special plates designed to the manufacturing specifications
Development of special solutions together with the customer
FEM analysis for critical components
Testing
Endurance tests with all new developments
Abrasion checking
Measurement of accuracy
Service
Initial operation of customer´s solution
Inspection and maintenance
Repairs

## Slide 10: VERO-S Overview
Milling and turning applications
Easy milling applications
Direct workpiece clamping
Automated machine loading
General milling applications
Further applications

## Slide 11: VERO-S NSA plus Example of application
VERO-S:
Special 4-way clamping station with NSA plus 120 clamping modules, Robot coupling NSR maxi, Pallet coupling PKL maxi.
Clamping device:
Clamping pallet with KONTEC KSC 125-160.
Features/Application:
Thanks to the monitoring systems of the clamping station, VERO-S is best suited for automated loading and unloading.

## Slide 12: VERO-S NSA plus
High-precision short taper centering
Patented dual stroke system
Turbo function
Large surfaces
Completely sealed system
Flat work surface at outer diameter
Cover caps for mounting screws
Lifting function when opening the modules
Contact monitoring
Entry radii on the module
Flexible piston
Pneumatic system
11
10
9
8
7
6
5
4
3
2
1
12
11
10
9
8
7
6
5
4
3
2
1
12
5
5

## Slide 13: VERO-S NSA plus
Integrated turbo function
Spring force
Additional force, resulting from the turbo function
2
1
2
1
Turbo function
max. 15 kN
Spring force clamping
max. 5 kN
Actuation pressure of the turbo function
Pull-down force
Locking via clamping slide
Centering via short taper
Comparison: Pull-down force spring clamping and turbo funtion

## Slide 14: VERO-S NSA plus
Clamping module opened – the lifting function lifts the pallet.
Clamping module closed – the lifting function is pushed back by the weight of the pallet.
Opened condition
Locked condition
2
1
2
1
Flat work surface at outer diameter
Lifting function
Monitoring of the clamping slide position via the dynamic pressure
Cleaning and monitoring the flat work surface
Contact surfaces
1
1
1
1
1

## Slide 15: VERO-S NSA plus
Configuration of clamping rings type A, B und C
Easy positioning – more user friendly
Extremely flat design
3
1
2
3
1
2
3
Typ A fixed
Typ B positioned
Typ C with centering play

## Slide 16: Variants VERO-S NSA plus
Technical Data | NSA plus 120 | NSA plus 160
Diameter [mm] | 118 | 158
Pull-down force [kN] | 3 | 5
Pull-down force with turbo [kN] | 9 | 15
Unlocking pressure [bar] | 6 | 6
Repeat accuracy [mm] | < 0.005 | < 0.005
Lifting force [kN] | 1 | 2
Weight [kg] | 2.5 | 5.8