## Slide 1
VERO-S NSR
Robot coupling for high-end pallet handling

## Slide 2: Product Overview
Chuck Jaws
VERO-S
Toolholders
Hydraulic Expansion Technology
Stationary Workholding
KONTEC
TANDEM
ROTA
MAGNOS
PLANOS
Lathe Chucks
Clamping Technology
Gripping Systems

## Slide 3: Challenges
zukünftig
heute
Time
Variants
Time
Quantities
Time
Product life cycle
Time
Demand
Time
Global competition
Time
Required accuracy
Increasing relevance of the set-up process

## Slide 4: VERO-S – the set-up time optimizer

## Slide 5: Potential for savings
Chart: 
| 50 | 100 | 150 | 200
Rüstkosten mit VERO-S [€] | 250 | 500 | 750 | 1000
Rüstkosten ohne VERO-S [€] | 1250 | 2500 | 3750 | 5000
Number of set-up procedures
Set-up costs [€]
0
Set-up costs
without VERO-S
Set-up costs
with VERO-S
Notes: 5 min Rüstzeit pro Rüstvorgang mit VERO-S
25 min Rüstzeit pro Rüstvorgang ohne VERO-S
60€/h Maschinenkosten

## Slide 6: Amortisation
Even for older machines, the investment in SCHUNK VERO-S quick change pallet system amortizes within a minimum of time.
Thanks to the consistent interface of the clamping pin, the existing clamping devices can easily be integrated in the new system.
Calculation for set-up costs | Case 1 | Case 2
Investment in SCHUNK VERO-S [€] | 5.000 | 10.000
Time per set-up procedure without VERO-S [min] | 25 | 
Time per set-up procedure with VERO-S [min] | 5 | 
Machine costs [€/h] | 60 | 
Number of set-up procedures per day | 5 | 
Working days per month | 20 | 
Working days per year | 240 | 
Payback Time |  | 
Set-up procedures | 250 | 500
Working days | 50 | 100
Months | 2,5 | 5
Years | 0,21 | 0,42

## Slide 7: Consistency of pull-down and holding forces
 | Pull-down force [N] |  | Holding force [N] |  |  |  |  |  |  | Recommended machines
 | Without Turbo | With Turbo | SPx mikro 10 |  | SPx mini 20 |  | SPx 40 |  |  | 
 |  |  | M3 | M4 | M6 | M8 | M10 | M12 | M16 | 
NSE mikro | 150 | 400 | 3.000 | 5.000 |  |  |  |  |  | 
NSE mini 90 | 500 | 1.500 |  |  | 15.000 | 25.000 |  |  |  | 
NSE mini 90-25 | 1.500 | 6.000 |  |  |  |  |  |  |  | 
NSE3 138 | 8.000 | 28.000 |  |  |  |  | 35.000 | 50.000 | 75.000 | 
NSE mikro
FHold
Fpull-down
NSE mini 90
NSE3 138
32
50
63
80
100
40
HSK-Size

## Slide 8: VERO-S modular system

## Slide 9: SCHUNK Services
Engineering
Dimensioning of special plates designed to the manufacturing specifications
Development of special solutions together with the customer
FEM analysis for critical components
Testing
Endurance tests with all new developments
Abrasion checking
Measurement of accuracy
Service
Initial operation of customer´s solution
Inspection and maintenance
Repairs

## Slide 10: VERO-S Overview
Milling and turning applications
Easy milling applications
Direct workpiece clamping
Automated machine loading
General milling applications
Further applications

## Slide 11: VERO-S NSR Example of application
VERO-S:
Clamping module NSE plus 138, Robot coupling NSR, Palett coupling PKL.
Clamping device:
Manual chuck ROTA-S plus 2.0.
Features/Application:
The high pull-down force of the NSR robot coupling enables the handling of extremely heavy pallets (up to 1000 kg with dimensions 800 x 800 mm). The slim construction of the PKL allows a low design of clamping station and clamping pallet.

## Slide 12: VERO-S NSR
High-precision short taper centering
Patented dual stroke system
Turbo function
Large surfaces
Completely sealed system
Steel inlays with integrated cleaning function
Monitoring of the clamping slide position module opened and module closed
Weight-optimized design
Anti-twist protection
Entry radii on the clamping pin
Actuation of the module
Fitting screws
Pneumatic system
5
6
7
8
9
10
4
3
2
1
13
12
11
5
6
7
8
9
10
4
3
2
1
13
12
11
9
11
5
5

## Slide 13: VERO-S NSR
Integrated turbo function
Locking via clamping slide
Spring force
Additional force, resulting from the turbo function
Turbo function connection
2
1
2
1
3
3
Turbo-Funktion
max. 50 kN
Spring force clamping
max. 12 kN
Pull-down force
Actuation pressure of the turbo function
Centering via short taper
Comparison: Pull-down force spring clamping and turbo funtion

## Slide 14: VERO-S NSR
Cleaning based on air purge
Monitoring of pallet presence (optional)
Monitoring opened or clamped (optional)
Control of the robot coupling
2
1
Open
Turbo function
Air purge
1
2
1
3
3
2
3
Robot coupling opened
Robot coupling closed

## Slide 15: VERO-S NSR
Torque pin via slanted surfaces on the robot coupling
Torque pin via two cylindrical pins in the front of the robot coupling
2
1
2
1
Easy positioning – more user friendly
Slim design
Torque pin for pallets

## Slide 16: Variants VERO-S NSR
Technical Data | NSR mini 100 | NSR 160 | NSR maxi 220
Length [mm] | 100 | 159 | 220
Width [mm] | 40 | 60 | 176
Pull-down force [kN] | 1 | 4 | 12
Pull-down force with turbo [kN] | 4 | 15 | 50
Unlocking pressure [bar] | 6 | 6 | 6
Repeat accuracy [mm] | < 0.02 | < 0.02 | < 0.02
Moment Mx max. [Nm] | 75 | 600 | 4000
Moment Mz max. [Nm] | 200 | 1600 | 4000
Weight [kg] | 0,4 | 1,6 | 21