## Slide 1
TANDEM KSA plus
Clamping Force Blocks I manually operated

## Slide 2: Product Overview
Chuck Jaws
Toolholders
Hydraulic Expansion Technology
Stationary Workholding
Lathe Chucks
Clamping Technology
Gripping Systems
MAGNOS
VERO-S
KONTEC
TANDEM
ROTA
Tombstones

## Slide 3: Challenges
zukünftig
heute
Time
Required
accuracy
Time
Variants
Time
Global
competition
Time
Automation
Increasing relevance of the set-up process

## Slide 4: TANDEM Clamping Force Blocks
High workpiece density at small space
Optimum accessibility of the machine spindle to the workpiece
High duration at low non-productive times per workpiece

## Slide 5: TANDEM Overview
Variants | Standard stroke | Long stroke (-LH) | With fixed jaw (-F)
Actuation Types | Pneumatic (KSP plus) | Hydraulic (KSH plus) | Manually (KSA plus) | Spring-loaded (KSF plus)

## Slide 6: TANDEM Portfolio
Stroke/jaw [mm]
Chart: Jaw Stroke
| 64 | 100 | 160 | 250
Standard stroke | 2 | 2 | 3 | 5
Long stroke | 4 | 6 | 8 | 15
With fixed jaw | 4 | 4 | 6 | 10
Size
Chart: Clamping Force
| 64 | 100 | 160 | 250
Standard stroke | 4.5 | 18 | 45 | 55
Long stroke | 4.5 | 16 | 40 | 20
With fixed jaw | 4 | 18 | 45 | 55
Max. clamping force [kN]
Size

## Slide 7: TANDEM Jaw Program
Supporting Jaws + SCHUNK Jaw Program | 
TBA-D | Chuck Jaws
Top Jaws Blank |  | 
Mounting: via tongue and groove | Mounting: via fine serrations 1,5 x 60° | 
KTR / KTR-H | STR / STR-H | STR-S

## Slide 8: SCHUNK Services
Engineering
Dimensioning of special plates designed to the manufacturing specifications
Development of special solutions together with the customer
FEM analysis for critical components
Testing
Endurance tests with all new developments
Abrasion checking
Measurement of accuracy
Service
Initial operation of customer´s solution
Inspection and maintenance
Repairs

## Slide 9: TANDEM Overview
Manual
Hydraulic
Pneumatic
Spring force

## Slide 10: TANDEM KSA plus
Wedge hook drive
Hardened and extremely rigid base body
Optimized lubrication system
Long jaw guidance
Low height
Improved design which is insensitive to dirt
Standard chuck jaw interface
Optimized outside contour
Control of the clamping modules
Chuck pistons guided in the body
Manually actuated system with large gear ratio
2
1
3
4
5
6
7
8
9
11
10
2
1
3
4
6
7
8
11
10
5

## Slide 11: TANDEM KSA plus
Z-version (optional)
Force Flow in the KSA plus
1
Actuating force depending on the applied torque
Clamping force depending on the actuating force and the transmission ratio
Normal force between the base jaw and chuck body
Torque on the pinion
2
3
4
Positioning bore
1
1
2
2
3
3
4
1
Chip-repellent design

## Slide 12: TANDEM KSA plus
Cover plugs for the mounting screws
Alignment edge
Lubrication system
2
1
Manual lubrication
Central lubrication
1
2
2
Coolant drain hole

## Slide 13: Variants of TANDEM KSA plus
Technical data | KSA plus 100 |  |  | KSA plus 160 |  | 
 | KSA | KSA-LH | KSA-F | KSA | KSA-LH | KSA-F
Stroke/jaw [mm] | 2 | 6 | 4 | 3 | 8 | 6
Clamping force [kN] | 18 | 8 | 18 | 45 | 20 | 45
Max. torque [Nm] | 8 | 8 | 8 | 15 | 15 | 15
Repeat accuracy vise [mm] | 0.01 | 0.01 | 0.01 | 0.02 | 0.02 | 0.02
Max. jaw height [mm] | 60 | 60 | 60 | 60 | 60 | 60
Weight [kg] | 5 | 5 | 5 | 14 | 14 | 14