## Slide 1
KONTEC KSC2
Centric clamping vise with jaw quick-change system

## Slide 2: Product Overview
Chuck Jaws
Toolholders
Hydraulic Expansion Technology
Stationary Workholding
Lathe Chucks
Clamping Technology
Gripping Systems
MAGNOS
VERO-S
KONTEC
TANDEM
ROTA
Tombstones

## Slide 3: Challenges
zukünftig
heute
Time
Depth of
production
Increasing importance
of workpiece clamping
Time
Flexibility
Time
Global
competition

## Slide 4: SCHUNK Services
Engineering
Dimensioning of special plates designed to the manufacturing specifications
Development of special solutions together with the customer
FEM analysis for critical components
Testing
Endurance tests with all new developments
Abrasion checking
Measurement of accuracy
Service
Initial operation of customer´s solution
Inspection and maintenance
Repairs

## Slide 5: KONTEC Portfolio
Single-acting Vise | Centric Clamping Vise | Multi Clamping Vise
Clamping towards a fixed jaw Fixed jaw as reference High repeat accuracy Especially suitable for workpieces with dimensioning from the side | Symmetric clamping Workpiece zero point is always in the center Optimum accessibility for 5-axis milling Especially suitable for workpieces with dimensioning from the center | Clamping of multiple workpieces Multifunctional usage Reduction of setup times Optimum usage of the machine table

## Slide 6: KONTEC Portfolio
Chart: Clamping range
| 40 | 65 | 80 | 90 | 100 | 125 | 160
Vise with fixed Jaw | 81 | 131 | 192 | 0 | 245 | 343 | 491
Centric clamping Vise | 71 | 123 | 120 | 0 | 0 | 301 | 461
Multi Clamping Vise | 571 | 571 | 126 | 571 | 0 | 121 | 331
Max. Clamping range [mm]
Jaw width
Chart: Clamping force
| 40 | 65 | 80 | 90 | 100 | 125 | 160
Vise with fixed Jaw | 12 | 20 | 25 | 0 | 40 | 40 | 50
Centric Clamping Vise | 7 | 15 | 25 | 0 | 0 | 35 | 50
Multi Clamping Vise | 30 | 30 | 25 | 30 | 0 | 40 | 0
Max. Clamping force [kN]
Jaw width

## Slide 7: Fast adaption to new clamping tasks
System Jaws |  |  | 
Standard reversible jaw | Reversible jaw, grip -grip | Enlarged span width -VS | Aluminium jaw -AL
Adapter- and swivel plates -R | 5-axis standard jaw -5A / -5A-VS | 6-fold jaw -6B | Reversible jaw grip, smooth central jaw -ST
Chuck Jaws |  |  | 
Chuck jaw with locator pin | Spring plate, pull-down jaw | Prismatic jaw | Stepped jaw, grip

## Slide 8: KONTEC Overview
Centric Clamping Vise
Single-acting Vise
Multi Clamping Vise

## Slide 9: KONTEC Centric Clamping Vise
KSC2
Clamping vise for small components
KSC
Basic Clamping Vise

## Slide 10: KONTEC KSC2 Example of application

## Slide 11: KONTEC KSC2
Complete encapsulated
Operation with hexagon connection
Jaw quick-change
Center adjustment
1st + 2nd sided machining
Compact design
2
1
3
4
5
6
1
3
4
6
5
2

## Slide 12: KONTEC KSC2
KSC2 grip
KSC2 precision

## Slide 13: Variants of KONTEC KSC2
Technical data | KSC2 40*1 | KSC2 65*2
Jaw width [mm] | 40 | 65
Clamping force [kN] | 7 | 15
Max. torque [Nm] | 20 | 50
*1 Additionally avaliable in -grip and -mini
*2 Additionally available in -grip