## Slide 1
KONTEC KSG
Modular designed machine vise

## Slide 2: Product Overview
Chuck Jaws
Toolholders
Hydraulic Expansion Technology
Stationary Workholding
Lathe Chucks
Clamping Technology
Gripping Systems
MAGNOS
VERO-S
KONTEC
TANDEM
ROTA
Tombstones

## Slide 3: Challenges
zukünftig
heute
Time
Depth of
production
Increasing importance
of workpiece clamping
Time
Flexibility
Time
Global
competition

## Slide 4: SCHUNK Services
Engineering
Dimensioning of special plates designed to the manufacturing specifications
Development of special solutions together with the customer
FEM analysis for critical components
Testing
Endurance tests with all new developments
Abrasion checking
Measurement of accuracy
Service
Initial operation of customer´s solution
Inspection and maintenance
Repairs

## Slide 5: KONTEC Portfolio
Single-acting Vise | Centric Clamping Vise | Multi Clamping Vise
Clamping towards a fixed jaw Fixed jaw as reference High repeat accuracy Especially suitable for workpieces with dimensioning from the side | Symmetric clamping Workpiece zero point is always in the center Optimum accessibility for 5-axis milling Especially suitable for workpieces with dimensioning from the center | Clamping of multiple workpieces Multifunctional usage Reduction of setup times Optimum usage of the machine table

## Slide 6: KONTEC Portfolio
Chart: Clamping range
| 40 | 65 | 80 | 90 | 100 | 125 | 160
Vise with fixed Jaw | 81 | 131 | 192 | 0 | 245 | 343 | 491
Centric clamping Vise | 71 | 123 | 120 | 0 | 0 | 301 | 461
Multi Clamping Vise | 571 | 571 | 126 | 571 | 0 | 121 | 331
Max. Clamping range [mm]
Jaw width
Chart: Clamping force
| 40 | 65 | 80 | 90 | 100 | 125 | 160
Vise with fixed Jaw | 12 | 20 | 25 | 0 | 40 | 40 | 50
Centric Clamping Vise | 7 | 15 | 25 | 0 | 0 | 35 | 50
Multi Clamping Vise | 30 | 30 | 25 | 30 | 0 | 40 | 0
Max. Clamping force [kN]
Jaw width

## Slide 7: Fast adaption to new clamping tasks
System Jaws |  |  | 
Standard reversible jaw | Reversible jaw, grip -grip | Enlarged span width -VS | Aluminium jaw -AL
Adapter- and swivel plates -R | 5-axis standard jaw -5A / -5A-VS | 6-fold jaw -6B | Reversible jaw grip, smooth central jaw -ST
Chuck Jaws |  |  | 
Chuck jaw with locator pin | Spring plate, pull-down jaw | Prismatic jaw | Stepped jaw, grip

## Slide 8: KONTEC Overview
Centric Clamping Vise
Single-acting Vise
Multi Clamping Vise

## Slide 9: KONTEC Single-acting Vise
KSO
Clamping vise for small components
KSC-F
Basic clamping vise
KSG
Machine vise
KSX
5-axis clamping vise
With force amplification
Without force amplification

## Slide 10: KONTEC KSG Anwendungsbeispiel
KONTEC:
Spannmittel:
Merkmale/Anwendung:

## Slide 11: KONTEC KSG
Encapsulated force transmission
Trouble-free clamping
Versatile range of chuck jaws
Controlled clamping force
Precise base body
Cooling lubricant drain
Clamping force via drawbar
Lever quick clamping
Easy removal of spindle assembly group
2
1
3
4
5
6
7
8
9
2
1
3
4
6
7
8
9
5

## Slide 12: KONTEC KSG
Can be cleanded and disassembled in just a few seconds
Completely encapsulated force transmission box
Lever quick clamping
Continously adjustable clamping force
1
1
2
2
Coupling pin
Spindle assembly group

## Slide 13: KONTEC KSG
Clamping by tension
Drainage slots
Threads for workpiece stops in the base body
Mounting options
1
1
Drainage slot
1
1
Thread for stops
1
1
2
2
3
3
Fastening via quick-change pallet system
Fastening using two screws
Fastening for positional orientation using fitting screws

## Slide 14: Variants of KONTEC KSG
Technical data | KSG 100* | KSG 125* | KSG 160*
Jaw width [mm] | 100 | 125 | 160
Clamping force [kN] | 4 - 30 | 4 - 40 | 4 - 40
* Additionally available in -VS, -R, -5A-VS