## Slide 1
MAGNOS MSC
Magnetic Clamping Technology

## Slide 2: Product Overview
MAGNOS
VERO-S
KONTEC
TANDEM
ROTA
Tombstones
Chuck Jaws
Toolholders
Stationary Workholding
Lathe Chucks
Hydraulic Expansion Technology
Clamping Technology
Gripping Systems

## Slide 3: SCHUNK Services
Engineering
Dimensioning of special plates designed to the manufacturing specifications
Development of special solutions together with the customer
FEM analysis for critical components
Testing
Endurance tests with all new developments
Abrasion checking
Measurement of accuracy
Service
Initial operation of customer´s solution
Inspection and maintenance
Repairs

## Slide 4: MAGNOS MSC-PM60D
Solid base body
Invertible AlNiCo magnets
Coil body, insulated version
Support segments
Synthetic resin grounting
Connection housing
Thread for stops
2
1
3
4
5
6
7
2
1
3
4
6
7
5

## Slide 5: MAGNOS MSC-PM62F
Solid base body
Invertible AlNiCo magnets
Coil body, insulated version
Support plate
Synthetic resin grounting
Connection housing
Workpiece stop bar
2
1
3
4
5
6
7
2
1
3
4
6
7
5

## Slide 6: MAGNOS MSC-PM15
Solid base body
Permanent magnets with different polarity
Aluminum segments
Brass segments
Support plate
Connection with hexagon socket
Workpiece stop bar
2
1
3
4
5
6
7
2
1
3
4
6
7
5

## Slide 7: MAGNOS MSC
Solid base body
Synthetic resin filling
Through-bores
KEH P control unit

## Slide 8: Variants of MAGNOS MSC
Technical data | MSC-PM60D | MSC-PM62F | MSC-PM15 | MSC-PM35
L [mm] |  |  |  | 
B [mm] |  |  |  | 
H [mm] | 71 | 81 | 52 / 60 | 68 / 78
Max. clamping force [N/cm2] | 75 | 75 | 75 | 80
Pole pitch | 5 mm + 5 mm | 3 mm + 0.8 mm | 1.5 mm + 0.8 mm | 
Number of poles |  |  |  | 10, 12, 14, 18
Connection | 4-PIN | 4-PIN |  | 
Amount of channels | 1 | 1 |  |