## Slide 1
VERO-S NSE-A3
Versatile clamping module for automated machine loading

## Slide 2: VERO-S NSE-A3
Integrated cone seal by default
Integrated monitoring
Integrated media transfer
Integrated cleaning function
Stepped flat surfaces
Positioning via short taper
Patented dual stroke system for highest pull-down forces
Turbo integrated by default
Form-fit, self-retained locking
The modules are stainless and completely sealed
All modules can be operated with a system pressure of 6 bar
General information

## Slide 3: VERO-S NSE-A3
Standard cone seal
Anti-twist protection V4
Patented dual stroke system
Turbo function
Completely sealed system
Monitoring of the clamping slide position „open condition“ and „locked condition“
Stepped flat surfaces
Integrated media transfer
1
2
3
5
6
4
7
8
Functional diagram
7
1
4
5
3
6
7
2
5
5
8
8

## Slide 4: VERO-S NSE-A3
Centering via short taper
The precise short taper centering combined with the form-fit and self-retaining locking characterizes the SCHUNK quick-change pallet system.
Locking via clamping slides
Large contact surfaces between clamping slides and clamping pin ensure a low surface pressure, resulting in a long service life.
Highlights
Cone seal integrated in the standard version
All clamping modules of the NSE-A3 series are equipped with a cone seal as standard. Due to this cone seal, the changing interface is reliably protected against the ingress of coolant, dust, and chips.

## Slide 5: VERO-S NSE-A3
Rolling friction between piston and clamping slide
In order to further increase the pull-down force, the plain bearing bushings are integrated in the piston for bearing the cylinder pin. Therefore the efficiency is increased and wear minimizes at the same time.
Integrated turbo function
In order to increase the pull-down force, the quick-change pallet module is additionally actuated with compressed air  turbo-function influences the pull-down force
Spring force
Additional force
Highlights
Stepped flat surfaces
The clamping device or the workpiece is located on stepped flat surfaces of the quick-change pallet module. This ensures clean and ideal support for transmitting high torques.
1
2
1
2

## Slide 6: VERO-S NSE-A3
Cleaning and monitoring of the flat work surface
All NSE-A3 plus clamping modules have integrated contact montitoring as standard. The contct surface is cleaned when loading the pallet.  reliable sequence
Monitoring of the clamping slide position – opened condition
Deaeration: Compressed air can escape because the clamping slide is not positioned above the bore hole.
Dynamic pressure: Compressed air cannot escape because the clamping slide is above the bore hole.
Highlights
Monitoring of the clamping slide positon – locked condition
Dynamic pressure: Compressed air cannot escape because the clamping slide is above the bore hole.
Deaeration: Compressed air can escape because the claming slide is not positioned above the bore hole.
1
2
1
2
1
2
1
2

## Slide 7: VERO-S NSE-A3
Control of the quick-change pallet system
The modules are actuated via lateral or bottom air connections.
Benefit: The module is versatile in installation.
Hermetically sealed – maintenance-free
The cover plate at the lower piston chamber seals the system off completely.
Benefit: No penetration of chips, dirt or coolant. The module is maintenance-free.
Highlights

## Slide 8: VERO-S NSE-A3
Made of stainless steel – long service life
All functional components are made of hardened stainless steel.
Pressure spring made of stainless steel
For maximum service life, all of the actuating springs are made of fatigue-free stainless steel.
Highlights

## Slide 9: VERO-S NSE-A3
Clamping stroke
Jaw fast stroke
Y-axis
X-axis
Actuation force
Force on the clamping slide
Pull-down force on the clamping pin
Fast and Clamping Stroke – the Patented Force
1
2
3
5
6
7
4
1
2
3
5
6
7
4
5
6
6

## Slide 10: VERO-S NSE-A3
Actuation force of the spring force clamping
Actuation force of the turbo function
Pull-down force of the spring force clamping
Pull-down force of the turbo function
Y-axis
X-axis
Fast and Clamping Stroke – the Patented Force
1
2
3
5
6
4
1
2
5
4
1
3
3
3
6