## Slide 1
TRIBOS Mini ER | Polygonal clamping system for Turning applications

## Slide 2: TRIBOS - Mini ER

## Slide 3: The role of the toolholders in the production process
Machine spindle
Toolholder
Tool
Workpiece
Vibration system

## Slide 4: Funktionsprinzip TRIBOS Technologie
1. Clamping diameter polygon-similar
By using the TRIBOS SVP clamping devices and the matching pressure actuation, the polygonal clamping diameter of the toolholder becomes round.
2. Clamping diameter becomes round
The tool shank is now easy to insert.
3. Inserting the tool shank
If the pressure on the clamping diameter eases off, then it will assume its polygonal shape again.
4. Tool clamped
The inserted tool shank is process-reliably clamped at a high repeat accuracy.

## Slide 5: Polygonspanntechnik
Patented TRIBOS polygonal clamping technology for your lathe
Process reliability
direct clamping of smallest shanks.
Slim interfering contour
for machining in areas which are difficult to access.
Rotationally symmetrical design
for highest speeds and precise shape and position tolerances during filigree machining operations.
Maximum stability
for longer service life of turning tools.

## Slide 6: Run-out accuracy
Absolute- & Repeat accuracy
Maximum measured run-out errors (bar) and span of individual measurements (line)
Concentricity deviation
75% lower dispersion of run-out repeat accuracy with
30% lower absolute accuracy

## Slide 7: Stability comparison
Conclusion: with the TRIBOS ER, the stable speeds are very clearly pronounced. In these areas, the productivity can be increased compared to the conv. By an increased infeed

## Slide 8: Set-up times
20 sec. parallel main time
0,02mm unclamped length
vs.
Tool change in machine room „under oil“
Estimate the unclamping length with the caliper gauge
Clamping force = Depending on the type of man

## Slide 9: Advantages of TRIBOS - Mini ER
Run-out accuracy < 0,01 mm at 2,5 x D
Compatible with all conventional ER clamping nuts
Advantages opposite ER collet chucks:
Higher stability
Higher tool change accuracy
Produced bore shape is more accurate
Setting times / ease of operation

## Slide 10: Examples: Clamping nuts
Fits into any collet chucks of the most popular manufacturers
through optimization of the interface (ER) and contact surfaces.
No new chucks needed!!!

## Slide 11: Machines and workspace
Examples:
Citizen
STAR
Index / Traub
Tornos
Maier
TRIBOS - Mini ER
For driven as well as fixed spindles
With ER interface.
BAZ
Robotics
Swiss type lathe
Lathes
etc.

## Slide 12: Unstable clamping of the tools for the purpose of accessibility
Due to large mold relief

## Slide 13: Solution: TRIBOS - MINI ER
Distance from spindle to turret
Short clamping of the tools
Stable clamping
Less interference contour
Less vibrations
High run-out properties
Repeat accuracy
Longer service life
Universally applicable
Fast set-up times
Less machine downtime
Low costs

## Slide 14: Dimensions TRIBOS - Mini ER
Mounting
Clamping
diameter
with
without

## Slide 15: TRIBOS-ER blank concept
Prefabricated blanks in stock
Different interfaces in ER
Special diameters possible
Faster availability