## Slide 1
Product presentation
RM-W
Vane swivel unit

## Slide 2
Vane swivel unit
Vane swivel unit with high torque for fast rotation tasks

## Slide 3
Modular. Compact. Flexible.

## Slide 4
Principle of function
Stop lever
3
Mounting pattern
2
Drive
1
Robust bearing
4
End position damping
5
The drive is pneumatic and based on the rotor principle. The rotary table is very robust due to axial and radial bearings.
Swivel angle adjustment
6
Functional description

## Slide 5
Advantages – Your benefits
Stop system with integrated fine adjustment of rotation angle for sensitive adjustment of end positions
Direct drive of the rotary table with integrated rotor cylinder ensured highest repeat accuracies
Very compact design for minimal interfering contours
Solid axial and radial bearings for the rotary table for high load bearing capacities in all directions
End-position monitoring with optional standardized monitoring sets
Integrated shock absorbers with adjustable absorption characteristics for optimal damping
Standardized mounting bores for numerous combinations with other components from the modular system

## Slide 6
Technical data
Technical data overview
Size | Angle of rotation | Torque | Weight | Repeat accuracy
 | [°] | [Nm] | [kg] | [°] |  |  | 
50 | 90 .. 180 | 0.7 | 0.65 | 0.044
110 | 90 .. 180 | 1.95 | 1.12 | 0.036
200 | 90 .. 180 | 4 | 2.1 | 0.044
310 | 90 .. 180 | 22 | 8.3 | 0.046