## Slide 1
TANDEM KSP3
Compact, pneumatically actuated powerhouses with an enormously wide range of variants in the standard version

## Slide 2
Chuck Jaws
VERO-S
Toolholders
Hydraulic Expansion Technology
Stationary Workholding
KONTEC
TANDEM
ROTA
MAGNOS
Lathe Chucks
Clamping Technology
Gripping Systems
Tombstones

## Slide 3: TANDEM 3
Increasing relevance of the set-up process
Challenges

## Slide 4: TANDEM KSP3
Enormous diversity of variants
Force amplification for O.D. clamping via spring force
Patented monitoring of the base jaw position via dynamic pressure
Workpiece presence control through the base jaw
Inductive jaw monitoring
Precision wedge hook clamping force block for top-quality demands
Square design with ideal outside contour
High efficiency of the wedge hook system
Base jaws with tongue and groove and fine serration as a dual interface as standard
Optimal jaw support due to the use of a very long base jaw guidance
All functional parts are ground and hardened
Advantages – Your benefits

## Slide 5: TANDEM 3 Lead Vises
Way above 300 standard versions
 | Pneumatic KSP3 |  |  |  |  | 
Standard stroke |  |  |  |  |  | 
 | KSP3 |  |  |  |  | 
 | Size | 64 | 100 | 140 | 160 | 250
 | Jaw stroke (mm) | 2 | 2 | 3 | 3 | 5
 | Number of versions | 8 | 12 | 12 | 12 | 12
L | Pneumatic KSP3-LH |  |  |  |  | 
Long stroke |  |  |  |  |  | 
 | KSP3-LH |  |  |  |  | 
 | Size | 64 | 100 | 140 | 160 | 250
 | Jaw stroke (mm) | 4 | 6 | 7 | 8 | 15
 | Number of versions | 8 | 12 | 12 | 12 | 12
 | Pneumatic KSP3-F |  |  |  |  | 
With fixed jaw |  |  |  |  |  | 
 | KSP3-F |  |  |  |  | 
 | Size | 64 | 100 | 140 | 160 | 250
 | Jaw stroke (mm) | 4 | 4 | 6 | 6 | 10
 | Number of versions | 8 | 8 | 8 | 8 | 8

## Slide 6: TANDEM 3
Standard stroke
For the standard stroke, a high force transmission is achieved via a small wedge angle.
Advantage: High clamping forces.
Long stroke (-LH)
For a long stroke, a larger jaw stroke is achieved via an increased wedge angle. Due to the enlarged angle, however, the LH version achieves a lower clamping force than the standard stroke version. Advantage: Longer jaw stroke.
With fixed jaw (-F)
One chuck jaw is screwed immovably to the body. The force transmission takes place via the movable jaw.
Fixed clamping jaw
Movable clamping jaws
1
2
1
2
Variants

## Slide 7: TANDEM KSP3
Clamping force and jaw stroke
Chart: Clamping force
| 64 | 100 | 140 | 160 | 250
Standard stroke | 4.5 | 18 | 30 | 45 | 55
Long stroke | 2.3 | 8 | 15 | 20 | 20
With fixed jaw | 4.5 | 18 | 30 | 45 | 55
Chart: Jaw stroke
| 64 | 100 | 140 | 160 | 250
Standard stroke | 2 | 2 | 3 | 3 | 5
Long stroke | 4 | 6 | 7 | 8 | 15
With fixed jaw | 4 | 4 | 6 | 6 | 10

## Slide 8: TANDEM KSP3
Wedge hook drive
Hardened and extremely rigid base body
Sophisticated greasing system
Long jaw guidance
Low height
Improved design which is insensitive to dirt
Standard jaw interface
Ideal outside contour
Control of the clamping force block
Piston guided in the body
Greasing channels in the cover plate
Fitting screws available as an option
1
2
3
5
6
4
7
8
Functional diagram
9
10
11
12
7
4
12
11
8
6
1
10
9
9
5
3
2

## Slide 9: TANDEM KSP3
Clamping force depending on the actuation pressure
The clamping force increases in direct proportion to the incerease in actuation pressure. The minimum air pressure should not drop below 2 bar during this process.
Clamping force
Actuation pressure
Chip-repellent design
The special design of the base jaw and cover strip prevents chips becoming permanently lodged. During the clamping process, the chips are pushed from the base jaw by the incline of the cover strip.
Highlights
Cover plugs for the mounting screws
All four mounting screws are sealed with anodized aluminium plugs. Chip build-up is therefore completely eliminated in advance.
1
2
1
2

## Slide 10: TANDEM KSP3
Alignment edge
An alignment edge is recessed into the side of the clamping force block. It extends parallel to the jaw guidance and enables an exact alignment of the vises to the machine table.
Coolant drainage hole
All clamping force blocks are equipped with a coolant drainage hole. This allows penetrated coolant to be drained to the outside. The drainage hole is sealed with a sintered filter to prevent the entry of chips.
Highlights
Greasing system
Manual greasing: A grease gun is used to supply all friction surfaces evenly.
Central greasing: The connections on the base side are used to supply all friction surfaces evenly with grease.
1
2
2
1
2

## Slide 11: TANDEM KSP3
Base plates
Base plates offer several integrated options for mounting the clamping force blocks on the machine table.
Fastening via quick-change pallet system
Fastening via cylindrical clamps
Mounting via T-nuts
1
2
3
1
2
3

## Slide 12: TANDEM KSP3
Jig-produced positioning bores (-Z)
In order to position several clamping force blocks very accurately in relation to one another on the clamping devices, jig-produced positioning bores are integrated in the Z-version.
Positioning bore
Clamping force amplification for O.D. clamping (-AS)
Spring assemblies that are integrated in the vise, increase the clamping force of the pneumatic pressure by up to 20% during O.D. clamping.  This increases the application possibilities.
Stainless, fatigue-resistant pressure springs
Standardized equipment versions
1
1
1
1
1

## Slide 13: TANDEM KSP3
Pneumatic monitoring (-PM)
The PM version of the TANDEM 3 generation includes several features. The base jaw positions can be queried via dynamic pressure.
Patented monitoring of the base jaw position
Air transfer
Inductive jaw monitoring (-IM)
Two inductive proximity switches in the base jaw‘s recesses enable monitoring of the base jaw positions. This monitoring is particularly suitable for fully automated machining processes.
Standardized equipment versions
1
2
1
2

## Slide 14: TANDEM KSP3
Documents
Catalog chapter (link follows)
Homepage (link follows)

## Slide 15
TANDEM System jaws and top jaws
Maximum flexibility due to the modular system consisting of supporting jaws and a large selection of top jaws

## Slide 16: TANDEM Jaws
Individually adjustable for new clamping tasks
Supporting jaw system
Large modular system of matching top jaws
Advantages – Your benefits

## Slide 17: TANDEM 3 Jaws
Top jaw blanks |  | 
Mounting: Via tongue and groove | Mounting: Via fine serrations 1,5 x 60° | 
KTR / KTR-H | STR / STR-H | STR-S
Supporting Jaw and SCHUNK Jaw Program | 
TBA-D | Clamping jaws
3-axis jaws
S3A-G5
5-axis jaws
S5A-G5

## Slide 18: TANDEM 3 Jaws
KTR/KTR-H |  |  |  | 
Description | ID | Length [mm] | Width [mm] | Height [mm]
KTR 64 | 0402120 | 28,5 | 34 | 16
KTR 100 | 0402121 | 47 | 55 | 25
KTR 140 | 1349707 | 65 | 70 | 35
KTR 160 | 0402122 | 76 | 80 | 40
KTR 250 | 0402123 | 120 | 125 | 50
KTR-H 64 | 0402220 | 28,5 | 34 | 35
KTR-H 100 | 0402221 | 47 | 55 | 48
KTR-H 140 | 1349708 | 65 | 70 | 70
KTR-H 160 | 0402222 | 76 | 80 | 77,5
KTR-H 250 | 0402223 | 120 | 125 | 100
STR-S |  |  |  | 
Description | ID | Length [mm] | Width [mm] | Height [mm]
STR-S 64 | 0402110 | 25 | 34 | 20
STR-S 100 | 0402111 | 42 | 55 | 25
STR-S 140 | 1349712 | 55 | 70 | 38
STR-S 160 | 0402112 | 60 | 80 | 40
STR-S 250 | 0402113 | 90 | 125 | 50
STR/STR-H |  |  |  | 
Description | ID | Length [mm] | Width [mm] | Height [mm]
STR 64 | 0402100 | 28,5 | 34 | 20
STR 100 | 0402101 | 42 | 55 | 25
STR 140 | 1349709 | 62 | 70 | 35
STR 160 | 0402102 | 66 | 80 | 40
STR 250 | 0402103 | 108 | 125 | 50
STR-H 64 | 0402200 | 28,5 | 34 | 35
STR-H 100 | 0402201 | 47 | 55 | 50
STR-H 140 | 1349710 | 70 | 70 | 70
STR-H 160 | 0402202 | 76 | 80 | 80
STR-H 250 | 0402203 | 120 | 125 | 100
TBA-D |  |  |  | 
ID | Interface | Length [mm] | Width [mm] | Height [mm]
0402294 | W-65-1 | 63,6 | 65 | 34
1349715 | W-90-1 | 83 | 90 | 53
0402295 | W-100-1 | 92,8 | 100 | 53
0402296 | W-125-1 | 113,4 | 125 | 63
S3A-G5 |  |  | 
ID | Length [mm] | Width [mm] | Height [mm]
1471165 | 25,5 | 34 | 22
1471166 | 36 | 50 | 26
1471167 | 48 | 69 | 31
1471168 | 48 | 80 | 31
1471187 | 66 | 125 | 40
S5A-G5 | Length [mm] | Width [mm] | Height [mm]
ID | Length [mm] | Width [mm] | Height [mm]
1471189 | 25,5 | 34 | 40
1471190 | 36 | 50 | 50
1471197 | 49,5 | 69 | 50
1471198 | 58,5 | 80 | 50
1471200 | 72 | 125 | 110

## Slide 19
ABP-h plus
Base plates for KSP plus clamping force blocks

## Slide 20: ABP-h plus Base Plates
VERO-S interface
Pneumatic connection from three sides
Versatile in use
Manually operable pneumatic valves
Integrated pressure maintenance valve
Media transfer at the base
Advantages – Your benefits

## Slide 21: ABP-h plus Base Plates
TANDEM KSP plus clamping force block
Pneumatic connection from three sides
Integrated pressure gauge
Manually operable pneumatic valves
VERO-S interfacee
Media transfer at the base
1
2
3
5
6
4
Functional diagram
1
2
3
2
2
4
5
6

## Slide 22
KSL 3
Base plates for KSP3 and KSH3 clamping force blocks

## Slide 23: KSL3 base plates
Vero-S interface
Prepared for cylindrical clamps and T-nuts
Advantages – Your benefits