## Slide 1
TANDEM PGS3
Perfection and reliabilty for simple, automated machine loading

## Slide 2
Chuck Jaws
VERO-S
Toolholders
Hydraulic Expansion Technology
Stationary Workholding
KONTEC
TANDEM
ROTA
MAGNOS
Lathe Chucks
Clamping Technology
Gripping Systems
Tombstones

## Slide 3: TANDEM 3
Increasing relevance of the set-up process
Challenges

## Slide 4: TANDEM PGS3
Integrated console plate
Ready for immediate use
Base body made of light aluminium
Low height
Optimized outside contour
Cubic design
High efficiency of the wedge hook system
Precision wedge hook clamping force block for top-quality demands
Optimal jaw support due to the use of a very long base jaw guidance
Advantages – Your benefits

## Slide 5: TANDEM 3 Lead Vises
Way above 300 standard versions
 | Pneumatic PGS3 |  | 
Standard stroke |  |  | 
 | PGS3 |  | 
 | Size | 100 | 140
 | Jaw stroke (mm) | 2 | 3
 | Number of versions | 1 | 1
 | Pneumatic PGS3-LH |  | 
Long stroke |  |  | 
 | PGS3-LH |  | 
 | Size | 100 | 140
 | Jaw stroke (mm) | 6 | 7
 | Number of versions | 1 | 1
The TANDEM PGS3 clamping force block
A strong combination partner for light machining and simple automation tasks.

## Slide 6: TANDEM 3
Standard stroke
For the standard stroke, a high force transmission is achieved via a small wedge angle.
Advantage: High clamping forces.
Long stroke (-LH)
For a long stroke, a larger jaw stroke is achieved via an increased wedge angle. Due to the enlarged angle, however, the LH version achieves a lower clamping force than the standard stroke version. Advantage: Longer jaw stroke.
With fixed jaw (-F)
One chuck jaw is screwed immovably to the body. The force transmission takes place via the movable jaw.
Fixed clamping jaw
Movable clamping jaws
1
2
1
2
Variants

## Slide 7: TANDEM PGS3
Clamping force and jaw stroke
Chart: Clamping force
| 100 | 140
Standard stroke | 10 | 17
Long stroke | 4.5 | 8.5
Chart: Jaw stroke
| 100 | 140
Standard stroke | 2 | 3
Long stroke | 6 | 7

## Slide 8: TANDEM PGS3
Wedge hook drive
Integrated console plate
Long jaw guidance
Compact design
Improved design which is insensitive to dirt
Jaw interface with tongue and groove
Simple lateral control of the clamping force block
Piston guided in the body
1
2
3
5
6
4
7
8
Functional diagram
6
5
8
4
1
7
3
2
7

## Slide 9: TANDEM PGS3
Standard stroke
For the standard stroke, a high force transmission is achieved via a small wedge angle.
Benefit: The PGS3 has high clamping forces.
Highlights
Long stroke
For a long stroke, a larger jaw stroke is achieved via an increased wedge angle. Due to the enlarged angle, however, the LH-version achieves a lower clamping force than the standard stroke version.
Advantage: Longer jaw stroke.
Pneumatic drive
Clamping and loosening is performed via a double-acting pneumatic cylinder with permanent pressure.

## Slide 10: TANDEM PGS3
Chip-repellent design
The special design of the base jaw and cover strip prevents chips becoming permanently lodged. During the clamping process, the chips are pushed from the base jaw by the incline of the cover strip.
Highlights
Mounting options
The clamping force block can be used for minimizing the set-up time. It can be placed on the VERO-S NSE3 with anti-twist protection using the existing VERO-S interface.
Fastening via quick-change pallet system
Fastening via cylindrical clamps
Mounting via T-nuts
Easy commissioning
Quickly and easy commissioning. Due to the integrated console plate, the clamping force block can be mounted directly on the machine table or quick-change pallet system. The lateral air connections allow the vise to be controlled directly with a 5/3-way valve.
1
2
3

## Slide 11: TANDEM PGS3
Documents
Catalog chapter
Homepage

## Slide 12
TANDEM PGS3 top jaws

## Slide 13: TANDEM PGS3 Jaws
Top jaw blanks
Mounting: Via tongue and groove
KTR/KTR-H
KTR/KTR-H |  |  |  | 
Description | ID | Length [mm] | Width [mm] | Height [mm]
KTR 100 | 0402121 | 47 | 55 | 25
KTR 140 | 1349707 | 65 | 70 | 35
KTR-H 100 | 1349708 | 47 | 55 | 48
KTR-H 140 | 0402222 | 65 | 70 | 70