## Slide 1
Product presentation
HLM
Stroke module

## Slide 2
Stroke module
Stroke module with optimized length, with pneumatic drive and pre-loaded crossed roller bearings, free from play

## Slide 3
Modular. Compact. Loadable.

## Slide 4
Principle of function
Mounting pattern
3
Drive
2
Cross roller guidance
1
Damping adjustment
4
Module fastening
5
The linear sliding movement is facilitated by a drive piston that is actuated with compressed air.
Functional description

## Slide 5
Advantages – Your benefits
Crossed roller guide design and solid design ensured high load bearing capacities and end position accuracy in all installation positions
Pretensioned junction rollers That means absolutely scope-free
High basic load ratings in all load directions
Standardized fixing bores and connection dimensions identical for LM series for numerous combinations with other components from the modular system
Shock absorbers and proximity switches integrated in the projecting surfaces for vibration-free movements and end position monitoring
Rod lock by means of clamping cartridge for safety in case of emergency stops

## Slide 6
Technical data
Technical data overview
Size | Stroke | extend force | retracted force | Weight
 | [mm] | [N] | [N] | [kg] |  |  | 
25 | 25 .. 59 | 67 | 50 | 0.5 .. 0.66
50 | 25 .. 100 | 120 | 103 | 0.85 .. 1.39
100 | 25 .. 150 | 294 | 247 | 1.62 .. 3.24
200 | 50 .. 150 | 482 | 415 | 3.42 .. 5.64