## Slide 1
MTB Applications kits
2022-03-18 | Benjamin Schell

## Slide 2: Agenda
Target application
Why automate?
Target customers and their challenges
Product presentation
Competitive comparison
Timeline, Availibility, Pricing

## Slide 3: The world of automation solutions for machining applications is huge. Where do we set our focus?
Partly automated CNC machining applications on lathes or milling machines with machine loading and unloading by a robot/cobot.
High-Mix-Low-Volume (Highest flexibility, different workpieces and tasks, low output)
Simple cutting machines (e.g. 3-axis standard machining)
Automation costs in the range of approx. 25 Tsd€ to 100 Tsd€
Use of low-cost easy-to-use robots/cobots (cheap purchase, simple programming)
Either self-implemented (DIY) or together with a small integrator

## Slide 4: Sequence of automated machine loading
Grip raw material
Open machine door
Open clamping device
Remove chips and cooling lubricant
Remove finished part from clamping device
Insert raw material into clamping device and close it
Close door
Start machining cycle
Source: Robotiq
Other important basics:
Machine safety, risk assessment, space conditions, handshake between machine and robot controller, raw material feeding, finished part storage

## Slide 5: Why automate?
Increase productivity
Increase the capacity of employees for demanding tasks and counteract against the shortage of available skilled workers
Increase machine output by e.g. have the robot taken over the third shift
Increase quality
Errors, e.g. when clamping the workpiece, are minimized
Reduce employee workload
Reduce physical load of employees (humans must bend less into the machine)
Reduce monotone work of employees (loading and unloading is always the same activity)
Reduce risk of injury (due to chips, sharp edges and cooling lubricant)

## Slide 6: Who is our target customer and what are their challenges?
Who is our target customer?
Operator/Owner of the cutting machine (end user)
What challenges does our target customer have?
Request to increase productivity, improve quality and reduce employee workloads
Little to no automation know-how
Infinite availability of individual automation solutions
Limited availability of simple and flexible "Plug & Work" solutions (esp. in the area of grippers)
Unclear whether an automation solution is it worth (ROI)
As a result of the challenges, there is general indecision on the subject of automation

## Slide 7: How can SCHUNK support?
1. Single Gripper Perfect for use in tight spaces.
2. Double Gripper Loading and unloading in just one cycle. Increases machine productivity.
3. Clamping Vise Reliable holding of the workpiece during machining.
The MTB application kits enable fast and easy implementation of automated machine loading. They take over the important key role of workpiece handling and workpiece clamping while seamlessly integrating into the machine environment.

## Slide 8: Single gripper and double gripper in detail
Single gripper
Double gripper
Sealed valve box (IP67) with status LED
Mechanical adapter for robot connection
M12 plug for electrical connection
Push-in fitting for compressed air connection
Pre-assembled blow-off nozzle
Universal intermediate jaw UZB (available as accessory)
Universal top jaw AUB JGP-P (available as accessory)
 |  | MTB-SG-JGP 80-1 | MTB-SG-JGP 100-1 | MTB-DG-JGP 64-1 | MTB-DG-JGP 80-1
Stroke per jaw | [mm] | 8 | 10 | 6 | 8
Closing/opening force | [N] | 550/610 | 870/930 | 350/375 | 550/610
Recommended workpiece weight | [kg] | 2,75 | 4,35 | 1,75 | 2,75
Mass | [kg] | 0,99 | 1,38 | 1,62 | 2,1

## Slide 9: Single gripper and double gripper in detail
1. T-slot guidance loadable, robust base jaw guidance for extremely long gripper fingers
2. Base Jaw for the connection of workpiece-specific gripper fingers
4. Housing is weight-optimized due to the use of high-strength aluminum alloy
5. Centering and mounting possibilities for universal assembly of the gripper
6. Wedge-hook design for high force transmission and centric gripping
3. Sensor system Proximity switch can be assembled without mounting kit
7. Piston maximum force through maximum surface of drive piston
Functional description JGP-P

## Slide 10: What accessories are available for the grippers?
Universal intermediate jaw UZB
Fast, tool-free and safe horizontal adjustment of top jaws
Changeover to new workpiece size in a short time
BSWS-M quick-change jaw system without tools
Fast, manual and tool-free change of jaws
Changeover to a new workpiece geometry
Universal top jaws JGP-P
Usable for different clamping ranges
Gripping of cylindrical or square workpieces

## Slide 11: Clamping vise in detail
Power clamping vise TANDEM PGS3
Integrated flange for direct mounting on the machine table
Sealed valve box with status LED prepared for field mounting
Push-in fitting for compressed air connection
M12 plug for electrical connection
Top jaw blanks KTR-H for individual adjustment (available as accessories)

## Slide 12: Clamping vise in detail
Wedge hook drive
Integrated console plate
Long jaw guidance
Compact design
Improved design which is insensitive to dirt
Jaw interface with tongue and groove
Simple lateral control of the clamping force block
Piston guided in the body
1
2
3
5
6
4
7
8
6
5
8
4
1
7
3
2
7
Functional description TANDEM PGS3

## Slide 13: What accessories are available for the clamping vise?
Top jaw blanks KTR-H
with cross offset and prefabricated mounting holes for reworking by the customer
For further accessories such as clamping bolts (e.g. for zero point clamping systems) see catalog page PGS3.

## Slide 14: Which robots are supported?
e-Series UR5e
UR10e
UR16e
GoFa (CRB15000)
CRX-Series
CRX-10iA
CRX-10iA/L
TM5
TM12
TM14
TM5
TM12
TM14
A-Serie
M-Serie
H-Serie
Component
Robot Connection Kit
Mechanical Adaption
Software Integration
Electric Adaption

## Slide 15: Robot Connection Kits
The combination of a suitable connection package and the used robot enables seamless interaction between the component and the robot.
Scope of delivery of the gripper connection package:
Robot adapter plate, Velcro stripes for attaching cables and hoses, connection cable (5m)*, pneumatic hose (10m), USB stick (empty), leaflet with link to MTB download area
Scope of delivery connection package power clamp:
Connecting cable (5m)*, pneumatic hose (20m), tension spring for hose protection, USB stick (empty), leaflet with link to MTB download area

## Slide 16: Functions of the robot plug-ins (e.g. Universal Robots)
Configuration of the input and output configuration
Teach switching positions MMS-PI2
Activate blow-off nozzle (time adjustable)
closing/opening of force clamps and grippers
Activate configuration (Enable)
Small example program available per robot manufacturer (will be described in the BA)

## Slide 17: Competitive comparison
Biggest pressure comes from Robotiq and OnRobot with electric grippers!
Are there other competitors?
Zimmer GPP5000, Weiss Gripkit Pro, PHD PneuConnect, Air Vise, EMI
MTB Double Gripper with UZB and Fingers 3876 €
Robotiq Machine Tending Kit approx. 8000 €
Air Vise UR+ Package (without jaws and valves) approx. 1335 €
OnRobot 2FG7 Double Gripper approx. 8840 €
MTB Vise PGS3 (with jaws and valves) ca. 2615 €
EMI Dual Gripper Configuration (with Fingers, without Valves) ca. 3740 €
How can we argue against it?
Price
Reliability/robustness
Application specialization (blow-off nozzle, gripping clamping synergy)
Robot integration

## Slide 18: Pricing
ID | Description | Type | List Price
1490825 | MTB SG-JGP-P 80-1 | Single Gripper Bundle JGP 80-1 | 1.600 €
1490827 | MTB SG-JGP-P 100-1 | Single Gripper Bundle JGP 100-1 | 1.670 €
1490830 | MTB DG-JGP-P 64-1 | Double Gripper Bundle JGP 64-1 | 2.460 €
1490832 | MTB DG-JGP-P 80-1 | Double Gripper Bundle JGP 80-1 | 2.550 €
1490833 | MTB KS-PGS3 100 | Vise Bundle PGS3-LH 100 | 2.350 €
1490834 | MTB CNK-SG/DG-RF1 | Gripper Connection Kit | 230 €
1490839 | MTB CNK-KS-RF1 | Vise Connection Kit | 110 €
1490841 | MTB AUB-JGP-P 64/15 | Standard Finger Set JGP-P 64 | 235 €
1490846 | MTB AUB-JGP-P 80/25 | Standard Finger Set JGP-P 80 | 250 €
1490854 | MTB AUB-JGP-P 100/32 | Standard Finger Set JGP-P 100 | 290 €
0402221 | MTB KTR-H 100 | Tandem KTR-H 100 | 155 €
0300042 | UZB 64 | Intermediate jaw UZB 64 (one piece) | 179 €
0300043 | UZB 80 | Intermediate jaw UZB 80 (one piece) | 197 €
0300044 | UZB 100 | Intermediate jaw UZB 100 (one piece) | 218 €

## Slide 19: Contact persons
Team Mechatronic

## Slide 20
Questions?