## Slide 1
RAPIDO-A2
SCHUNK automated quick jaw change

## Slide 2: RAPIDO-A2
Why automated jaw change?
Time
Variants
Time
Demand
Time
Global competition
Flexibility, increase in productivity and efficiency

## Slide 3: RAPIDO-A2
Your advantage through automated jaw change:
Increased productivity thanks to higher output
Consistently high quality thanks to automated processes
Competitiveness through maximum flexibility and shortest response time
COMPETITVE ADVANTAGE

## Slide 4: RAPIDO-A2
Standard lathe
Automation cell with change gripper
Jaw deposit and workpiece supply
Cleaning concept for jaws and interfaces
Integration readiness, or integrator
Solid machining processes
Prerequisites for automated jaw change

## Slide 5: RAPIDO-A2
Automated jaw change

## Slide 6: RAPIDO-A2
Arrangement of the components:
Lathe chuck
Base jaw
Top jaw internal/external clamping
Unlocking top jaw
3
4
2
1
Components: Chuck
Internal clamping
External clamping

## Slide 7: RAPIDO-A2
Components: Chuck
ROTA NCF plus with integrated RAPIDO A2 interface and through hole
Mechanical pressure bolt
Mechanical locking bolt

## Slide 8: RAPIDO-A2
Components: Top jaw
Cones for gripper
Limit line max. permissible unscrewing of top jaw
Hole for RFID chip
Locking hole
Chip guard
Surface for power transmission
Clearance insertion aid
Fitting surface
Support surface

## Slide 9: RAPIDO-A2
Actuate pressure bolt
Locking bolt retracts
Do not actuate pressure bolt
Reset by spring force
Function: mechanical locking bolt
Motion and force transmission over inclined
surfaces

## Slide 10: RAPIDO-A2
1,5 mm
1,5 mm
0 mm
0 mm
Replace top jaw,
Pre-positioning (see dimensions)
Function: Joining external clamping
Place top jaw
on base jaw
Engage top jaw
into base jaw

## Slide 11: RAPIDO-A2
Function: Detail Joining External Clamping
Fit clearance, responsible for concentricity and repeatability
0,005mm
0,035mm
0,01mm
0,04mm
1 mm
Clearance in top jaw
Engaging top jaw into base jaw
Fitting surface base jaw
Fit produced
Insertion aid

## Slide 12: RAPIDO-A2
1,5 mm
1,5 mm
0 mm
0 mm
Replace top jaw,
Pre-positioning (see dimensions)
Function: Joining internal clamping
Place top jaw
on base jaw
Engage top jaw
into base jaw

## Slide 13: RAPIDO-A2
Function: Power transmission
Workpiece
Top jaw
Workpiece stop
Base jaw
Two-dimensional force transmission from top jaw to base jaw (red area), responsible for repeat accuracy
Flat support on base jaw (blue area)
Introduced clamping force
Acting clamping force
Support

## Slide 14: RAPIDO-A2
Components: Gripping unit

## Slide 15: RAPIDO-A2
Components: Gripping unit
RFID Reader
RFID Chip
2x sensor for gripper sensing
Piston stroke sensing
2x sensor for cylinder position

## Slide 16: RAPIDO-A2
Components: Gripping unit
M12 8-pole
Sensor distributor
Optical sensor for
- Interrogation of pressure pin
- Interrogation top jaw

## Slide 17: RAPIDO-A2
Components: Gripper unit
Gripper PGN-plus-P 125
Gripper fingers
with gripper cones
Actuating cylinder pneumatic

## Slide 18: RAPIDO-A2
Components: Gripping unit
Sensing pressure bolt extended
Sensing top jaw available

## Slide 19: RAPIDO-A2
Required distance X:
Size 215-315:
55mm
Size 400:
65mm
Components: Jaw and gripper rest
Jaw rest
Gripper for jaw change
Gripper for workpiece change
Griper rest
X

## Slide 20: RAPIDO-A2
Components: Jaw and gripper rest
lateral guide Jaw rest
Hanging in deposit by means of hooks of the top jaw

## Slide 21: RAPIDO-A2
Components: Jaw and gripper rest
Jaw deposit optionally
in different sizes

## Slide 22: RAPIDO-A2
Components: Gripping unit
Interface by customer:
M23 connector 19-pin with bayonet lock for sensor signals
of the gripping unit and the changing system.
M12 connector 4-pin for the RFID reader
7 x pneumatic screw connection G1/8" for hose diameter 6x1
  Quick-change unit (SWS) open
  Quick-change unit (SWS) close
  Gripper open
  Gripper close
  Actuating cylinder open
  Actuating cylinder close
  Cleaning jet
Signals Gripping unit:
Gripper open
Workpiece gripped
Cylinder extended
Cylinder retracted
Optical sensor signal

## Slide 23: RAPIDO-A2
Function: Joining and Removal
Actuating the actuating pin and removing the top jaw
Join the top jaw and Sensing pressure bolt extended

## Slide 24: RAPIDO-A2
Limits of the system
Compliance with the defined limits is essential for the function and process reliability of the automated quick jaw change.
The most important factors are:
Clamping force
RPM
Feeding accuracy Robot
Cleaness of the change-over interfaces

## Slide 25: RAPIDO-A2
Limits of the system
Jaw interface must
be free of chips

## Slide 26: RAPIDO-A2
Function: Clean

## Slide 27: RAPIDO-A2
Technical data