## Slide 1
PGL-plus-P
The world's first pneumatic gripper with certified safe gripping force maintenance

## Slide 2: Pneumatic universal gripper PGL-plus-P World's first
Certified, safe gripping force maintenance
PL-d, Kat. 3
integrated sensor
Detection via IO-Link
Double stroke per jaw
Compared to the PGN-plus-P with comparable gripping force
Basic version with IP 64
Metallic encapsulation all around and additional sealing at the base jaws
SCHUNK multi-tooth guidance
Proven and robust

## Slide 3: Pneumatic universal gripper PGL-plus-P Overview of sizes and technical data
size | stroke/ jaw | gripping force | max. finger length
PGL-plus-P 10 | 10 mm | 220 N | 100 mm
PGL-plus-P 13 | 13 mm | 350 N | 125 mm
PGL-plus-P 16 | 16 mm | 550 N | 160 mm
PGL-plus-P 20 | 20 mm | 870 N | 200 mm
PGL-plus-P 25 | 25 mm | 1300 N | 245 mm

## Slide 4
Pneumatic universal gripper PGL-plus-P Functional description
1. Base jaw with standardized screw-on mounting pattern for adapting the workpiece-specific gripper fingers. Loss-proof centering sleeves cannot be lost when the fingers are changed.
2. multi-tooth guidance Maximum service life due to lubricant pockets in the robust multi-tooth guidance, and absorption of high
forces and torques by means of the large guidance support
4. Kinematics The pinion-rack kinematics synchronize the base jaws and ensures centric gripping
3. Drive connection Direct power transmission of the piston to the gripper fingers via a robust driver connection.
5. Drive Maximum force generation by two oval pneumatic pistons
6. Dust cover The whole gripper is metal-encapsulated all around and additionally sealed with a lip seal at the base jaws, so that it can be used universally, even in dirty environments.

## Slide 5: Pneumatic universal gripper PGL-plus-P One gripper - All applications
external sensors – inductive proximity switch
external sensors – Magnetic switch
16/20/25
10/13
certified safe gripping force maintenance
Precision version
Conventional gripping force maintenance
IP protection class 64
and H1 grease
integrated in the Baisis version
integrated sensor – IO-Link
High temperature version

## Slide 6
One sensor for all applications –
Simple. More compact. More robust.
Position monitoring over the whole stroke
Finally no more external sensors
Pneumatic universal gripper PGL-plus-P integrated sensor - IO-Link

## Slide 7
Pneumatic universal gripper PGL-plus-P integrated sensor - IO-Link
Unique selling points
Higher accuracy
as external sensors, thus fine workpiece differentiation possible
Less dirt-sensitive
compared to external sensors and therefore less sensitive to interference
different modes programmable
  the right sensor setting for all applications
Preassembled unit
simplification of the selection, design, procurement, and assembly process
Easy integration and flexible use

## Slide 8: Pneumatic universal gripper PGL-plus-P gripping force maintenance
State of the art
Gripper with SDV-P
Gripper with conventional gripping force maintenance

## Slide 9: Pneumatic universal gripper PGL-plus-P gripping force maintenance
7. Gripping force maintenance via spring The conventional gripping force maintenance via spring ensures a minimum gripping force even in the case of pressure loss.
1. Base jaw with standardized screw-on mounting pattern for adapting the workpiece-specific gripper fingers. Loss-proof centering sleeves cannot be lost when the fingers are changed.
2. multi-tooth guidance Maximum service life due to lubricant pockets in the robust multi-tooth guidance, and absorption of high
forces and torques by means of the large guidance support
4. Kinematics The pinion-rack kinematics synchronize the base jaws and ensures centric gripping
3. Drive connection Direct power transmission of the piston to the gripper fingers via a robust driver connection.
5. Drive Maximum force generation by two oval pneumatic pistons
6. Dust cover The whole gripper is metal-encapsulated all around and additionally sealed with a lip seal at the base jaws, so that it can be used universally, even in dirty environments.

## Slide 10: Pneumatic universal gripper PGL-plus-P certified safe gripping force maintenance
PGL-plus-P – The world's first pneumatic gripper with certified safe gripping force maintenance
World's first
GripGuard

## Slide 11: Pneumatic universal gripper PGL-plus-P certified safe gripping force maintenance
Unique selling
certified and safe (PL-d, Kat. 3)
Time and cost savings in the risk analysis of the plant
no uncontrolled jaw movement
No risk of injury during troubleshooting
High residual gripping force of at least 80%
Use of smaller / lighter grippers possible
Constant gripping force over the whole stroke

## Slide 12: Pneumatic universal gripper PGL-plus-P certified safe gripping force maintenance
7. Pinion shaft
The one-piece pinion shaft connects the pinion with the mechanics of the safe gripping force maintenance.
8. Clamping element In the case of a pressure loss without a gripped workpiece, the clamping element prevents the pinion from rotating. This prevents potentially dangerous movement of the gripper fingers.
10. Spring-loaded pneumatic piston During normal operation of the gripper, the pneumatic piston is always supplied with compressed air. No separate air supply is required for this. In case of a failure, a pressure air loss, the piston is pushed back via the spring assembly and the clamping element blocks the pinion shaft, so that a movement of the gripper fingers is no longer possible.
9. Elastomer In the event of a pressure loss with a gripped workpiece, the gripping force stored in the elastomer (energy storage) grips the workpiece securely. The clamping element prevents the gripper fingers from opening.
11. Pressure compensation valve The pressure compensation valve allows the pressure, that has built up inside, to escape to the outside. At the same time, it prevents dirt or liquids from getting inside the gripper.
Position 1 – 6
identical to the basic gripper