## Slide 1: Flexible Universal Gripper EGU Flexible Small Part Gripper EGK
EGU/EGK vs. Zimmer GEH 6000 and 8000
&

## Slide 2: Competitive Environment
Competitive Environment EGU and EGK
Who are the competitors we are fighting with EGU and EGK?
GEH 6000
(-03 powerful vs. EGU) (-31 gentle vs. EGK)
GEH 8000
(vs. EGU 80)
Hand-E (vs. EGU 50)
2FG7 (vs. EGU 50)
RG2 & RG6 (vs. EGK)
LEHF (vs. EGK)
MPLM (vs. EGK)
MPLF (vs. EGU and EGK)
WPG (vs. EGK 50)
CRG Series (vs. EGK)
IEG & IEG-Plus Series (vs. EGK)
RCP6 (vs. EGK)
2F-85 & 2F-140 (vs. EGK)

## Slide 3: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
EGU & EGK vs. ZIMMER
GEH 6000 Series
EGU Series
GEH 8000
EGK Series
Type | Stroke/ jaw[mm] | Force [N] | Mass [kg] | Price
GEH6040IL-03-B | 40 | 100 - 1000 | 0,7 | 2.730 €
GEH6060IL-03-B | 60 | 100 - 1000 | 0,9 | 2.800 €
GEH6140IL-03-B | 40 | 150 - 1800 | 1,9 | 2.925 €
GEH6180IL-03-B | 80 | 150 – 1800 | 2,6 | 3.110 €
GEH6040IL-31-B | 40 | 10 - 180 | 0,7 | 2.995 €
GEH6060IL-31-B | 60 | 10 - 180 | 0,9 | 3.060 €
GEH 8860* | 60 | 200 – 3200 | 9,3 | 4.420 €
Type | Stroke/ jaw[mm] | Force [N] | Mass [kg] | Price
EGU 50 IL | 51 | 150 – 450 | 1,49 | 2550 €
EGU 60 IL | 60 | 325 – 975 | 2,90 | 2850 €
EGU 70 L | 70 | 650 – 1950 | 4,52 | 3150 €
EGU 80 IL | 80 | 1000 - 3000 | 7,72 | 3450 €
*price without external controller and cabeling
Type | Stroke/ jaw [mm] | Force [N] | Mass [kg] | Price
EGK 25 IL | 26.5 | 20 - 50 | 0.62 | 2300 €
EGK 40 IL | 41.5 | 55 - 150 | 1.02 | 2500 €
EGK 50 IL | 51.5 | 150 - 300 | 1.63 | 2800 €
Changes depending on the version:
Industrial Ethernet (PN/EI/EC) or Modbus RTU versions: +300 €
Version with dust-tight protection (only EGU): +250 €
Version without gripping force maintenance: -100 €
Note: Pricing is partly estimated on basis of exisiting prices for some versions. List prices in Germany. Including latest price increase with approx. 6%. Status from 13th of September 2022.

## Slide 4: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
Drive train EGU & EGK vs. ZIMMER
Kinetic Energy (Peak) determines the gripping force
  Self-locking
  Inherent gripping force maintenance
  Compact Design with low mass
  Low efficiency over finger length
  Gripping force depending on impact speed
  Starting distance necessary
Motor torque determines the gripping force
  Highest efficiency over finger length
  No starting distance
  Permanent gripping force
  No gripping force maintenance
  Larger installation space and higher mass
  Slightly higher costs
Helical gear unit
Worm gear

## Slide 5: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
Drive train EGU & EGK vs. ZIMMER
Scenario: Asychronous contact of the jaws to the workpiece
WP
Gripper
Worm gear
Helical gear unit
Note: Impact force of the worm gear is reduced due to earlier impact on one of the two jaws
WP
Gripper
Note: Impact force of the worm gear is reduced due to earlier impact on one of the two jaws
Scenario: Asychronous contact of the jaws to the workpiece or lifting a WP with one jaw.

## Slide 6: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
Drive train EGU & EGK vs. ZIMMER
Worm gear
Helical gear unit
Scenario: Gripping a part out of a clamping device
WP
Gripper
Note: Workpiece will be reoriented after the vise opened. Impact force is already gone. Regripping with worm gear is only party possible.
Vise
Vise unopened while gripping. Part will be released after the gripper has picked to workpiece
Gripper is not perfectly orientated

## Slide 7: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
Drive train EGU & EGK vs. ZIMMER
Worm gear
Helical gear unit
Scenario: Gripping a part out of a tray without having to much distance left for start up. Handling of a heavy workpiece with max. force.
WP
Gripper
Note: Worm gear needs a start up distance to generate the highest gripping forces. Helical gear unit can generate them without start up distance.
Tray

## Slide 8: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
Drive train EGU & EGK vs. ZIMMER
Worm gear
Helical gear unit
Scenario: Short fingers length, heavy part. Good orientation from gripper to part.
WP
Gripper
Note: Both types will perform great. Worm gear with a lower overall mass.
Scenario: High fingers length, heavy part. Good orientation from gripper to part.
WP
Gripper
Note: Helical gear unit will perform well with a constant force. Worm gear depending since a lot of kinetic energy will be reduced on impact by the long fingers as the fingers bend.

## Slide 9: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
Drive train example: ZIMMER GEH 6040 (-03 powerful) vs. EGU 50
EGU 50-PN-M-B
GEH6040IL-03-B
catalog values max. 1000 N
min. 100 N
catalog values
max. 450 N
min. 150 N

## Slide 10: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
Drive train example: ZIMMER GEH 6040 (-31 gentle) vs. EGK
EGK 40-PN-M-B
GEH6040IL-31-B
Catalog values max. 180 N
min. 10 N
Catalog values max. 150 N
min. 55 N

## Slide 11: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
EGU & EGK vs. ZIMMER
GEH 6000 Series
EGU Series
GEH 8000
EGK Series
Type | Stroke/ jaw[mm] | Force [N] | Mass [kg] | Price
GEH6040IL-03-B | 40 | 50 - 500 | 0,7 | 2.730 €
GEH6060IL-03-B | 60 | 50 - 500 | 0,9 | 2.800 €
GEH6140IL-03-B | 40 | 125 - 1150 | 1,9 | 2.925 €
GEH6180IL-03-B | 80 | 125 - 1150 | 2,6 | 3.110 €
GEH6040IL-31-B | 40 | 22 - 185 | 0,7 | 2.995 €
GEH6060IL-31-B | 60 | 22 – 185 | 0,9 | 3.060 €
GEH 8860* | 60 | 200 – 3000 | 9,3 | 4.420 €
Type | Stroke/ jaw[mm] | Force [N] | Mass [kg] | Price
EGU 50 IL | 51 | 150 - 440 | 1,49 | 2550 €
EGU 60 IL | 60 | 350 - 950 | 2,90 | 2850 €
EGU 70 L | 70 | 660 - 1850 | 4,52 | 3150 €
EGU 80 IL | 80 | 1100 - 2500 | 7,72 | 3450 €
*price without external controller and cabeling
Type | Stroke/ jaw [mm] | Force [N] | Mass [kg] | Price
EGK 25 IL | 26.5 | 20 – 50 | 0.62 | 2300 €
EGK 40 IL | 41.5 | 55 – 150 | 1.02 | 2500 €
EGK 50 IL | 51.5 | 150 - 300 | 1.63 | 2800 €
Changes depending on the version:
Industrial Ethernet (PN/EI/EC) or Modbus RTU versions: +300 €
Version with dust-tight protection (only EGU): +250 €
Version without gripping force maintenance: -100 €
Note: Pricing is partly estimated on basis of exisiting prices for some versions. Including latest price increase with approx. 6%. Status from 13.09.2022.
Comparison @ 50 mm finger length
Notes: Please note that Zimmer force is sinking with longer fingers

## Slide 12: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
EGU & EGK vs. ZIMMER
GEH 6000 Series
EGU Series
GEH 8000
EGK Series
Type | Stroke/ jaw[mm] | Force [N] | Mass [kg] | Price
GEH6040IL-03-B | 40 | 50 - 350 | 0,7 | 2.730 €
GEH6060IL-03-B | 60 | 50 - 350 | 0,9 | 2.800 €
GEH6140IL-03-B | 40 | 125 - 900 | 1,9 | 2.925 €
GEH6180IL-03-B | 80 | 125 – 1000 | 2,6 | 3.110 €
GEH6040IL-31-B | 40 | 17 - 170 | 0,7 | 2.995 €
GEH6060IL-31-B | 60 | 17 - 170 | 0,9 | 3.060 €
GEH 8860* | 60 | 200 – 2900 | 9,3 | 4.420 €
Type | Stroke/ jaw[mm] | Force [N] | Mass [kg] | Price
EGU 50 IL | 51 | 155 - 400 | 1,49 | 2550 €
EGU 60 IL | 60 | 325 - 875 | 2,90 | 2850 €
EGU 70 L | 70 | 650 - 1700 | 4,52 | 3150 €
EGU 80 IL | 80 | 1000 - 3000 | 7,72 | 3450 €
*price without external controller and cabeling
Type | Stroke/ jaw [mm] | Force [N] | Mass [kg] | Price
EGK 25 IL | 26.5 | 20 – 50 | 0.62 | 2300 €
EGK 40 IL | 41.5 | 55 – 150 | 1.02 | 2500 €
EGK 50 IL | 51.5 | 150 - 300 | 1.63 | 2800 €
Changes depending on the version:
Industrial Ethernet (PN/EI/EC) or Modbus RTU versions: +300 €
Version with dust-tight protection (only EGU): +250 €
Version without gripping force maintenance: -100 €
Note: Pricing is partly estimated on basis of exisiting prices for some versions. Including latest price increase with approx. 6%. Status from 13.09.2022.
Comparison @ 80 mm finger length
Notes: Please note that Zimmer force is sinking with longer fingers

## Slide 13: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
EGU & EGK vs. ZIMMER
GEH 6000 Series
EGU Series
GEH 8000
EGK Series
Connectivity
Embedded Systems
via MATCH or SCM external gateway
Digital I/O
BLDC Motor
Integrated Electronics
Incremental Encoder
Passive gripping force maintenance self-locking drive (only -03 powerful version)
IP54
STO function in a customer specific version
5 Mio. cycles warranty
BLDC Motor
External Electronics
Singleturn Absolut Encoder (Multiturn with battery)
Passive gripping force maintenance self-locking drive
IP 54
10 Mio. cycles warranty
BLDC Flat-Motor
Integrated Electronics
Incremental and Absolut Encoder
Active gripping force and position maintenance by electromagnetic brake
IP 67
STO function by external safety relay (preparation)
5 Mio. cycles warranty (StrongGrip only 3 Mio.)
(via external BOSCH controller) No further consideration of services Product can be controlled like a servodrive which offers a lot of possibilities with highest complexity

## Slide 14: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
EGU & EGK vs. ZIMMER
GEH 6000 Series
EGU Series
EGK Series
Services
Functions:
Grip Workpiece with different force profiles
Positioning
Gripping Force adjustment
Workpiece lost detection (depending on force profile)
SW-Services:
PLC Blocks for Beckhoff and Siemens
Robot integration with Plugins via MATCH and external gateway SCM (UR, TM, HANWHA, Mitsubishi, FANUC, Doosan, ABB, HORST, Yaskawa, Elite, KUKA)
ControlZ commissioning software (requires a SCM module)
Functions:
Grip Workpiece with different force profiles
Positioning
Gripping Force adjustment
Workpiece lost detection (active detection with active motor control, passive detection with activated gripping force maintenance)
SW-Services:
PLC Blocks for Beckhoff, Siemens and Allen Bradley
Robot integration without external gateways to FANUC, UR, ABB and Yaskawa (TM, Doosan and KUKA coming)
MTSN2 commissioning software (for industrial ethernet versions)
FGR finger designer

## Slide 15: EGU/EGK vs. ZIMMER GEH 6000 and 8000
Competitive Environment EGU and EGK
Summary EGU & EGK vs. ZIMMER
GEH 6000 Series
EGU Series
GEH 8000
EGK Series
No starting distance for workpiece gripping or dependence of the gripping force to speed
Always referenced due to absolut encoder
Permanent gripping force possible (not with StrongGrip)
“Real” gripping force maintenance
Attractive Pricing
Higher IP Rating
Ethernet Interfaces
Dust protected version (EGU only)
Lower installation space and lower mass (exception GEH 8000)
Higher gripping forces with very low finger length, depending on size and gripping situation
Partly lower gripping forces, depending on finger length and type

## Slide 17: Competitive Environment
Product Training EGU & EGK

## Slide 18: Availability
Product Training EGU & EGK

## Slide 19: EGU – Pricing vs. our competitors
ExpertGroup Mechatronics | 2022-07-06
Zimmer GEH6040
2.732€
2.550€
EGU50 with GKS
2.850€
EGU50 with GKS
3.640€
SCHUNK EGL 90
2.800€
EGK 40 with GKS
2.500€
EGK 40 with GKS
3.640€
SCHUNK EGI 80
Zimmer GEH6040 (sensitive)
2.925€
SMC LEHF 40-80
2.700€
Weiss CRG 200-085
3.738€
EGK
EGU

## Slide 20
EGU/EGK vs. Zimmer & Weiss Robotics
Confidential

## Slide 21: Inhaltsverzeichnis:
3. EGK:
Zimmer GEH6040IL-31-B
Zimmer GEH6060IL-31-B
Weiss CRG 30-050
Weiss CRG 200-085
Weiss IEG 55-020
Weiss IEG 76-030
4. Zusatz
Erklärung IP-Schutzklassen
1. Generell:
Informationen zu den Folien
Funktion und Integration EGU/EGK
Vergleich Antriebskonzepte
2. EGU:
Zimmer GEH6040IL-03-B
Zimmer GEH6060IL-03-B
Zimmer GEH6140IL-03-B
Zimmer GEH6180IL-03-B
Zimmer GEH8660-B
Confidential

## Slide 22: 1. Generell
Confidential

## Slide 23: Inhaltsverzeichnis:
3. EGK:
Zimmer GEH6040IL-31-B
Zimmer GEH6060IL-31-B
Weiss CRG 30-050
Weiss CRG 200-085
Weiss IEG 55-020
Weiss IEG 76-030
4. Zusatz
Erklärung IP-Schutzklassen
1. Generell:
Informationen zu den Folien
Funktion und Integration EGU/EGK
Vergleich Antriebskonzepte
2. EGU:
Zimmer GEH6040IL-03-B
Zimmer GEH6060IL-03-B
Zimmer GEH6140IL-03-B
Zimmer GEH6180IL-03-B
Zimmer GEH8660-B
Confidential

## Slide 24: Informationen
Diese Präsentation umfasst Folien, die nur zur internen Verwendung freigegeben sind
Schrift in dieser Farbe hebt die Eigenschaften der Konkurrenz hervor
Schrift in dieser Farbe hebt die Gemeinsamkeiten mit der Konkurrenz hervor
Stand der Präsentation 02.05.2022
Confidential

## Slide 25: Inhaltsverzeichnis:
3. EGK:
Zimmer GEH6040IL-31-B
Zimmer GEH6060IL-31-B
Weiss CRG 30-050
Weiss CRG 200-085
Weiss IEG 55-020
Weiss IEG 76-030
4. Zusatz
Erklärung IP-Schutzklassen
1. Generell:
Informationen zu den Folien
Funktion und Integration EGU/EGK
Vergleich Antriebskonzepte
2. EGU:
Zimmer GEH6040IL-03-B
Zimmer GEH6060IL-03-B
Zimmer GEH6140IL-03-B
Zimmer GEH6180IL-03-B
Zimmer GEH8660-B
Confidential

## Slide 26
SCHUNK
Greifer
SIEMENS
Steuerung/Peripherie
SITOP PSU 8600
24V Spannungsversorgung
SIMATIC
ET 200 eco PN IO-Link Master
IO-Link
PROFINet
PROFINet
Ansteuerung über IO-Link
Ansteuerung über industrielles Ethernet
Confidential

## Slide 27: Basis Funktionen
 | IO-Link EGU | IO-Link EGK | Industrielles Ethernet EGU | Industrielles Ethernet EGK
Greifen und öffnen zum Greifen und Halten von Werkstücken | ✔ | ✔ | ✔ | ✔
Greifkraft Anpassung Anpassung an empfindliche Werkstücke | ✔ | ✔ | ✔ | ✔
Positionierung zum vorpositionieren der Finger | ✔ | ✔ | ✔ | ✔
Feinanpassung der Bewegungsabläufe z.B. Geschwindigkeit, Motorstrom usw. | - | - | ✔ | ✔
Confidential

## Slide 28: Integrierte Sensoren und Diagnosefunktionen
 | IO-Link EGU | IO-Link EGK | Industrielles Ethernet EGU | Industrielles Ethernet EGK
Individuelle Positionen z.B. geöffnet, geschlossen, Werkstück gegriffen | ✔ | ✔ | ✔ | ✔
Positionen über den kompletten Hub zur Werkstückerkennung und Inspektion | ✔ | ✔ | ✔ | ✔
Wartungs- und Diagnosesignal z.B. Spannung, Temperatur, Zyklenzahl usw. | ✔ | ✔ | ✔ | ✔
Identifikationsdaten z.B. Materialnummer, Seriennummer, Softwareversion | ✔ | ✔ | ✔ | ✔
Zusätzliche Sensordaten z.B. Geschwindigkeit, Motorstrom usw. | - | - | ✔ | ✔
Confidential

## Slide 29: Integration und Konnektivität
 | IO-Link EGU | IO-Link EGK | Industrielles Ethernet EGU | Industrielles Ethernet EGK
SPS Verbindung ohne zusätzliche Module für leichte Integration in die Maschine | - | - | ✔ | ✔
Echtzeitfähig für zeitkritische Anwendungen | - | - | (✔) | (✔)
Webserver zur leichten Inbetriebnahme | - | - | ✔ | ✔
Übertragungsrate und Bandbreite für intelligente Produktionen und Cloud-Anwendungen | + | + | ++++ | ++++
Confidential

## Slide 30: Inhaltsverzeichnis:
3. EGK:
Zimmer GEH6040IL-31-B
Zimmer GEH6060IL-31-B
Weiss CRG 30-050
Weiss CRG 200-085
Weiss IEG 55-020
Weiss IEG 76-030
4. Zusatz
Erklärung IP-Schutzklassen
1. Generell:
Informationen zu den Folien
Funktion und Integration EGU/EGK
Vergleich Antriebskonzepte
2. EGU:
Zimmer GEH6040IL-03-B
Zimmer GEH6060IL-03-B
Zimmer GEH6140IL-03-B
Zimmer GEH6180IL-03-B
Zimmer GEH8660-B
Confidential

## Slide 31: Vor- und Nachteile
Antrieb Schnecke
Kinetische Energie (Impuls) bestimmt die Greifkraft
+ Selbsthemmung
+ Inhärente Greifkrafterhaltung
+ Kompakt
- Niedriger Wirkungsgrad
- Greifkraft geschwindigkeitsabhängig
- Anlaufweg
Antrieb Stirnrad
Motormoment bestimmt die Greifkraft
+ Hoher Wirkungsgrad
+ Geringer bzw. kein Anlaufweg
+ Greifkraft Anwendungsunabhängig
- Keine Greifkrafterhaltung (durch Kinematik)
- Großer Bauraum
- Höhere Kosten
Confidential

## Slide 32: The title of the presentation is also written here in two lines
Here can be the subline

## Slide 33: The title of the presentation is also written here in several lines
Here can be the subline

## Slide 34: The title of the presentation is also written here in several lines
Here can be the subline

## Slide 35: The title of the presentation is also written here in two lines
Here can be the subline

## Slide 36: The title of the presentation is also written here in several lines
Here can be the subline

## Slide 37: The title of the presentation is also written here in several lines
Here can be the subline

## Slide 38: The title of the presentation is also written here in two lines
Here can be the subline

## Slide 39: The title of the presentation is also written here in two lines
Here can be the subline

## Slide 40
Agenda item one
Agenda item two
Agenda item three

## Slide 41: Here is a quote / Recommendation / Result
Optional quoter

## Slide 42: Here the headline is also in several lines
Here is the chapter
Lorem ipsum dolor sit amet, consetetur sadipscing elitr, sed Highlight tempor invidunt ut labore et dolore magna aliquyam erat, sed diam voluptua. At vero eos et accusam et justo duo dolores et ea rebum.
An intermediate headline can look like this
Lorem ipsum dolor sit amet, consetetur sadipscing elitr, sed diam nonumy eirmod tempor invidunt ut labore et dolore magna aliquyam erat.
Enumeration with a highlight as an example
This is an important point in an enumeration
Another bullet point

## Slide 43: Here the headline is also in several lines
Here is the chapter
At vero eos et accusam et justo eos et accusam
Lorem ipsum dolor sit amet sto duo dolores
Stet clita kasd gubergren, no sea takimata ipsum dolor sit amet
Duis autem vel eum iriure dolor in hendrerit in vulputate velit esse molestie
Nam liber tempor cum soluta nobis eleifend option congue nihil

## Slide 44: Here the headline is also in several lines
Here is the chapter
At vero eos et accusam et justo eos et accusam
Lorem ipsum dolor sit amet sto duo dolores
Stet clita kasd gubergren, no sea takimata ipsum dolor sit amet
Duis autem vel eum iriure dolor in hendrerit in vulputate velit esse molestie
Nam liber tempor cum soluta nobis eleifend option congue nihil

## Slide 45: Here the headline is also in several lines
Here is the chapter
At vero eos et accusam et justo eos et accusam
Lorem ipsum dolor sit amet sto duo dolores
Stet clita kasd gubergren, no sea takimata ipsum dolor sit amet
Duis autem vel eum iriure dolor in hendrerit in vulputate velit esse molestie
Nam liber tempor cum soluta nobis eleifend option congue nihil

## Slide 46: Here the headline is also in several lines
Here is the chapter
Example table
Description | Table title | Table title | Table title | Table title | Table title | Table title | Table title
 | Unit | Unit | Unit | Unit | Unit | Unit | Unit
Content | Content | Content | Content | Content | Content | Content | Content
Highlighted line |  |  |  |  |  |  | 

## Slide 47: Here the headline is also in several lines
Here is the chapter
Example table
Description | Table title | Table title | Table title | Table title | Table title | Table title | Table title
 | Unit | Unit | Unit | Unit | Unit | Unit | Unit
Content | Content | Content | Content | Content | Content | Content | Content
Highlighted line |  |  |  |  |  |  | 

## Slide 48: The title of the presentation in several lines
Here is the product name

## Slide 49: Lorum Ipsum dore
Here is the product name
90 %

## Slide 50: Here the headline is also in several lines
Here is the chapter
At vero eos et accusam et
Lorem ipsum dolor sit
Stet clita kasd gubergren, no
Less Lorum Ipsum
30 %

## Slide 51: Template SCHUNK Colors
Primary Colors
Accent Color
0–61–106
0–158–224
188–207–0
0–61–106
0–158–224
188–207–0
216–186–34
0–61–106
0–158–224
188–207–0
227–227–227
Copy Text
Highlight Color in Tables
Representation Oil for Tool Holders
Color backgrounds from quiet to loud (e.g. for info boxes)

## Slide 52: Design elements
Example Plus Point

## Slide 53: Don’ts
Do not crop or obscure important image content in application images.
Only use images whose license you have.
The type plate logo must always be fully visible. Note the protective space around the logo.
Use the accent colour "Lemon" really only as an accent - not inflationary.
Do not overload the pages. Ensure clarity and comprehensibility of the content. → Brand value Clarity and quality
The “Next-Level-Element" must not be scaled or distorted unproportionally. The angle is always
27 degrees