## Slide 1: Hausen on AIR FUEL CELL
BDM E-MOBILITY
OEE
HAIRPIN-TECHNOLOGY
BATTERY PRODUCTION
ROTARY MODULES
LINEAR
MODULES
GRIPPING MODULES
CLAMPING
TECHNOLOGY
SOLUTIONS
ROBOT
ACCESSORIES
QUICK RESPONSE
PICK & PLACE UNITS
MATERIAL REMOVAL
FULL
SERVICE
E-MOBILITY
FUELL CELL PRODUCTION

## Slide 2
Introduction
Fuel cell system - Overview
Fuel cell stack
  Structure
  Function
  Components and production
Market players
Scenario - number of units
Excursus: Electrolyser

## Slide 3: NOSCO
Fuel cell stack – Components and production

## Slide 4: What is a fuel cell?
Introduction
"galvanic cell that converts the chemical reaction energy of a continuously supplied fuel and oxidant into electrical energy."
  chemical energy  electric energy
  Energy storage  Enery converter
PEMFC: Polymer-Exchange Membrane Fuel Cell
  Fuel: Hydrogen H2 | Oxidizer: Oxygen O2
  2H2 + O2  2H20
Notes: Ähnlich einer Batterie
- „Abfallprodukt“ Wasser

## Slide 5: Fuel cells and hydrogen - advantages
Introduction
Hydrogen is available in infinite quantities
Long ranges of 600 -800 km
Fast refuelling (3 – 5 minutes)
High gravimetric energy density
Notes: Ähnlich einer Batterie
- „Abfallprodukt“ Wasser

## Slide 6: Energy densities
Introduction
Quelle: https://upload.wikimedia.org/wikipedia/commons/c/c6/Energy_density.svg
Chart: Storage density of tank systems
| Kategorie 1
Otto | 32
FCEV | 8
BEV | 1
…but no direct comparison possible:
Battery = energy storage; H2 requires additional tank
Battery supplies power directly; with H2 this must still be generated by the fuel cell
Efficiency losses

## Slide 7: Efficiencies
Introduction
Quelle: https://www.e-mobilbw.de/service/datacenter
Chemical industry
Electrolyser
Hydrogen
Renewable Energies
Overall Efficiency

## Slide 8: Which type of drive for which vehicle?
Introduction
Small vehicles
Heavy-duty vehicles
Light commercial vehicles
Medium/large cars, fleets, taxis
Buses
Weight in tons
Average km per day/trip
BEV
FCEV
Renewable fuels

## Slide 9: Fuel Cell Electric Vehicle (FCEV)
Introduction
FOR SCHUNK
= No applications
= Applications in process
= Applications in Handling

## Slide 10: Supply Chain BEV
Introduction
Production of battery cells
Battery module
Battery pack
Production Drive / motor components
E-motor assembly
Machining & Assembly Engine
Chassis-Assembly
Subassemblies
Pressing
Car body
Paint shop
Docking
Final assembly
Final inspection
Production Drive / engine components
Chassis- assembly
Body shop
Docking / Wedding
Additional process for EV
Changed process for EC
Process wih little / no changes for EV
Elliminated process for EV
*Proton Exchange Membran
Herstellung MEA
Herstellung Bipolar platen

## Slide 11: Supply Chain FCEV
Introduction
Production of battery cells
Battery module
Battery pack
Production Drive / motor components
E-motor assembly
Chassis-Assembly
Subassemblies
Pressing
Car body
Paint shop
Docking
Final assembly
Final inspection
Production Drive / engine components
Chassis- assembly
Body shop
Docking / Wedding
Additional process for EV
Changed process for EC
Process wih little / no changes for EV
Elliminated process for EV
*Proton Exchange Membran
Herstellung MEA
Herstellung Bipolar platen
Fuel cell stack
Production bipolar plate
Machining & assembly drive
Production MEA

## Slide 12: Fuel cell systeme
Fuel cell system - Overview
Fuel cell stack
Venting
Hydrogen tank
Recirculation fan
H2
Filter
Humidifier
Compressor
Air
Air, water vapor
Cooling
Cooling
Pumpe
Coolant
Current management
Stack
Balance of Plant
Tank system
Notes: Evtl. Bild einer BPP einblenden  Drei Kanäle erklären.
Vier Subsysteme erklären
Balance of Plant Komponenten: Luftkompressor, Befeuchtung, Wasserstoffversorgung, Purgeventile, Wärmemanagement-Modul, Leistungselektronik

## Slide 13: Fuel cell systeme
Fuel cell stack – Components and production
Notes: Komponenten genauer erklären, bevor die Function kommt?

## Slide 14: Structure Fuel cell stack
Fuel cell stack – Components and production
Bipolar Plate (BPP)
Membrane-Electrode-Assembly (MEA)
Notes: Komponenten genauer erklären, bevor die Function kommt?

## Slide 15: Structure Fuel cell stack
Fuel cell stack – Components and production
Bipolar plate (BPP)
Gas-Diffusion-Layer (GDL)
Catalyst Coated Membrane (CCM)
Gas-Diffusion-Layer (GDL)
Bipolar plate (BPP)
Membrane-Electrode-Assembly (MEA)
Notes: Komponenten genauer erklären, bevor die Function kommt?
Hinzu kommen dann noch die Balance-of-Stack-Komponenten: Endplatten, Stromkollektoren, Verteilerplatte, Überwachungseinheit

## Slide 16: Function
Fuel cell stack – Components and production

## Slide 17: Function
Fuel cell stack – Components and production
H2 is distributed via the flowfield
GDL distributes H2 finely
Contact with the catalyst layer of the CCM
Hydrogen
Notes: Prinzip immer gleich:
2 Elektroden: Anode, Kathode
Dazwischen Membran mit Elektrolyt (elektrisch Leitfähigen Stoff)
  Bei PEM, Polymer mit Platin

## Slide 18: Function
Fuel cell stack – Components and production
Air is distributed over the flowfield
GDL distributes Air finely
Hydrogen
Oxygen

## Slide 19: Function
Fuel cell stack – Components and production
H2 oxidizes at the anode/ is catalytically split  2 protons  2 Electrons
Electrons are guided to the BPP via the conductive GDL (they cannot pass through the membrane)
Protons diffuse through the membrane towards the cathode
+
+
-
-
Oxygen
Hydrogen

## Slide 20: Function
Fuel cell stack – Components and production
If the cirvuit is closed, electrons can flow via an external load
Oxygen is redudced and reacts with protons and electrons to water 2H2 + O2  2H20
Water (reaction product) is removed via the cathode side of the BPP
Oxygen
Hydrogen

## Slide 21: Overview
Fuel cell stack – Components and production
Mixing
Coating
Decal
Testing & Confection
CCM production
Cutting Subgasket
Apply CCM
Laminating
Apply GDL
Testing & Confection
MEA production
Stacking
Pressing
Fixing
Leakage test
Conditioning
Stack production
Bipolar plate production
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Bipolar plate production
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Bipolar plate production
Notes: Primäre Kostentreiber: Herstellung der MEA und Bipolar platen
  CCM: rohmaterialkosten und der Verarbeitung zum Platinkatalysator
  GFL/BPP: große Aufwendungen, die aus einer technologisch unausgereiften, nicht hochratenfähigen Verfahrenstechnik begründet sind

## Slide 22: Bipolar plate production
Fuel cell stack – Components and production
Main function BPP:
Electrical connection of two galvanic cells
Gas distribution via Flow-Field
  Anode side (Hydrogen)
  Cathode side (Air)
Gas separation between neighboring cells
Seal to the outside
Cooling
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Cleaning
(Air) Oxygen
Coolant
Hydrogen
A:A (with bordering GDL)
Notes: Eine metallische BPP besteht aus zwei umgeformten Halbschalen, die durch Laser welding miteinander verbunden werden.

## Slide 23: Bipolar plate production
Fuel cell stack – Components and production
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Cleaning
Materials | Graphite | Metal
Advantages | Barely any corrosion  no coating necessary  High durability | Established manufacturing processes for forming and laser welding
 | Great freedom of design | Relatively productive, especially the forming
 |  | Efficient use of sealing material for beaded gaskets
Disadvantages | Very fragile | Metallic ions can dissolve and impair the functionality of the MEA
 | Resistance in material higher | Surface oxidation increases resistance  coating required
 | Comparatively high process times | Limitations in design due to limited degree of forming
Notes: Metallische BPP: Schaeffler, … Hersteller aufzählen?
Graphit, Vorteile in höchster Lebensdauer >40.000h
(beschichtetes) Metall, geringeres Gewicht, geringeres Volumen, bessere Kaltstartfähigkeit, Potenzial für geringere Fertigungskosten bei Serienproduktion
Grafit-Polymer-Compound,
Keramik

## Slide 24: Bipolar plate production - Forming
Fuel cell stack – Components and production
Forming the Flow-Field  Performance and efficiency
Optimum:
  Contact with the GDL as good as possible  flat land
  As much gas as possible should flow  wide channel  steep side angles; challenge for forming technology
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Cleaning
BPP
GDL
Land
Channel
Notes: Kontakt zur GDL: elektrische Leitung
Ideal: senkrecht, damit Verhältnis von Kontakt und Gasmenge maximal ist
Anforderung: hohe Genauigkeit, um Strömungsfeldkanäle qualitätsgerecht in die dünnen metallischen Folien einzubringen
Abweichung der Sollform, z.B. bei Kanalgeometrie hat einen negativen Einfluss auf den späteren Betrieb

## Slide 25: Bipolar plate production - Forming
Fuel cell stack – Components and production
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Cleaning
Progressive compound tool
  Material: steel (1.4301, 1.4404) or titanium
  Usual sheet thickness: 75 µm
- Tool contour - BPP - Active medium
Alternative: Hydroforming
Stamp
Die
Schuler, Andritz, Thyssenkrupp: Unrolling/Embossing
Notes: Folgeverbundwerkzeug: Werkzeugkosten hoch, Anzahl Werkzeugstufen: mehrere (Folgeverbundwerkzeug)
Sukzessive Materialbeanspruchung auch vorteile hinsichtlich der Erreichung höherer Umformgrade und besser ausgeformter Kanalstrukturen + direkt Schneiden mit demselben Werkzeug
Szenarien: 60 Hübe/min 60 BPP Halblatten pro Minute
Hydroforming: Werkzeugkosten gering (weniger Verschleiß und weniger Werkzeuge), 1 Werkzeug für verschiedene Materialstärken verwendbar
Vorteil: besserer Ausnutzuung des Umformvermögens des eingesetzten Werkstoffs; keine Reibung auf der Wasserseite: Eignung für vorbeschichtetes Material Im Vergleich aber geringe Produktionsrate, Ta
200 Mpa; Rückfederungseffekte werden minimiert -> qualitativ hochwertigere Platten entstehen
Walzen:
Eignet sich für eine signifikante Erhöhung der Ausbringungsmenge auf über 100 BPP-Halbplatten pro Minute
Schuler: Prägen und Beschneiden von Bipolar platenhälften aus Edelstahl; Knielhebelpressen bis 2.000 t Presskraft;
Vorfügen über Punktschweißprozess, so dass die Position beider Hälften zueinander fixiert ist,

## Slide 26: Bipolar plate production - Cleaning
Fuel cell stack – Components and production
Removal of processing media from pre-processes (Oils, greases, emulsions)
  Laser cleaning
  CO2 snow jets
  Hot steam cleaning
  Wet chemical cleaning (for oils and greases)
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Cleaning
Laserax: Laser Cleaning Fuel Cell Biplar Plates
CO2 snow jet cleaning

## Slide 27: Bipolar plate production - Laser welding
Fuel cell stack – Components and production
Connection of the BPP-half plates
Sealing the cooling channel
Reduce electrical resistance (Active Area Welding)
Requirements:
Extensive clamping technologies
High welding speeds
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Cleaning
Schuler, Andritz, Thyssenkrupp: Welding
Notes: Humping-Effekt: bei hohen Schweigeschwindigkeiten hebt sich das Schmelzbad und perlt; die Naht wird undicht
1 m/s, 1,2 m/s anvisiert
Andritz Soutec: Laserschweißanlagen, die mit mehrerer parallel arbeitenden Laserstrahlquellen die Bipolar platen verschweißen

## Slide 28: Bipolar plate production - Coating
Fuel cell stack – Components and production
Function:
Corrosion protection
Improvement of the electrical conductivity
Materials:
Gold
Carbon-based
Prozesse: PVD, CVD oder PECVD
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Cleaning
Schuler, Andritz, Thyssenkrupp: Coating
Notes: Korrosionsbeständig, elektrisch leitfähig
Freisetzen von Ionen aus metallischen BPP, die zu einer Vergiftung der Membran führen würden und eine Reduzierung der Brennstoffzellenleistung nach sich zieht, verhindert.

## Slide 29: Bipolar plate production - Coating
Fuel cell stack – Components and production
Function:
Corrosion protection
Improvement of the electrical conductivity
Materials:
Gold
Carbon-based
Alternative process: - Use of precoated coils Caution: Forming must not damage the coating!
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Cleaning
Cleaning
Coating
Inline QS
Slitten, Verpacken
Notes: Korrosionsbeständig, elektrisch leitfähig
Freisetzen von Ionen aus metallischen BPP, die zu einer Vergiftung der Membran führen würden und eine Reduzierung der Brennstoffzellenleistung nach sich zieht, verhindert.

## Slide 30: Bipolar plate production - Sealant application
Fuel cell stack – Components and production
Tasks of the seal:
Preventing internal/external leaks
Compensation of production tolerances
Connection component of MEA and BPP  Great influence to the lifetime
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Cleaning
Procedures:
Seal-on GDL
Screen printing
Injection molding
Dispensing
Schuler, Andritz, Thyssenkrupp: Apply Sealing
Notes: Verhindern von internen und externen Leckagen
Ausgleich von Toleranzen, die durch vorgelagerte Fertigungsprozesse der Komponenten entstehen,
Verbindende Komponente von MEA und BPP, großer Einfluss auf die Lebensdauer
Thyssenkrupp: Dichtung wird appliziert, getrocknet und optisch auf korrekte Qualität überprüft

## Slide 31: Bipolar plate production - Testing
Fuel cell stack – Components and production
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Cleaning
Schuler, Andritz, Thyssenkrupp: Leak Test

## Slide 32: Bipolar plate production - Example
Fuel cell stack – Components and production
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Cleaning
Schuler, Andritz, Thyssenkrupp
EKPO
Notes: Eine metallische BPP besteht aus zwei umgeformten Halbschalen, die durch Laser welding miteinander verbunden werden.

## Slide 33: Bipolar plate production - graphitic
Fuel cell stack – Components and production
Simplified process flow:
Tool drawing die for anode and cathode
Preform
  Graphite powder, epoxy, phenol resin, release agent
Press
  temperature (80 – 200 °C) + pressure (5 – 40 Mpa) + duration: 30 – 90s  Crosslinking of the plastic component
  Final curing in the oven
Gluing
  Adhesive must be electrically conductive
  Screen printing bonding
Preform
Gluing
Leakage test
Pressing / Sintering
Current paths
plastic
graphite

## Slide 34: Overview
Mixing
Coating
Decal
Testing & Confection
CCM production
Fuel cell stack – Components and production
Mixing
Coating
Decal
Testing & Confection
CCM production
Cutting Subgasket
Apply CCM
Laminating
Apply GDL
Testing & Confection
MEA production
Stacking
Pressing
Fixing
Leakage test
Conditioning
Stack production
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Bipolar plate production
Cutting Subgasket
Apply CCM
Laminating
Apply GDL
Testing & Confection
MEA production

## Slide 35: Overview – CCM | GDL | MEA
Mixing
Coating
Decal
Testing & Confection
CCM production
Fuel cell stack – Components and production
Cutting Subgasket
Apply CCM
Laminating
Apply GDL
Testing & Confection
MEA production
  Similar processes to the battery– very specific, no real applications for SCHUNK

## Slide 36: MEA production
Fuel cell stack – Components and production
Cutting Subgasket
Apply of the GDL
Testing and Confection
Insert CCM
  Structure:
  MEA can include various components, the name itself is not always chosen consistently
  MEA3 = CCM (Electrode, Membrane, Electrode)
  MEA5 = Subgasket, CCM, Subgasket
  MEA7 = GDL, Subgasket, CCM, Subgasket, GDL
Lamination

## Slide 37: CCM production
Fuel cell stack – Components and production
  CCM  Electrochemical core component of the PEM fuel cell
  Structure:
  Membrane with catalyst layer (graphite particles on which platinum particles are deposited)
Mixing
Decal
Testing und Confection
Coating the carrier film
Platinum
CCL = Cathode Catalyst Layer MEM = Membrane ACL = Anode Catalyst Layer

## Slide 38: CCM production
Fuel cell stack – Components and production
Mixing
Decal
Testing und Confection
Coating the carrier film
Catalyst powder
Platinum
Carbon-Particle
CCM is very sensitive to fluctuations in air humidity
      Humidity in production 50% at 23°C

## Slide 39: MEA production
Fuel cell stack – Components and production
Cutting Subgasket
Apply the GDL
Testing
Insert the CCM
Lamination
Fig. 1. The complete MEA production line of fuel cells based on R2R manufacturing system.
Fig. 3. A detailed flow diagram of MEA lamination process.
Fig. 2. Subgasket / Seal
Notes: OPTIMA

## Slide 40: MEA production
Fuel cell stack – Components and production
FTCT Energy Fully Automated MEA Producton Line
https://www.optima-packaging.com/en/fuel-cell
Cutting Subgasket
Apply the GDL
Testing
Insert the CCM
Lamination

## Slide 41: Overview
Fuel cell stack – Components and production
Mixing
Coating
Decal
Testing & Confection
CCM production
Cutting Subgasket
Apply CCM
Laminating
Apply GDL
Testing & Confection
MEA production
Stacking
Pressing
Fixing
Leakage test
Conditioning
Stack production
Bipolar plate production
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Bipolar plate production
Stacking
Pressing
Fixing
Leakage test
Conditioning
Stack production

## Slide 42: Stack production
Fuel cell stack – Components and production
Fuel cell stack:
Cell stack consisting of a large number of BPPs, MEAs and sealings + End plates and tensioning system
Number of layers (height of the stack) influences the performance
  Per cell around 0,6 - 0,7 V voltage
  usually 350 – 400 layers/stack
Stacking is often done directly on the end plates or so-called media modules
Stacken
Leakage test
Conditioning
Pressing
Fixing

## Slide 43: Stack production - Stacking
Fuel cell stack – Components and production
Requirements:
  Stacking-Speed: 0,5s
  Accurancy <0,1mm
Gripping:
  Vacuum gripper, Low-pressure surface gripper
  ADHESO  testing in progress
Manipulator:
  gantry systems / linear axes
  Scara robots
  Articulated robots
Stacken
Leakage test
Conditioning
Pressing
Fixing

## Slide 44: Stack production - Stacking
Fuel cell stack – Components and production
Challenges:
  Deposit accuracy
Stacken
Leakage test
Conditioning
Pressing
Fixing
Notes: Buckle in the plate

## Slide 45: Stack production - Stacking
Fuel cell stack – Components and production
Stacken
Leakage test
Conditioning
Pressing
Fixing
Pick & Place
Gantry system
Delta-Picker
Conveyer belt/ fall magazine
Almost web-shaped
ThyssenKrupp, EKPO
Hyundai
VAF
GROB

## Slide 46: Stack production - Pressing
Fuel cell stack – Components and production
Pressing…
  … to reache the needed contact pressure of the seals (up to 10 - 160 kN over a defined period)
  Contact resistance decreases (Attention: Transport losses of the media when pressing too hard)
Stacken
Leakage test
Conditioning
Pressing
Fixing
Weak compression
Strong compression
Ruhlamat fuel cell stack pressing machine

## Slide 47: Stack production - Fixing
Fuel cell stack – Components and production
End plates distribute contact pressure as evenly as possible
Fixing via…
  Tension straps (mechanically fixed or laser welded)
Stacken
Leakage test
Conditioning
Pressing
Fixing
Ballard
EKPO
  Threaded rods

## Slide 48: Stack production - Leakage test
Fuel cell stack – Components and production
Mandatory tests:
  Insulation check  Rule out short circuit
  Gas leak test  Exclude leak
      Differential pressure check
      Alternatively with helium (Localization possible via sniffer probe)
Stacken
Leakage test
Conditioning
Pressing
Fixing
Sequence of a leakage test

## Slide 49: Stack production - Conditioning
Fuel cell stack – Components and production
Serial connection of the cells  Single cells cannot be controlled directly
Stacken
Leakage test
Conditioning
Pressing
Fixing
Cell Voltage Monitoring System (CVM):
  Measuring the cell voltage of a single cell
   Consideration of failure cases
   Analyses
   Monitoring service life
   Prevention of damage to individual cells
Contacting the bipolar plates

## Slide 50: Stack production - Conditioning
Fuel cell stack – Components and production
Defined profiles are run through (different supply of the gases)
Fuel cell performance increases over time
Stacken
Leakage test
Conditioning
Pressing
Fixing
Conditioning (hours)
Voltage at same current
Break-in procedure is a company secret (mostly)
Process is time-consuming and uses larger quantites of hydrogen

## Slide 51: Overview
Fuel cell stack – Components and production
Mixing
Coating
Decal
Testing & Confection
CCM production
Cutting Subgasket
Apply CCM
Laminating
Apply GDL
Testing & Confection
MEA production
Stacking
Pressing
Fixing
Leakage test
Conditioning
Stack production
Forming
Laser welding
Coating
Sealant application
Testing & Confection
Bipolar plate production
Notes: Primäre Kostentreiber: Herstellung der MEA und Bipolar platen
  CCM: rohmaterialkosten und der Verarbeitung zum Platinkatalysator
  GFL/BPP: große Aufwendungen, die aus einer technologisch unausgereiften, nicht hochratenfähigen Verfahrenstechnik begründet sind

## Slide 52: Mobile fuel cells
Market players
User
Stack producer
Stacking machine producers
Notes: https://www.fuel-cell-cooperation.com/de/ (Zeltwanger, weil technology, von Ardenne)

## Slide 53: Scenario up to 2035
Scenario - number of units
414
Chart: Volume scenario by pwc
| 45658 | 47484 | 49310
North America | 0 | 29 | 84
Europe | 0 | 36 | 93
China | 0 | 93 | 237
2025 2035
Chart: Needed number of stacks
| 45658 | 47484 | 49310
North America | 0 | 58 | 168
Europe | 0 | 72 | 186
China | 0 | 186 | 474
2025 2035
828
Typical 400 twin stack design for trucks (image reference: Bosch)

## Slide 54: Szenario bis 2035
Scenario - number of units
828
2025 2035
Chart: Needed number of stacks
| 45658 | 47484 | 49310
North America | 0 | 58 | 168
Europe | 0 | 72 | 186
China | 0 | 186 | 474
Stacking machine 3 shifts, 7 h/day, 250 d/yr, utilization rate of 90%, stacksize 400
Chart: Output stacks / year with 1 machine
| 5 s | 1 s | 0,5 s | 0,1 s
Datenreihe 1 | 8.5 | 42.5 | 85 | 425
Fuel cells will only have a small market share within a region or company
i
Szenario: 0,1 s, (= 10Hz stacking) Global demand of stacking machines : 2.
i

## Slide 55: Fields of Application for hydrogen
Excursus: Electrolyser
Hydrogen
Short-term demand
Long-term demand
Refineries
Emission-free Heavy goods traffic and public transport
Emission-free Railway service
Steel production
Fuel cells cars
Renewable Aviation fuels
Renewable Marine fuels
Chemical industry
Heating sector
Notes: Wasserstoff ist das am häufigsten vorkommende chemische Element im Universum. Jedes Kilogramm H2 enthält etwa 2,4-mal so viel Energie wie Erdgas.
Vorteile sind längst erkannt:
Ölraffinerien, Herstellung von Ammoniak für Düngemittel, Produktion von Methanol und Stahl.
Speicherung von Erneuerbaren Energien.
Ersatz für fossile Brennstoffe in der Chemie- und Kraftstoffproduktion.
--- Wasserstoff ist ein sauberer, vielseitiger Brennstoff, der keine direkten Treibhausgasemissionen erzeugt. Zur Freisetzung der Energie wird lediglich Sauerstoff benötigt, und das einzige Nebenprodukt ist Wasser.
Leider gibt es keine reinen Wasserstoffvorkommen. Wasserstoff kommt in der Natur nur in gebundener Form vor.
https://www.ipa.fraunhofer.de/de/presse/presseinformationen/Electrolysere-sollen-massenware-werden.html
https://www.enbw.com/unternehmen/eco-journal/wasserstoff-farben.html
Türkiser Wasserstoff: Methanpyrolyse. Methan im Erdgas in Wasserstoff und Kohlenstoff gespalten. Kein CO2 in der Atmosphäre. Wenn Energie aus erneuerbaren Energien stammt ist die Erzeugung klimaneutral.
Grauer Wasserstoff: Dampfreformierung fossiler Brennstoffe wie Erdgas, Kohle oder Öl. Abfallprodukt CO2 – nicht Klimaneutral.
Blauer Wasserstoff: wie grauer, nur dass CO2 unterirdisch gelagert wird und nicht in die Atmosphäre gelangt.
Juni 2020 „natinale Wasserstoffstrategie“ – Bis 2023 Elektrolysekapazität von mind. 10 Gigwatt

## Slide 56: Hydrogen market development
Excursus: Electrolyser
Notes: Wasserstoff ist das am häufigsten vorkommende chemische Element im Universum. Jedes Kilogramm H2 enthält etwa 2,4-mal so viel Energie wie Erdgas.
Vorteile sind längst erkannt:
Ölraffinerien, Herstellung von Ammoniak für Düngemittel, Produktion von Methanol und Stahl.
Speicherung von Erneuerbaren Energien.
Ersatz für fossile Brennstoffe in der Chemie- und Kraftstoffproduktion.
--- Wasserstoff ist ein sauberer, vielseitiger Brennstoff, der keine direkten Treibhausgasemissionen erzeugt. Zur Freisetzung der Energie wird lediglich Sauerstoff benötigt, und das einzige Nebenprodukt ist Wasser.
Leider gibt es keine reinen Wasserstoffvorkommen. Wasserstoff kommt in der Natur nur in gebundener Form vor.
https://www.ipa.fraunhofer.de/de/presse/presseinformationen/elektrolyseure-sollen-massenware-werden.html
https://www.enbw.com/unternehmen/eco-journal/wasserstoff-farben.html
Türkiser Wasserstoff: Methanpyrolyse. Methan im Erdgas in Wasserstoff und Kohlenstoff gespalten. Kein CO2 in der Atmosphäre. Wenn Energie aus erneuerbaren Energien stammt ist die Erzeugung klimaneutral.
Grauer Wasserstoff: Dampfreformierung fossiler Brennstoffe wie Erdgas, Kohle oder Öl. Abfallprodukt CO2 – nicht Klimaneutral.
Blauer Wasserstoff: wie grauer, nur dass CO2 unterirdisch gelagert wird und nicht in die Atmosphäre gelangt.
Juni 2020 „natinale Wasserstoffstrategie“ – Bis 2023 Elektrolysekapazität von mind. 10 Gigwatt

## Slide 57: Hydrogen market development
Excursus: Electrolyser
Notes: Wasserstoff ist das am häufigsten vorkommende chemische Element im Universum. Jedes Kilogramm H2 enthält etwa 2,4-mal so viel Energie wie Erdgas.
Vorteile sind längst erkannt:
Ölraffinerien, Herstellung von Ammoniak für Düngemittel, Produktion von Methanol und Stahl.
Speicherung von Erneuerbaren Energien.
Ersatz für fossile Brennstoffe in der Chemie- und Kraftstoffproduktion.
--- Wasserstoff ist ein sauberer, vielseitiger Brennstoff, der keine direkten Treibhausgasemissionen erzeugt. Zur Freisetzung der Energie wird lediglich Sauerstoff benötigt, und das einzige Nebenprodukt ist Wasser.
Leider gibt es keine reinen Wasserstoffvorkommen. Wasserstoff kommt in der Natur nur in gebundener Form vor.
https://www.ipa.fraunhofer.de/de/presse/presseinformationen/elektrolyseure-sollen-massenware-werden.html
https://www.enbw.com/unternehmen/eco-journal/wasserstoff-farben.html
Türkiser Wasserstoff: Methanpyrolyse. Methan im Erdgas in Wasserstoff und Kohlenstoff gespalten. Kein CO2 in der Atmosphäre. Wenn Energie aus erneuerbaren Energien stammt ist die Erzeugung klimaneutral.
Grauer Wasserstoff: Dampfreformierung fossiler Brennstoffe wie Erdgas, Kohle oder Öl. Abfallprodukt CO2 – nicht Klimaneutral.
Blauer Wasserstoff: wie grauer, nur dass CO2 unterirdisch gelagert wird und nicht in die Atmosphäre gelangt.
Juni 2020 „natinale Wasserstoffstrategie“ – Bis 2023 Elektrolysekapazität von mind. 10 Gigwatt
https://www.presseportal.de/pm/122303/4914663

## Slide 58: Production of hydrogen
Excursus: Electrolyser
Natural gas
Coal
Oil
Hydrocarbons
Steam reforming
Steam reforming
Natural gas
Oil
Coal
Natural gas
Carbon (C)
Methane pyrolysis
Current
Electrolysis
Notes: https://www.ipa.fraunhofer.de/de/presse/presseinformationen/Electrolysere-sollen-massenware-werden.html
https://www.enbw.com/unternehmen/eco-journal/wasserstoff-farben.html
Türkiser Wasserstoff: Methanpyrolyse. Methan im Erdgas in Wasserstoff und Kohlenstoff gespalten. Kein CO2 in der Atmosphäre. Wenn Energie aus erneuerbaren Energien stammt ist die Erzeugung klimaneutral.
Grauer Wasserstoff: Dampfreformierung fossiler Brennstoffe wie Erdgas, Kohle oder Öl. Abfallprodukt CO2 – nicht Klimaneutral.
Blauer Wasserstoff: wie grauer, nur dass CO2 unterirdisch gelagert wird und nicht in die Atmosphäre gelangt.
Juni 2020 „natinale Wasserstoffstrategie“ – Bis 2023 Elektrolysekapazität von mind. 10 Gigwatt

## Slide 59: Production of green hydrogen
Excursus: Electrolyser
Structure of electrolyser similar to fuel cells, chemical reaction is reversed: H2O  Spaltung  Sauerstoff O2 + Wasserstoff H2
Elektrolyse-Stack:
  100-200 Zellen
  Kernkomponente: Kunststoffmembran mit Katalysatorschicht
Notes: 800x750x10
5er-Zellstapel: 100 Kg  bis 4 Tonnen.
100-200 Zellen
Kunststoffmembran mit Katalysatorschicht, an der der Wasser in Wasserstoff und Sauerstoff gespalten wird.

## Slide 60: BD E-Mobility
contacts
Patrick Engelhardt patrick.engelhardt@de.schunk.com
+49-7133-103-2959
+49-151-52738990
Simon Heinrich simon.heinrich@de.schunk.com
+49-7133-103-2038 +49-151-12001492
Marcel Conz marcel.conz@de.schunk.com
+49-7133-103-2948 +49-160-91932764
Andreas Brahner andreas.brahner@de.schunk.com
+49-7133-103-2641
Christian Göhler christian.goehler@de.schunk.com
+49-7133-103-3546 +49-151-12921421
e-mobility@de.schunk.com
Hotline: -3014

## Slide 62: Bildquellen
https://www.electrive.net/wp-content/uploads/2019/09/flixbus-freudenberg-sealing-technologies-Fuel cell system-fuel-cell-system-brennstoffzellen-bus-fuel-cell-bus-concept-2019-01-min.png
https://www.springerprofessional.de/en/automobil---motoren/brennstoffzelle/leichte-beschichtete-Bipolar platen-fuer-brennstoffzellen/6587154
https://www.schaeffler.com/remotemedien/media/_shared_media_rwd/06_press/press_kits_events/kolloquium_2022/digital_conference_book/commercial_vehicles/16_9-schaeffler-kolloquium-2022-commercial-vehicles_11_rwd_1200.jpg
https://link.springer.com/content/pdf/10.1007/s35144-021-1304-5.pdf
https://www.fuelcellstore.com/image/data/Products/MEA/3,5,7-layer-meas.jpg
https://www.sciencedirect.com/science/article/pii/S1526612516300792#sec0010