## Slide 1: PPD Pneumatic Positioning Device
Positioning device for flexible control of pneumatic grippers

## Slide 2: Positioning device for flexible control of pneumatic grippers
PPD: Pneumatic Positioning Device
enables cycle time optimization or collision avoidance by pre-positioning the gripper fingers
Gripping force adjustability by adjusting the outlet pressure
Adjustability of the gripper jaw speed
Free positioning of a pneumatic gripper
for gripping workpieces of varying sensitivity
for workpiece-friendly gripping due to the reduction of the gripping impulse

## Slide 3: Functional description
PPD: Pneumatic Positioning Device
The pneumatic positioning device is an accessory for pneumatic grippers. Together with a position sensor, any positions of the gripper fingers can be approached in addition to the end positions (gripper open and gripper closed).
Four integrated high-speed 2/2 valves together with the integrated electronics ensure a closed control loop.
Pneumatic Positioning Device PPD
Pneumatic Standard Gripper
Position sensor

## Slide 4: Example video
PPD: Pneumatic Positioning Device
PGN-plus-P 200-1-AS
mit MMS 22-IOL
PHL 32-080
with BALLUFF BIP

## Slide 5: Field of application
The PPD enables flexibility in all applications with pneumatic grippers through free positioning, gripping force and speed adjustment.
The sealed design makes the PPD ideally suited for use in industrial environments.
PPD: Pneumatic Positioning Device

## Slide 6: Required components
Pneumatic gripper
Position sensor
PPD
It takes 3 things to make a pneumatic gripper positionable:
PPD: Pneumatic Positioning Device

## Slide 7: 1 size - 3 variants
Name | PPD 10-IOL | PPD 20-IOL | PPD 40-IOL
Valve nominal size | Ø 1,0 | Ø 2,0 | Ø 4,0
Flow rate at 6 bar | 63 l/min | 266 l/min | 868 l/min
Weight | 1,8 kg | 1,8 kg | 1,8 kg
Dimensions | 146x84x66 | 146x84x66 | 146x84x66
Depending on the gripper, the appropriate PPD variant is selected
One PPD controls one gripper
The 3 variants differ in the internally installed valves:
PPD: Pneumatic Positioning Device

## Slide 8: Pneumatic gripper
Standard gripper, no modification or special variant required
Piston surface A (gripper opening) and piston surface B (gripper closing) must be known  Table in software handbook
Other grippers are also possible in principle, but the piston areas must be known.
PPD: Pneumatic Positioning Device

## Slide 9: Position sensor
Requirements for the sensor
Position signal required over the entire gripper stroke
Plug M8, 4-pin connector directly into PPD (Pos)
Sensors
SCHUNK IO-Link Sensor
  Integrated IO-Link Sensor
  MMS-22-IOL
Analog Sensor (4-20mA)
  Externally mounted sensor (mounting kit!)
  BALLUFF BIP
PGL-plus-P…-IOL
MMS-22-IOL
BIP position sensor
PPD: Pneumatic Positioning Device

## Slide 10: Matching PPD/gripper/sensor
Gripper/Size | PPD 10-IOL | PPD 20-IOL | PPD 40-IOL
PGL-plus-P | 10, 13, 16 | 20, 25 | -
PGN-plus-P | 50, 64, 80 | 100, 125, 160 | 200
JGP-P | 50, 64, 80 | 100, 125, 160 | 200
DPG-plus | 64, 80 | 100-160 | 
PZN-plus |  | 64, 80, 100, 125 | 160
JGZ |  | 64, 80, 100, 125 | 160
DPZ-plus |  | 64, 80, 100, 125 | 160
PZH-plus | 20* | 30, 50, 75* | -
PHL | 25* | 32, 40, 50, 63* | -
PLG | - | 20, 30** | 50, 75, 120**
* = external position sensor required, standard mounting kits for BALLUFF BIP in preparation
** = external position sensor required, in preparation
PPD: Pneumatic Positioning Device

## Slide 11: Application examples
PPD: Pneumatic Positioning Device
Handling of bars/tubes
Gripper fingers must be pre-positioned to be able to remove the parts from the deposit station without causing a collision