## Slide 1: SCHUNK Engineering
Solution Book - Metal Processing
Note:
This presentation contains confidential information and is only released for non-public use by customers and suppliers.
Consultation with specialist department may be necessary.
- Remove this note before use -

## Slide 2: Gripping unit Handling of cylinder liners for marine engines
Metal Processing
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
Function Loading and unloading a lathe with very heavy cylinder liners (350 kg)
Customer benefit
  High flexibility with a wide range of components
  High scalability
  Handling of heavy components >350 kg
  Easy and quick replacement of wear parts
Customized attachment jaws with interchangeable clamping inserts
Expert project planning team Sizing, design and assembly by SCHUNK
RELIABILITY
STRONG
ACCURACY
second page available
Notes: SCHUNK ID: 1579207

## Slide 3: Gripping unit Handling of cylinder liners for marine engines
Metal Processing
1 x heavy duty tool changing system SWS-L-510
Adapter plate
distributor
valves
Customized attachment jaws with interchangeable clamping inserts
2 x parallel gripper SPG 100-SDV-P with pressure maintenance valve
Notes: SCHUNK ID: 1579207

## Slide 4: 6-fold gripping swivel unit Gripping of small items / bulk material
Metal Processing
Function Loading, unloading, and crimping process for small parts. The customer-side counterpart for centering is changed using a quick-change system.
Customer benefit
  Quick changeover
  Maximum parallelization
  Integrated media feed-through
  High scalability
Expert project planning team Sizing, design and assembly by SCHUNK
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
HIGHSPEED
RELIABILITY
ACCURACY
second page available
Notes: SCHUNK ID: 1502263

## Slide 5: 6-fold gripping swivel unit Gripping of small items / bulk material
Metal Processing
1 x swivel unit SRU-plus 50
6 x 2-finger parallel gripper KGG 60-40
Adapter plates, sensor distributor, valves, magnetic switch, energy chain
6 x jaw quick-change system BSWS - customer-side counterpart for centering not shown
Notes: SCHUNK ID: 1502263

## Slide 6: Double-Gripper unit Gripping of small items / bulk material
Function Crimping of gripped parts with counterpart via pressing device
Customer benefit
  Compact design
  handling of high variety of parts variants
  Short setup times
  Short cycle times
Attachment to robot flange via adapter plate
Expert project planning team Sizing, design and assembly by SCHUNK
Metal Processing
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
HIGHSPEED
RELIABILITY
ACCURACY
second page available
Notes: SCHUNK ID: 1502264

## Slide 7: Double-Gripper unit Gripping of small items / bulk material
Metal Processing
1 x 3-finger centric gripper PZB-plus 100
5 x jaw quick-change system BSWS-BM 80
pressing device
Adapter, magnetic switch, valve, distributor
1 x parallel gripper PGN-plus-P 80
Attachment to robot flange via adapter plate
Notes: SCHUNK ID: 1502264

## Slide 8: 3-fold gripper unit Gripping of small items / bulk material
Metal Processing
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
Function Gripping three different small metal parts as bulk goods via customer camera system.
Customer benefit
  Compact multiple gripper solution
  Handling of high variety of parts variants
  Short setup times
  Short cycle times
Attachment to robot flange via adapter plate
Expert project planning team Sizing, design and assembly by SCHUNK
HIGHSPEED
RELIABILITY
ACCURACY
second page available
Notes: SCHUNK ID: 1502261

## Slide 9: 3-fold gripper unit Gripping of small items / bulk material
Metal Processing
Exemplary representation of one gripper:
third gripper
second gripper
2-finger parallel gripper PGL-plus-P 10-AS
jaw quick-change system BSWS-BM 64
various attachment jaws
magnetic switch
valves
distributor
Notes: SCHUNK ID: 1502261

## Slide 10: Gripper assemblies along a truss Handling of 4-meter steel beams weighing up to 500 kg
Metal Processing
Function Handling of very long and heavy components: gripper assemblies along a truss to reduce weight
Scope
  Crossbeam construction with flange connection for robots
  3x reinforced special grippers for workpiece weights up to 500 kg
  3x angular gears for customer-specific attachment of a servo motor
  3x fixed and movable attachment jaws each
Expert project planning team Sizing, design and assembly by SCHUNK
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
ACCURACY
second page available
Notes: SCHUNK ID: 1472620 (l) /1511530 (r)

## Slide 11: Gripper assemblies along a truss Handling of 4-meter steel beams weighing up to 500 kg
Metal Processing

## Slide 12: Electric 3-finger centric gripper with large stroke Handling of large rotationally symmetrical components
Metal Processing - Machine tool
Scope
  Sheet metal housing
  Wiper
  Accessible lubrication adapter
  Passive pressure unit
  Angular gearbox
Servo-electric drive Servomotor adaptable by the customer
Robust guidance Recirculating ball bearing
Large stroke / high gripping force
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
STRONG
Notes: SCHUNK ID: 1562643 / ausschließlich ENTWURF-Status

## Slide 13: 2-finger gripper swivel modules Handling of rotor shafts and drive shafts
Metal Processing
Function and benefits Machine tending of a turning machine: handling of rotor and drive shafts OP1 + OP2
Scope - each module consisting of:
  1x rotary module SRU-plus 50
  1x rotary module SRH-plus-D 40
  2 x sealed 2-finger parallel gripper DPG-plus 100 (IP67)
  adapter plates with internal air feed-through for space saving design
  8 x magnetic sensors
Customized top jaws gas nitrocarburized & oxidized steel inserts
Expert project planning teams Sizing, design and assembly by SCHUNK
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
WET
second page available
Notes: SCHUNK ID: 1571789 / 1571786

## Slide 14: 2-finger gripper swivel modules Handling of rotor shafts and drive shafts
Metal Processing
The gripper swivel modules are operated on a gantry system between central storage and turning machine  gantry systems also scope of SCHUNK Engineering
1x rotary module SRU-plus 50
adapter plates with internal air feed-through for space saving design
2 x sealed 2-finger parallel gripper DPG-plus 100 (IP67) with customized to jaws
1x rotary module SRH-plus-D 40
Notes: SCHUNK ID: 1571789 / 1571786

## Slide 15: 3-finger double gripper + quick-change system Light-weight design with maximum gripping force
Metal Processing
Function and benefits 3-finger double gripper with manual quick-change system as end-of-arm on a robot. Reduction of gripper weight to allow heaver workpiece but carry over the existing robot.
Scope
  2x 3-finger centric gripper PZN-plus 125-2
  quick change system SHS-125
  light-weight adapter plate
  Pressure maintenance valve SDV-P
Customized top jaws with peaky inserts for higher friction
Expert project planning teams Sizing, design and assembly by SCHUNK
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
ACCURACY
second page available
Notes: SCHUNK ID: 1566116

## Slide 16: 3-finger double gripper + quick-change system Light-weight design with maximum gripping force
Metal Processing
2x 3-finger centric gripper PZN-plus 125-2
with customized top jaws: peaky inserts for higher friction
manual quick change system SHS-125
light-weight adapter plate
Pressure maintenance valve SDV-P
Notes: SCHUNK ID: 1566116

## Slide 17: Heavy-duty handling Handling an engine block weighing approx. 350 kg for trucks
Metal Processing - Machine tool
Function and customer benefits Transferring the unmachined casting part to the machine tool. Multiple tolerance compensation enables clamping on raw clamping contours with component tolerances of several millimeters.
Scope
  C-axis
  x-y-z compensation unit
  2-finger parallel gripper
  Swivel finger with tolerance compensation
  Adapter plates and other accessories
Expert project planning team Sizing, design and assembly by SCHUNK
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
ACCURACY
second page available
Notes: SCHUNK ID: 1535228

## Slide 18: Heavy-duty handling Handling an engine block weighing approx. 350 kg for trucks
Metal Processing - Machine tool
C-axis
x-y-z compensation unit
2-finger parallel gripper
Swivel finger with tolerance compensation
Others:
Adapter plates
Sensors, Gear unit
Blow nozzles for cleaning the gripper pins incl. tubing
Notes: SCHUNK ID: 1535228

## Slide 19: Rotary feed-through DDF-060 Loading and unloading sheet metal processing machines
Metal Processing - Sheet metal processing
DDF-060 Rotary feed-through
Pneumatic feed-trough
  1 x pneumatic G1/4 inch 4-10 bar
  1 x pneumatic G1/8 inch 4-10 bar
  1 x Vacuum G1/4 inch
Electrical feed-through 4 x ASI+/-, AUX+/-, connector M12 4-pin
Mounting hole pattern possible according to customer specifications
Short project lead time Sizing, design and assembly by SCHUNK
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
ACCURACY
Notes: SCHUNK ID: 1401942

## Slide 20: Quick-change system Loading and unloading sheet metal processing machines
Metal Processing - Sheet metal processing
SWS-060-T Quick-change system,
Payload up to 75 kg, Mxy up to 197 Nm
Feed-through of of pneumatic / vacuum and electrics 2 x G18“ pneumatic / vacuum
4 pins für ASi-bus
Mounting hole pattern possible according to customer specifications
Short project lead time Sizing, design and assembly by SCHUNK
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
ACCURACY
Notes: SCHUNK ID: 30021712/30021713

## Slide 21: 3-finger centric gripper Handling of parts within the cleaning machine
Metal Processing - Cleaning
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
ACCURACY
Tight 3-finger centric gripper Material: stainless steel and seawater-resistant aluminum
Chemically and thermally resistant double seal with robust scraper
Screw-on pattern top jaws corresponding DPZ-plus 80
One contact person for the entire system including construction and assembly
Notes: SCHUNK ID: 1336370

## Slide 22: 2-axes Linear Unit Transferring electronic housings in progressive tools
Metal Processing - Sheet metal processing
Application Handling for a progressive die. Housings for car radios are manufactured. Three parts have to be gripped at the same time in the press cycle and transported to the next tool stage.
Axes X-axis: LDF-UF-1000-1050-1460 Z-axis: LDT-EL-0600-0100-0460
Scope of delivery Power and encoder cable, compact ejector with vacuum gripper, mounting bracket for Z-axis, 3x pneumatic Z-axes and energy chain
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
HIGHSPEED
RELIABILITY
ACCURACY
Notes: SCHUNK ID: 394057 (SES)

## Slide 23: Gripping unit PGN-plus, EGM Separation and loading and unloading of B-pillars
Metal Processing - Sheet metal processing
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
ACCURACY
Expert project planning team Sizing, design and assembly by SCHUNK
Parallel gripper PGN-plus Customized gripper fingers with integrated spreading function
Magnetic gripper EGM Floating bearing for flexible workpiece mounting
Compensation unit AGE-U Compensation direction X, Y, Z, angle
Notes: SCHUNK ID: 1347859

## Slide 24: Tight 2-finger parallel gripper Handling of parts within the cleaning machine
Metal Processing - Cleaning
Tight 2-finger parallel gripper Material: stainless steel and seawater-resistant aluminum
Chemically and thermally resistant double seal with robust scraper
Monitoring with pressure switch through mechanically actuated valves
One contact person for the entire system including construction and assembly
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
ACCURACY
Notes: SCHUNK ID: 1376342

## Slide 25: Gripping unit DPG-plus Use in high-pressure water jet cleaning system
Metal Processing - Cleaning machines
Tight gripper DPG-plus HD with Viton sealings and integrated sensors
Special gripper fingers and cover made of stainless steel with pressure mechanism in the gripper finger
Use in high-pressure cleaning system Water jet pressure 750 bar
Expert project planning teams Sizing, design and assembly by SCHUNK
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
WET
Notes: SCHUNK ID: 1490313

## Slide 26: Long-stroke Gripper MGHG heat-protected Loading/unloading of hot gears
Metal Processing – Hardening - High temperature
Handling hot workpieces Workpiece temperature >1000° C
Different workpiece diameters Gripping diameter 200-600 mm
High gripping force / heavy workpieces Workpiece weight 70 kg, positive gripping
Dynamics Integrated position measuring system also for servopneumatics
Expert project planning teams Sizing, design and assembly by SCHUNK
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
STRONG
HOT
RELIABILITY
Notes: SCHUNK ID: 1386683

## Slide 27: Double gripper unit for sand cores Unloading a sand core shooter
Metal Processing - Sand core production - High temperature
2-fold gripping unit as a complete solution with standard gripper PGN-plus 50-1
Dust-protected gripper Dust protection version SD
Gentle gripping with with rubber clamping inserts and pressure regulator
Integrated blow-out function to clean the tool
Plug and Play with valve technology and electrical distributor, completely wired and hosed
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
Notes: SCHUNK ID: 1416753

## Slide 28: Gripping unit SPG 100 & heat protection Removal of red-hot saw cuttings from the oven
Metal Processing - High temperature
Gripping unit SPG 100 Workpiece weight 50 kg, Workpiece temperature >1000° C
Heat protection with sheet metal housing, heat shield, ceramic insulation, high-temperature grease, high-temperature seals
Optimized opening/closing times with quick venting valves, special damping elements
Customized top jaws Form-fit prismatic with insulation
Short project lead time Sizing, design and assembly by SCHUNK
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
STRONG
HOT
RELIABILITY
Notes: SCHUNK ID: 30087158

## Slide 29: Servo-electric 3-finger centric gripper with compensation unit Loading/unloading of ring gears from a hardening press
Metal Processing - Hardening - High temperature
Servo-electric 3-finger centric gripper with gearbox, bevel gears, spindle
Heat protection with radiant heat plate, thermal insulation
Customized top jaws with ceramic coating
X-/compensation unit as tolerance compensation during loading
Pressure unit with “workpiece present” monitoring
Customized interface for mounting on robots
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
ACCURACY
Notes: SCHUNK ID: 30082733

## Slide 30: Linear gripper unit Unloading housings from a die casting machine
Metal Processing - Die casting machines - High temperature
Complete functional module through combination of standard components
Traversing axis Pneumatic with clamping
Standard 3-finger centric gripper PZ-plus with dust cover, high temperature sealings, high temperature grease
Customized interface for attachment to your robot incl. attachment option for energy hose
Customized top jaws with claw clamping inserts for gripping the sprue
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
ACCURACY
Notes: SCHUNK ID: 30049061

## Slide 31: Swivel-Gripper Unit Turning gears during the hardening process
Metal Processing - Hardening - High temperature
Complete functional module through combination of standard components
Pneumatic swivel unit SRM with air feed-through, proximity switch
2-finger Parallel gripper PHL with proximity switch
Customized top jaws interchangeable QUENTES clamping inserts
Gripping force maintenance pressure maintenance valve
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
ACCURACY
Notes: SCHUNK ID: 1474362

## Slide 32: Double gripping unit Loading/unloading valves into/from a welding machine
Metal Processing - Welding - High temperature
Double gripping unit 2x PGN-plus 100 with proximity switch
Heat protection version High-temperature sealings, high-temperature grease, heat radiation plates, shielded sensors
Heat-resistant top jaws Material: Stainless steel
Electrical distributor Complete electrical installation with electrical diagram
Customized interface for robot mounting
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
STRONG
HOT
RELIABILITY
Notes: SCHUNK ID: 1400648

## Slide 33: Gripping unit PGN-plus-P with heat protection - Handling of test specimens
Metal Processing - Forming technology - High temperature
Including change system SWA-110-R19VL-PG3 and storage module
Gripper PGN-plus-P 240-2-AS-SD Fixed jaw due to connection to a base jaw, housing moves
Heat protection Radiant heat plates, Viton sealings
Top jaw with one-sided pendulum, toothed carbide clamping inserts
Expert project planning teams Sizing, design and assembly by SCHUNK
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
STRONG
HOT
RELIABILITY
Notes: SCHUNK ID: 1423242, 1423244

## Slide 34: Gripping unit for pipes A-pillar Loading/unloading of hydroforming presses
Metal Processing - Forming technology - High temperature
Complete assembly with pneumatic 2-finger parallel grippers
Heat protection with radiant heat panel, thermal insulation
Customized top jaws with ceramic clamping inserts
Quick-change system with media feed-through
Complete with installation Hoses and cables covered with fire protection
Customized interface for mounting on robots
TYPICAL PRODUCTS
TYPICAL PROCESS
REQUIREMENTS
RELIABILITY
STRONG
ACCURACY
Notes: SCHUNK ID: 30086493